## Slide 1: 2018 Integrated Resource Plan Presentation to WUTC Commissioners and Stakeholders
Monday March 11th, 2019
WUTC Offices
Olympia, WA
Cascade Natural Gas Corporation

## Slide 2: Agenda
  IRP Objectives
  Stakeholder Engagement Process
  Demand Forecast
  Gas Supply Overview
  Environmental Considerations
  Avoided Cost
  Demand Side Management
  Distribution System Planning
  Supply Resource Optimization Process
  Action Plan

## Slide 3: IRP Objectives
Present a transparent roadmap of the overall Company plan…
  For immediately-contemplated actions (i.e., in the next two years),
  to characterize emerging issues (and related approaches for mitigation, if necessary), and
  to outline the long-term direction a company is headed vis-a-vis the industry including economic trends, industry structure [partners such as the pipeline(s) and their impact/actions], technology, customer usage, etc.).
Promote internal coordination.
  Even the best-managed companies are challenged to have inter-departmental deep discussions, particularly among analysts.
Describe to stakeholders and the public the complex utility system unique to each local distribution company (LDC) and management decision-making processes.
While commissions do not approve the IRP—and, hence future actions—the description of potential actions generally provides for expeditious response of such future requests because stakeholders have a basis for what is driving those decisions.

## Slide 4: Stakeholder Engagement Process
The Company’s Gas Supply Oversight Committee (GSOC) and other senior management are actively involved throughout the IRP Process.
Input and feedback from Cascade’s Technical Advisory Group (TAG) is an important resource to help ensure the IRP includes perspectives external to the Company and responsive to stakeholders.
Five Technical Advisory Group (TAG) meetings were held in Seattle.
Multiple opportunities for public participation were available.
Several walkthroughs of technical components (e.g., SENDOUT® modeling) were conducted upon request.

## Slide 5
“Original” 2018 IRP TIMELINE

## Slide 6: Demand Forecast Process

## Slide 7: Expected Growth
Cascade expects system load growth to average 1.25% per year or 25% over the 20-year planning horizon.
 | Residential | Commercial | Industrial | System
2019-2038 | 1.44% | 0.94% | 0.45% | 1.25%

## Slide 8: Methodology Evolutions
Stochastic analysis of growth
Stochastic analysis of weather using Monte Carlo simulations

## Slide 9: Pipeline transport flow

## Slide 10: Highlights For The 2018 Portfolio Design
Portfolio procurement design based on a declining percentage each year, accordingly:
  Year 1: ~80% of annual requirements;
  Year 2: ~40%;
  Year 3: ~20%.
    80% allows more flexibility operationally; and
    Allows us to be in the market monthly through FOM purchase or Day Gas purchases.
Hedged Percentages (fixed-price physical) Currently max 40% of annual requirements. Second year should be set at 25%, and 20% hedged volumes for year three.
GSOC would consider a modification of this plan if the outer year 3 year forward price is 20% higher/lower than the front month over a reasonably sustained period.
Annual load expectation (Nov-Oct) is approximately 30,000,000 dths, consistent with recent load history.

## Slide 11
Chart: 
| AECO | HUNT | SUMAS | STATION 2 | RM POOL | WY POOL | OPAL
Total | 3940000 | 9548000 | 1204000 | 365000 | 2094750 | 2884500 | 2715000
2018/2019 Supply by Location

## Slide 12
Chart: 
Current Supply | 56000
RFP Supply | 80000
FOM Spot Gas | 10000
SGS Storage | 56366
Daily Spot Gas | 10000
Peaking Deal | 20000
3rd Party Citygate | 10000
Pipeline Pack | 8156.07
LS Storage | 78125
Peak Day Stack Example

## Slide 13: GHG Emissions from Natural Gas Industry
Natural Gas Distribution Facility Emissions;
  Fugitive methane emissions from pipeline infrastructure and CO2 emissions from combustion equipment;
    Cascade’s annual facility emissions in Washington are about 27,000 metric tons of CO2.
Natural Gas Distribution Customer Emissions;
  Cascade’s core customer CO2 emissions from combustion of natural gas are in the range of about 2 to 2.5 million metric tons of CO2 per year.
At this time, we are not required to consider upstream/downstream GHG emissions in permitting our types of projects/activities.

## Slide 14: Cascade’s GHG Emission Reductions
Methane fugitive emissions and leak reductions;
  Cascade became a founding member of EPA’s Natural Gas Star Methane Challenge Program in March 2016;
    Participating in Excavation Damages Prevention.
  System Integrity Projects.
Energy efficiency and conservation programs.
Streamlining emissions through demand management strategies including conservation and direct use.

## Slide 15: GHG Policy Trends
Local
  Municipal-level action due to less national focus;
  Local movements to monitor:
    City of Bellingham - Reduce municipal greenhouse gas emissions to 85% below 2000 levels by 2030 and 100% below 2000 levels by 2050. Reduce community emissions by 70% below 2000 levels by 2030 and 85% below 2000 levels by 2050.
    Whatcom County - Committed to the “Ready for 100” campaign: 100% renewable electricity for county operations and larger Whatcom County community by 2035 , Established commitments in ordinance.
    City of Bend - Voluntary goals established in 2016 for city facilities and operations: 40% reduction of 2010 baseline year emissions by 2030, 70% reduction of 2010 baseline year emissions by 2050. May determine to use more recent years for baseline, and could potentially could expand voluntary goals community-wide .
    Go 100% Renewable Energy lists some additional local commitments.

## Slide 16: CO2 Adders Modeled
Main cost modeled - Social Cost of Carbon with a 3% discount rate.
Other sensitivities modeled:
  I-1631 Ballot Initiative
  Gov. Inslee proposed tax
  House of Representatives Market Choice
Emission Reduction Unit costs not used as a carbon adder due to court invalidating CAR.
Sensitivity analyses include 0%, 20%, and 30% environmental adder sensitivities.
Chart: Carbon Cost Projection - $/Dth
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038
SB 6203 - Inslee/Carlyle Carbon Tax | 0.61975 | 0.71271 | 0.80567 | 0.89863 | 0.99159 | 1.0846 | 1.1775 | 1.2705 | 1.3634 | 1.4564 | 1.5494 | 1.5494 | 1.5494 | 1.5494 | 1.5494 | 1.5494 | 1.5494 | 1.5494 | 1.5494
I-1631 | 0.77468 | 0.8944 | 1.0167 | 1.1415 | 1.269 | 1.3992 | 1.5321 | 1.6679 | 1.8066 | 1.9481 | 2.0927 | 2.2404 | 2.3912 | 2.5452 | 2.7024 | 2.863 | 3.027 | 3.1944 | 3.3655
Social Cost of Carbon - 3% Discount | 2.1691 | 2.1691 | 2.2208 | 2.2724 | 2.3241 | 2.3757 | 2.4273 | 2.479 | 2.5306 | 2.5306 | 2.5823 | 2.6339 | 2.6856 | 2.7372 | 2.7889 | 2.8405 | 2.8922 | 2.9438 | 2.9954
House Market Choice | 1.2395 | 1.2896 | 1.3417 | 1.3959 | 1.4523 | 1.5109 | 1.572 | 1.6355 | 1.7016 | 1.7703 | 1.8418 | 1.9162 | 1.9936 | 2.0742 | 2.158 | 2.2452 | 2.3359 | 2.4302 | 2.5284

## Slide 17: Avoided Cost Overview
For the 2018 IRP, Cascade has revamped its avoided cost formula to create a more transparent and intuitive final number.
Cascade evaluates the impact that a range of environmental externalities, including CO2 emission prices, would have on the avoided costs in terms of cost adders and supply costs.
The Company produces an expected avoided cost case based on peak day for each of four climate zones.
New to this IRP cycle, Cascade will include avoided distribution system costs in its final calculation.
These are calculated by taking Cascade’s margin for each rate class, and deriving a one day system weighted margin figure, which is assumed to grow by inflation each year.

## Slide 18: Share of 2018 WA IRP Avoided Cost

## Slide 19
Nominal Avoided Cost by Conservation Zone, 2018 WA IRP (Cost per Therm)

## Slide 20: Conservation Short term Annual Goals
 | 2018* | 2019 | 2020
C&I | 345,000 | 370,587 | 437,271
RES | 420,000 | 333,424** | 369,466
Snapshots
Residential programs brought in-house 2016
Incentives increased 2017
  Residential > Commercial/Industrial
  Both Programs increased uptake
  Improved DBtC ratio
2019 Program Design adopted AEG’s LoadMAP updates and incorporated lower Avoided Costs
  Maintains most Residential offerings
  Increases many C&I rebates
  Adds new measures
Monitor 2019 C/I vendor performance
* 2018 figures represent preliminary performance
** 2019 residential reflects lower deemed therms

## Slide 21
CPA Therm Results
Select therm savings updated per 2018 CPA for the 2019 Program Year – reflect normal weather
LoadMAP Model Forecast Process

## Slide 22: Biennium Performance
Annual Performance
Cumulative potential DSM Forecast
Twenty Year Total:
47 Million
therms
Year 20 Cumulative DSM = 16% of Core Forecasted Demand

## Slide 23: LOW-INCOME WEATHERIZATION
Increase in forecasted program savings anticipated as a result of tariff updates in August 2018
  $10,000 per project cap removed
  Health and Safety specifications broadened to include all H&S associated with qualified measures as part of total project cost
  Avoided costs upwardly adjusted to $18.77 for 30 year measures per most recently acknowledged IRP
  Added project coordination payment of 15% and indirect rate of 10% of total project costs
Synchronization with Commerce Deemed Measures Policy 5.2.7-SF in light of new Prevailing Wage requirements
Increased communication and coordination, & outreach with Agencies

## Slide 24: 2019 Program UPDATES
Residential
Added 2nd tier to Tankless, Duct Sealing & Insulation, as well as Windows
Consolidated fireplace incentives
Removed Conventional Water Heaters
Decreased Combination System due to new savings
Maintained New Home Certifications’ rebate levels
Increased Air Sealing, Boiler and Thermostat rebates
Added Floor Insulation & Windows
Removed Clothes Washers
Decreased standard rebates on two measures: Water Heaters and Gas Conveyer Oven
Increased rebates on 13 measures: Insulation, Furnaces, Boilers, Tankless, Fryers, Radiant Heating, Double Rack and Convection Ovens, Pipe Insulation, Dishwasher, and more.
business

## Slide 25: Distribution System Planning Project Process Flow
Info & Data
Project & Schedules

## Slide 26: Distribution System Planning
Cascade plans to undertake the following distribution system enhancement projects over the next four years:
Umatilla 2” Reinforcement
Pendleton 4” IP Reinforcement
Pendleton 4” HP Reinforcement
Pendleton Korvola Road 4” PE RE
Bend 8”/6” HP Steel Reinforcement
RF; 4” PE; Bend; 600’ Hayes Ave
RF; 4” PE; Bend; 600’ Archie Briggs Rd

## Slide 27: Current Optimization Methodology Flow Chart

## Slide 28: Steps 1-4
As-is Analysis: Deterministic optimization of current resources.
Introduce Additional Resources: Incremental supply, storage, transportation.
Stochastic Analysis: Run portfolios through Monte Carlo weather simulations.
Rank Portfolios: Using risk adjusted total system cost and unserved means and Value at Risk (VaRs).

## Slide 29: Steps 5-8
Stochastic Weather: Top ranked portfolio undergoes Monte Carlo simulations.
Exceed limits? Examine results, ensure VaR/mean limits were not exceeded.
Stochastic Price: Top ranked portfolio undergoes Monte Carlo simulations.
Exceed limits? Examine results, ensure VaR/mean limits were not exceeded.
29
29

## Slide 30: As-Is Analysis Shortfalls

## Slide 31: Final Ranking of Portfolios

## Slide 32: Top Ranked Candidate Portfolio Components
Bremerton Shelton Realignment
Incremental GTN Capacity From Stanfield – 8,369 Dth by 2028, 22,533 dth by 2038
Incremental GTN Capacity From Kingsgate – 1,291 Dth by 2038
Monitor Incremental Nova

## Slide 33: Peak Day Transport Vs. Demand

## Slide 34: Conclusion
Cascade has identified potential deficiencies starting in 2019.
From 2019-2023, Cascade expects the Bremerton-Shelton acquisition to solve this shortfall.
From 2024 through the end of the planning horizon, Cascade uses a mix of incremental Transportation and DSM to solve the deficiency.
Cascade will continue to monitor the GTN shortfall in further IRPs.
With the resource mix that is designated the “Preferred Portfolio” Cascade forecasts the ability to serve all firm demand through the 20-year planning horizon.

## Slide 35: 2-Year Action Plan
Cascade will make a recommendation to GSOC regarding the volume and timing of acquiring incremental GTN capacity.
Cascade will continue to monitor NGTL incremental capacity and Spire storage.
Cascade will complete discussions with NWP regarding their Shelton lateral proposal.
Cascade will also continue to explore biogas opportunities.
Cascade will continue to work with Gelber & Associates to design and implement processes and analytics to comply with the WUTC UG-132019 policy statement.
Continue active participation in regional LDC IRP processes.
The Company will attempt to increase stakeholder engagement for the IRP process.
Cascade will cross-validate new methodologies to ensure the accuracy of new modeling techniques.
Investigate incorporating a risk premium into the avoided cost calculation.

## Slide 36: 2-Year Action Plan
Monitor code updates, emerging technologies and research feasibility.
Continually reassess ramp rates.
Extend NEEA membership into Cycle 6 (2020-2024).
Expand and enhance outreach in Commercial/Industrial, Trade Ally and customer engagement.
Launch pilots and explore additional geographically targeted options.
Increase LI Weatherization engagement.

## Slide 37
Cascade will either begin or continue to participate/monitor the following items:
  Participate in City of Bellingham Climate Action Plan discussions;
  Participate on City of Bend Climate Action Steering Committee;
  Monitor service areas for potential Greenhouse Gas (GHG) reduction goal development relating to energy delivery and supply;
  Monitor carbon pricing and policy developments nationally and statewide (i.e., 2019 carbon tax or cap and trade bills, Market Choice, etc.);
  Monitor federal and state GHG regulation development for energy industry; and
  Continuation of current emission reduction and monitoring endeavors (i.e., Methane Challenge Program, Renewable Natural Gas studies).
2-Year Action Plan

## Slide 38: 2018 Integrated Resource Plan Presentation to WUTC Commissioners and Stakeholders
Monday March 11th, 2019
WUTC Offices
Olympia, WA
Cascade Natural Gas Corporation