##### PROPOSED DRAFT REPORTING REQUIREMENTS

WAC     480-75-036  Maps, drawings, and records of hazardous liquid facilities.

All petroleum pipeline companies must prepare, maintain,  and have available for inspection, copies of maps, drawings, and records as outlined in

49 CFR 195.404 that pertain to pipeline safety issues for a company's hazardous liquid facilities.  The maps, drawings, and records must be of sufficient scale and detail as is necessary to show the size and type of material of all facilities.

WAC     480-75-037  Reporting Requirements for proposed construction.

At least 30 days prior to the commencement of construction of a hazardous liquid pipeline

(as defined in “49 CFR 195.1 – Applicability”) the Pipeline Company will submit “FORM Z” (see attached) for review.

WAC     480-75-038  Pressure testing reporting requirements

If pressure testing is to be used to increase the maximum operating pressure of a pipeline, companyies must file a report with the commission at least 45 days prior to the pressure increase stating the change in the maximum operating pressure and the steps required to qualify the pipeline for higher operating pressure.

WAC     480-75-039  Incident Reporting

(1)  Accidents on intrastate hazardous liquid pipelines reportable under 49 CFR 195.50 and 49 CFR 195.52 must be reported by  telephoneto the commission, as soon as practicable but not to exceed two hours after the occurrence, of an incident.

#### Within 30 days of the incident,  a copy of the DOT 7000-1 report must be sent to the commission.WAC  480-75-040  Depth of Cover Survey

Every five years, depth-of-cover surveys must be conducted in right-of-ways subject to subsoiling.

#### WAC 480-75-042  Operations safety plan requirements

(1)  Each operator must prepare an operations safety plan (Plan) that demonstrates the pipeline system is designed, constructed, operated, and periodically modified to provide for protection of the public and the environment.  Facility operations must follow the Plan.  The Plan must be thorough and contain enough information, analysis and supporting documentation to demonstrate the company’s ability to meet the requirements of this chapter.  The Plan may be incorporated into a company’s existing operation, maintenance, or emergency plan as required by Title 49 CFR 195.402.

(2)  A log sheet must be included in the Plan to record amendments. The log sheet must include the date the old section was eliminated; any new sections that were added; the date; the initials of the individual making the change; and the signature of the person responsible for reviewing the amendment.   A description of the amendment(s) and its purpose must be included.

- at a minimum, the Plan must include the following:

(i)     the requirements in chapter 480-75 WAC,

        - a schedule of inspection and testing of all the mechanical components and electronic components within the pipeline system,

        - structural integrity of all pipelines determined through pressure testing, in-line inspection surveys, or other appropriate techniques,

        - failsafe systems including emergency shutdown and isolation procedures,

        - emergency management training for operators,

        - procedures for responding to earthquakes that must include a threshold for line shutoff, and procedures for integrity monitoring prior to restart,

        - procedure for assessing the potential for impacts on the pipeline system due to landslides.  Operators with facilities located within potential landslide areas must develop monitoring and remediation procedures for ensuring that pipeline integrity is maintained at these areas,

(3)  Hazardous liquid pipeline companies must submit a Plan to the commission within 12 months after the adoption date of this rule.  New pipeline operators must submit a Plan to the commission no later than sixty days (60) prior to startup.

The Plan must be submitted to:

Washington Utilities and Transportation Commission

Pipeline Safety Division

P.O. Box 47250

1300 S. Evergreen Park Dr. SW

Olympia, WA 98504-7250

(4)  Amendments to the Plan must be submitted to the commission within five days of the change.

(5)  Plans are subject to the commission’s review.  A Plan is deemed fit for service when it provides for pipelines that are designed, developed, constructed, operated and periodically modified to provide for public safety and protection of the environment.

(6)  The commission may require that a Plan be modified whenever it is determined that the pipeline does not meet the requirements of this chapter, or the pipeline is not designed, constructed, operated and periodically modified to provide for public safety and protection of the environment.

(7)  The operator must ensure that appropriate personnel are trained and familiar with the Plan’s content.

(8)  Plans must be evaluated annually and resubmitted to the commission every five years.