## Slide 1: Planning Process
UTC Rulemaking for Integrated Resource Planning Transmission and Distribution Workshop
March 10, 2017

## Slide 2: Planning considerations differ between gas and electric
* “Transmission” defined by how much stress pipeline is operating at (>20% SYMS)
Considerations | Natural Gas | Electric
Service obligations | Feasibly serve; Upon service - obligation to serve | Obligation to serve
Design Demand | Typically planning for winter peak hour | Winter and summer peak depending on customer equipment
Outages | Outages pose safety risk and are avoided; typically design for colder temperatures than electric | Outages can occur and result in reliability concerns
System configuration | High pressure backbone; networked/2 way flow, where practical Intermediate/low pressure pipelines; highly networked/2 way flow | Transmission networked; 2 way flow Distribution feeders maybe networked: 1 way flow Distribution laterals typically radial
Regulation | Operations and Maintenance including design is heavily regulated at all levels and audited by UTC routinely | Bulk Electric System is heavily regulated by FERC/NERC and audited every 2-3 years by WECC
Source supply | Interstate pipelines - Williams Northwest Pipeline | Self supply with PSE owned generation or from other providers such as Bonneville Power Authority
Regional planning responsibility | Interstate pipeline operators | Columbia Grid
Source augmentation | Mobile or permanent liquified natural gas or compressed natural gas injected on site from core supply, biogas | Battery storage, distributed generation

## Slide 3: Detailed process used to determine infrastructure needs and investments
Natural gas and electric infrastructure planning uses the same core process

## Slide 4: Multiple drivers for evaluating need
Drivers/criteria
  Customer request
  Load growth
  Reliability
  Compliance
  External commitment
  Aging Infrastructure
  Integration of resources

## Slide 5: Analysis tools are utilized
TOOL | USE | INPUTS | OUTPUTS
SynerGi® | Network modeling | Gas and electric distribution infrastructure and load characteristics | Predicted system performance
Power World Simulator – Power Flow | Network modeling | Electric transmission infrastructure and load/generation characteristics | Predicted system performance
PSS/E Power Flow & Stability | Network modeling | Electric transmission infrastructure and load/generation characteristics | Predicted system performance
PSLF Power Flow & Stability | Network modeling | Electric transmission infrastructure and load/generation characteristics | Predicted system performance
Electric Predictive Spreadsheet | Predictive analysis | Outage history | Predicted outage savings
Gas Outage Spreadsheet | Predictive analysis | Network model output for future capacity | Predicted outage savings
Estimated Unserved Energy (EUE) Spreadsheet | Electric financial analysis | Project costs; hourly load data; load growth scenarios | Net Present Value; income statement; load growth vs. capacity comparisons; EUE
Investment Decision Optimization Tool (iDOT) | Project data storage & portfolio optimization | Project scope, budget, justification, alternatives and benefits; resources/financial constraints | Optimized project portfolio; benefit cost ratio for each project; project scoping document

## Slide 6: Alternatives are evaluated
Electric
Add energy source
  Substation
Strengthen feed to local area
  New conductor
  Replace conductor
Improve existing facility
  Substation modification
  Expanded right-of-way
  Uprate system
  Rebalance load
  Modify automatic switching scheme
Load reduction
  Fuel switching
  Distributed energy resource
  Natural gas conversion
  Conservation / Demand response
  Load control equipment
  Possible new tariffs
Do nothing
Gas
Add energy source
  City-gate station
  District regulator
Strengthen feed to local area
  New high pressure main
  New intermediate pressure main
  Replace main
Improve existing facility
  Regulation equipment modification
  Uprate system
Load reduction
  Fuel switching
  Conservation
  Load control equipment
  Possible new tariffs
Do nothing

## Slide 7: Alternatives are evaluated and recommendations compared
Benefit analysis performed across multiple types of projects and risks
Maximize value
to PSE, customers,
employees,
and shareholders
PSE financial
success
Stakeholder
Concerns
/perceptions
Public
Workers
Natural
environment
Platform
for
success
Regulatory
compliance
Treated as constraint
Health
safety & the
environment
Key constituents
Citizens
WECC/NERC
WUTC
IPP’s
State & fed agencies
NGO’s
Other utilities
Property owners
Project Cost
Cost Savings
in Other Areas
Impacts on
Revenue
Customer
satisfaction
Outages
Unmet
Energy needs
Service
quality
Strategic
infrastructure
Flexibility
New technology,
learning
Advance other
components of
strategy

## Slide 8: Transparency
Growth Management Act Comprehensive Plans
Community engagements
Permitting processes
Project information and schedules on PSE website
Specific project community engagements
Commission Policy on Accelerated Replacement of Pipeline Facilities with Elevated Risk; effective December 31, 2012
Electric Service and Reliability Quality Reports