## Slide 1: Distribution System Planning WUTC
March 10, 2017
Juliet Homer, PNNL

## Slide 2: Agenda
Background
  U.S. Department of Energy efforts
  Resources
Washington Context
Distribution System Planning Tools Assessment
Summary of Efforts in Other States Related to Five Questions
Emerging Issues in IRP
Possible Places to Start
Next Steps for DOE Projects

## Slide 3: DOE’s grid modernization initiative
Aggressive five-year grid modernization strategy
  Alignment of the existing base activities among DOE Offices
  An integrated Multi-Year Program Plan (MYPP)
  Laboratory consortium with core scientific abilities and regional outreach
Scope
  Developing new architectural concepts, tools and technologies that measure, analyze, predict, protect and control the grid of the future
  Enabling the institutional conditions that allow for more rapid development and widespread adoption of these tools and technologies
Grid Modernization Lab Consortium
  Collaboration among 14 DOE national labs and regional networks that will help develop and implement the MYPP
  Includes support for PUCs and utilities on distribution planning
Slide taken from LBNL / Lisa Schwartz presentation to MN PUC on Oct. 24, 2016

## Slide 4: U.S. Department of Energy (DOE) – Grid Modernization Lab Consortium (GLMC)
Four main institutional support activities under DOE’s Multi-year Program Plan:
  Provide technical assistance to states and tribal governments
  Support regional planning and reliability organizations
  Develop methods and resources for assessing grid modernization: Emerging technologies, valuation and markets
  Conduct research on future electric utility regulations
Each activity has specific goals and target achievements to be completed by 2020

## Slide 5: GMLC 1.4.25 - Distribution System Decision Support Tool Development and Application
Expected Outcomes
Provide Technical Assistance to State Regulators in partnership with NARUC
Identify Gaps in Existing and Emerging Planning Practices & Approaches
Compile information on existing planning tools, identify gaps and make recommendations
Provide Technical Assistance (guides) to Electric Utility industry through organizations
Project Participants and Roles
Michael Coddington – PI – NREL (Utility Practices)
Lisa Schwartz – Lead for LBNL (Regulatory)
Juliet Homer – Lead for PNNL (Tools & Regulatory)
Project Description
Identify strategies and provide technical assistance to state regulators and utility organizations that focus on advanced electric distribution planning methods and tools, with a focus on incorporating emerging grid modernization technologies and significant deployment of DER

## Slide 6: Resources
Summary of Distribution Planning Activities in Leading States
Summary of Distribution Analyses with a Focus on DERs
  Summarizes analysis capabilities and relative maturity levels
Upcoming: Distribution planning training for commissioners and staff (labs and NARUC)
Email me for copies of these: Juliet.Homer@pnnl.gov
DSPx project
  A separate but connected effort also led by DOE
  Instigated by CPUC and NYPSC and regulators from DC, HI and MN
  “DOE-OE, with the sponsoring commissions, has brought together a team with industry expertise in the areas of grid planning, operations, market design, related technologies, and policy to support this effort.”
  Volume I: Customer and State Policy Driven Functionality
  Volume II: Advanced Technology Market Assessment
  Volume III: Decision Maker Guide
  www.doe-dspx.org

## Slide 7: Washington Context
Taken from Notice of Workshop and WUTC Concept Paper
Goal: Ensure utilities are applying IRP principles as they consider T&D resource options – electric and natural gas
  Improve transparency of T&D planning in IRP process
Proposal: Electric and gas utilities analyze some subset of their distribution system in each IRP cycle
Question topics:
  Baseline Information – granular understanding of current conditions, visibility, tools
  Scope of distribution plan – how prioritize lines, standard approaches to valuing and calculating levelized costs and benefits
  How to link T&D planning to resource acquisition – 5-year competitive bidding process
  Pros and cons of utilities versus others analyzing solutions
  Role of stakeholders

## Slide 8: Tools Assessment
Studied 10 Distribution System Analysis (DSA) tools
  8 commercial tools and 2 open source research tools
Evaluated maturity levels of analysis types
General categories considered:
  Power flow analysis
  Power quality analysis
  Fault analysis
  Dynamic analysis
  Market analysis
Distributed Energy Resources (DER) analyses considered:
  DERs and net load projections
  Basic distribution engineering with DERs
  Time-series power flow analysis with DERs
  Advanced optimization with DERs
  Hosting capacity and interconnection
  Dynamic studies with DERs
  Co-simulation with transmission systems.

## Slide 9: DSPx Planning Analysis Categories
Figures from DSPx Draft Volume 2 Report – www.doe-dspx.org

## Slide 10: Analysis Type Maturity Levels

## Slide 11: Modeling DERs
Integration of DERs may result in overcurrent, overvoltage, and miscoordination between protective devices
Hosting-capacity studies determine the amount of DERs that can be accommodated without affecting feeder power quality or reliability
  Four aspects: Voltage, power quality, protection and thermal limits
Interconnection impact studies cover the same things as hosting-capacity studies but for a single DER project
Most existing modeling tools can conduct basic distribution engineering studies and time-series simulations with DERs

## Slide 12: Nascent Areas and Gaps
Projecting growth of types and locations of DERs
Developing and validating an accurate distribution system model**
Interactions between the distribution and transmission systems
Advanced optimization studies for DERs with storage systems
Automation of hosting capacity / interconnection analysis, including workflow management aspects
Multiple DER anti-islanding studies
Simulating microgrids with custom controls
Inverter modeling for volt/var control
Support for holistic planning for sensing and measurement devices: Types, number, and location**
**Items 2) and 9) relate to Question 1 re: Baseline Info – Level of detail in feeder model and therefore granularity of data needed depends on analysis requirements. Start with questions that need to be answered.

## Slide 13: States are advancing distribution planning in a variety of ways.
Requirements for utilities to file distribution system/grid modernization plans with stakeholder engagement (e.g., NY, CA, MA)
Requirements for hosting capacity analysis (e.g., MN, CA, NY)
Consideration of cost-effective non-wires alternatives (e.g., NY, RI, VT)
Locational net benefits analysis for DERs at specific locations (e.g., CA)
Investigations into DER procurement strategies (e.g., HI, NY, CA)
Requirements for utilities to report regularly on poor-performing circuits and propose investments (e.g., PA)
Storm hardening and undergrounding requirements (e.g., FL)
Aggregation and participation of DERs in wholesale markets (e.g., TX)
Reliability codes and annual compliance reports (e.g., OH, IL)
Smart grid reporting (e.g., WA, OR)
From Lisa Schwartz’s presentation to MN PUC on Oct. 24, 2016

## Slide 14: General benefits of improved distribution planning
Makes transparent utility distribution system investments before showing up individually in rider or rate case
Provides opportunities for meaningful PUC and stakeholder engagement
Considers uncertainties under a range of possible futures
Considers all solutions for least cost/risk
Motivates utility to choose least cost/risk solutions
Enables consumers and third parties to participate in providing grid services
From Lisa Schwartz’s presentation to MN PUC on Oct. 24, 2016

## Slide 15: Stated Objectives of State DER Planning and Grid Modernization Activities
Stated Goals of Grid Modernization Efforts: | CA | DC | HI | IL | ME | MA | MN | NV | NH | NY | OR | TX
Protect and enhance reliability and resilience | X | X | X | X | X | X | X | X | X | X | X | X
Develop and integrate renewables and distributed resources | X | X | X |  | X | X | X | X | X | X | X | X
Lower costs | X | X | X |  | X | X | X | X | X |  | X | 
Enhance customer service and choice | X |  | X | X |  |  | X |  | X | X | X | 
Save energy, reduce peak, optimize demand |  | X |  |  | X | X |  |  | X | X | X | 
Optimize existing generation, transmission and distribution systems |  |  | X |  | X |  | X |  | X | X | X | 
Modernize / accommodate new smart technologies | X |  |  | X | X |  | X |  |  |  |  | 
Animate markets / provide grid platform | X |  |  |  |  |  | X |  |  | X |  | X
Enhance safety and security |  |  |  | X |  |  | X |  |  |  | X | 
Reduce emissions | X |  |  |  | X |  |  |  |  | X |  | 
Support workforce and economic development |  |  |  | X |  | X |  | X | X |  |  | 
Facilitate integrated planning |  |  |  |  |  |  | X |  |  |  |  | 

## Slide 16: Question 1) Baseline informational needs
From CA DRP Rulemaking R.14-08-013 a “baseline” hosting capacity methodology was developed. First two (of four) steps are:
  1) Establish distribution system level of granularity
    Establish Distribution Planning Areas (DPA)
    Perform analysis down to specific nodes within each line section of individual feeders.
    Nodes are to be selected based on impedance factor
  Model and extract power system data
    Load forecasting analysis tool (LoadSEER) must be used to develop load profiles at the feeder, substation and system levels by aggregating representative hourly customer load and generation profiles.
    Load profiled developed for each Distribution Planning Area (DPA)
    Power flow analysis tool used to model conductors, line devices, load and generation components that impact circuit power quality and reliability.
In District of Columbia the PSC ordered PEPCO to provide a load research plan (LRP) detailing how it will use digital grid information in expansion plans and rate designs.

## Slide 17: Question 2) Scope of Distribution Plan
From CA DRP Rulemaking R.14-08-013: Locational benefits and costs evaluation should be based on:
  Reductions or increases in local generation capacity needs
  Avoided or increased investments in distribution infrastructure
  Safety benefits
  Reliability benefits
  Any other savings to the grid or ratepayers
All CA utilities were required to us a common locational benefits methodology based on the Commission-approved E3 cost effectiveness calculator - Distributed Energy Resource Avoided Cost Calculator (DERAC)
IOUs in CA were required to evaluate (at a minimum) one near-term (0-3 year project lead time) and one longer-term (3 or more year lead time) distribution infrastructure project for possible deferral.
  In May 2016 original guidance was expanded on to include at least one voltage support/power quality or reliability/resiliency related deferral opportunity.

## Slide 18: Value Components in PG&E’s Locational Net Benefits Analysis

## Slide 19: Question 2) Scope of Distribution Plan, cont.
In Minnesota – Statute 216B.2425, subd.8. requires Xcel Energy to:
  Conduct a distribution study to identify interconnection points on its distributions system for small-scale distributed generation resources, and
  Identify upgrades necessary to support DERs
Minnesota PUC required Xcel to complete a distribution study by 12/1/16 including hosting capacity analysis of each feeder for small scale distributed generation (< 1MW) and potential upgrades needed to support DG additions, including those in IRP filings.
  Xcel must provide an updated hosting capacity analysis in the fall of 2017
In New York, utilities required to submit Distributed System Implementation Plans (DSIP) to ((Case 14-M-0101):
  Serve as a source of public information on objectives, needs and opportunities
  Serve as a template for utilities to develop and articulate an integrated approach to planning, investment and operations
  Enable the Commission to supervise implementation of REV in the context of system operations

## Slide 20: Question 2) Scope of Distribution Plan, cont.
NY PSC Staff released a Staff White Paper on Benefit-Cost Analysis that spells out the specific avoided cost calcs that should be performed by utilities in DSIPs
Initial utility DSIPs included:
  A self-assessment of utilities’ current capabilities
  A proposed roadmap for technology investments to improve grid intelligence and prepare it for higher DER penetration levels
  Data that supports greater transparency for planning and distribution market development.
Following individual utility DSIP submissions, a Supplemental Joint DSIP was filed that included:
  A load and DER forecasting stakeholder engagement process;
  A process for coordinating with NYISO on short- and long-term forecasting;
  A non-wires analysis suitability framework (forthcoming implementation matrices);
  A detailed roadmap for hosting capacity; and
  An interconnection data platform and process roadmap.

## Slide 21: Question 3) How link T&D planning to resource acquisition
Hawaii requires utilities to submit Power Supply Improvement Plans (PSIP) to the PUC that detail utility’s plans for major resource acquisitions and system operations (Docket 2014-0183).
Massachusetts 10-year grid modernization plans must include:
  A 5-year Short-Term Investment Plan (STIP) for capital investments
  Comprehensive business case analysis to support capital investments in STIP

## Slide 22: Question 4) Necessary for Utilities to Conduct Analysis of Solutions?
From CA DRP Process – Results of Integration Capacity Analysis (ICA) must be published via online maps
  Locational Net Benefits Analysis (LNBA) Working Group
In Minnesota, Statute 216.B.2425, subd.8. says when considering a large transmission or generating investment, utilities must evaluate possible alternatives including efficiency, load management and DG
One of the key drivers of NY REV is to better animate the market.
  NY PSC looking closely at the concept of Distribution System Operator (DSO)
In New York, utilities required to submit Distributed System Implementation Plans (DSIP) to ((Case 14-M-0101) that serve as a source of public information on objectives, needs and opportunities

## Slide 23: Question 5) Role of Stakeholders
From CA DRP Process after submittal of first DRP, CPUC directed through major IOUs to convene two working groups to monitor and provide input on demos and to refine methodologies:
  Integration Capacity Analysis (ICA) Working Group
  Locational Net Benefits Analysis (LNBA) Working Group
In Minnesota, stakeholders participating in Commission workshops identified policy-related suggestions, including:
  Making energy usage data easily accessible to customers
  Enabling third-party aggregation of demand response
  Offering consumers time-varying rates
In New York’s DSIP proceeding (Case 14-M-0101), the first step was for utilities to submit a plan and associated timeline for a stakeholder engagement process

## Slide 24: Emerging Issues in IRP
Distributed Generation (DG) can have significant impact on system operations, need for and timing of investments in conventional generation and T&D infrastructure
Utilities have limited direct control over adoption
That said, utilities:
  Do have some ability to target DG adoption
  Can plan for DG uncertainty
Key areas:
  How utilities are modeling DG adoption and its impact on bulk power system planning variables
  How utilities are valuing DG in resource plans
  How utilities and regulators are comprehensively assessing DG impacts, beyond traditional resource planning
  From The Future of Electricity Resource Planning by Fredrich Kahrl (E3), Andrew Mills (LBNL), Luke Lavin, Nancy Ryan and Arne Olsen (E3), Berkeley Lab, September 2016: feur.lbl.gov

## Slide 25: Emerging Issues in IRP
Emerging best practices
  Generating DG forecasts using models of customer adoption behavior
  Assessing locational value of DG, incorporating distribution deferral values in DG evaluation
  Making use of “triggers” and “signposts” to revisit plans if adoption is significantly different than anticipated
  From The Future of Electricity Resource Planning by Fredrich Kahrl (E3), Andrew Mills (LBNL), Luke Lavin, Nancy Ryan and Arne Olsen (E3), Berkeley Lab, September 2016: feur.lbl.gov

## Slide 26: Possible places to start:
Take early integration steps - Consistency in inputs (assumptions, forecasts), scenarios and modeling methods — updated in time — across distribution planning, integrated resource planning and transmission planning
Account for all resources – Consider energy efficiency, demand response (including direct load control, smart Tstats and time-varying pricing), distributed generation and energy storage, alongside traditional distribution solutions
Specify DER attributes – In order to meet identified needs
Analyze multiple possible futures – DERs plus other scenario drivers
Consider CVR/VVO in distribution plans (and in IRPs)
From Lisa Schwartz’s presentation to MN PUC on Oct. 24, 2016

## Slide 27: Possible places to start - 2:
Phase in hosting capacity analysis – To facilitate DG integration and indicate better or more difficult locations
Pilot evaluation of locational impacts – Identify where DERs might offer greatest benefits
Integration of new utility systems – If/when ADMS, AMI and other new systems are implemented, specify in advance how they will be used in distribution planning and lock in early consumer benefits
Test new sourcing and pricing methods – e.g., competitive solicitations, tariffs, programs
Training for staff – e.g., DOE-funded courses starting next summer
From Lisa Schwartz’s presentation to MN PUC on Oct. 24, 2016

## Slide 28: Future efforts:
Part of DOE Distribution Support Tools Project:
  Distribution planning training for commissioners and staff (labs and NARUC)
  Phase II Analytical tools and gap assessment
DSPx project
  Decision Maker Guide

## Slide 29: Thank you
Juliet Homer, PNNL
  Juliet.Homer@pnnl.gov