## Slide 1: Energy Imbalance Market Update
Body of State Regulators
Lake Tahoe – Incline Village
May 22, 2016
Mark Rothleder
VP, Market Quality & Renewable Integration

## Slide 2: EIM benefits total $64.6 million as of 1st Quarter 2016
Region | 4th Quarter 2014 | 1st Quarter 2015 | 2nd Quarter 2015 | 3rd Quarter 2015 | 4th Quarter 2015 | 1st Quarter 2016
CAISO | $1.24 | $1.44 | $2.46 | $3.48 | $5.28 | $6.35
NV Energy | - | - | - | - | $.84 | $1.70
PacifiCorp | $4.73 | $3.82 | $7.72 | $8.52 | $6.17 | $10.85
Total | $5.79 | $5.26 | $10.18 | $12 | $12.29 | $18.9
All estimated gross benefits are in millions of dollars per EIM entity.
Region | October | November | December | Total
CAISO | $1.27 | $1.30 | $2.70 | $5.28
NV Energy | n/a | n/a | $0.84 | $0.84
PacifiCorp | $1.24 | $2.19 | $2.75 | $6.17
Total | $2.51 | $3.49 | $6.29 | $12.29
Notes: NV Energy began parallel operations on September 1 following market simulation
ISO and NVE confirmed completion of EIM readiness criteria with no exceptions and certified with FERC on October 1
Activation on November 1 is pending FERC approval of the readiness criteria and certification
ISO and NVE defined a rigorous support plan to monitor and quickly respond to conditions
NV Energy and the ISO are ready to monitor market results.
The ISO published a market quality report on October 1
Pricing performance improvement continues and ISO continues to provide documentation to FERC
Parallel operations with NV Energy will continue until October 31 to ensure systems are stable in advance of the transactions becoming financially binding on November 1
The available balancing capacity enhancement will be implemented upon FERC approval
Puget and APS
Both entities executed EIM Entity Agreements
EIM Scheduling Coordinator and Participating Resource Agreements are on track to be executed by December 1
ISO provided 100 level training and CBTs, which will continue through January. A course on Access Provisioning will occur in December
ISO conducted an operator application overview and tour for APS and PSE operators to assist with operator planning
Portland
Oct 2014 – Oregon Commission directed PGE to provide a cost-benefit analysis of joining a regional EIM
Sept 2015 - Announced plans to participate in ISO’s EIM and withdraw from market initiative led by the Northwest Power Pool Members’ Market Assessment and Coordination Committee
Idaho
Sept 2015 - Announced plans to withdraw from market initiative led by the Northwest Power Pool Members’ Market Assessment and Coordination Committee
Initiating a cost/benefit study for EIM and expects to make a decision first quarter 2016

## Slide 3
Reducing Renewable Curtailment | 1st Qtr 2015 | 2nd Qtr 2015 | 3rd Qtr 2015 | 4th Qtr 2015 | 1st Qtr 2016 | Total To-Date
Mwh curtailment avoided | 8,860 | 3,629 | 828 | 17,765 | 112,948 | 144,030
Estimated metric tons of CO2 displaced | - | 1,553 | 354 | 7,521 | 48,342 | 57,770
EIM
Puget Sound Energy and Arizona Public Service on track to Go-Live October 2016
Portland General Electric has begun integration work and planned Go-Live is October 2017
Idaho Power to join EIM in April 2018

## Slide 4: Calculating the benefits
Start with the net EIM transfer of each BA.
Running an offline optimization simulation, re-dispatch the online or available resources in each BA to zero out the net EIM transfers based on actual market bids and fixed costs. This is called the counter-factual dispatch.
The EIM benefit is the cost of the counterfactual dispatch by multiplying the re-dispatch volume by the associated EIM bid cost.
EIM benefit distribution is not allocated but rather is determined based on the counterfactual benefits if EIM area based on the counterfactual results for each BAs, inter BA EIM transfers, transfer prices and base schedule optimality

## Slide 5
Transfer
200 MW
B
A
Transfer limit 300 MW
G1: 100MW at $30/MWh
G2: 300MW at $35/MWh
BAA B
BAA A
L = 200 MW
None
Supply bids (incremental from base schedule):
Demand (incremental from base schedule):
G3: 100MW at $50/MWh
G4: 300MW at $55/MWh
Example 1: benefit from non binding transfer
G1: 100 MW at $35/MWh
G2: 100 MW at $35/MWh
EIM dispatch and LMP:
G3: 0 MW at $35/MWh
G4: 0 MW at $35/MWh
Counter factual dispatch:
G3: 100 MW
G4: 100 MW
G1: 0 MW
G2: 0 MW
Transfer
0 MW
G1: 100MW at $30/MWh
G2: 100MW at $35/MWh
Total EIM benefit (cost saving):
G3: 100MW at $50/MWh
G4: 100MW at $55/MWh
being replaced by
Cost saving = 100*50+100*55 -(100*30+100*35) = $4,000
BAA A benefit (profit):
being sold at $35
Profit = 200*35 -(100*30+100*35) = $500
G1: 100MW at $30/MWh
G2: 100MW at $35/MWh
BAA B benefit (cost saving):
being replaced by $35 transfer
Cost saving = 100*50+100*55 -(200*35) = $3,500
G3: 100MW at $50/MWh
G4: 100MW at $55/MWh

## Slide 6
B
A
Transfer limit 300 MW
G1: 100MW at $30/MWh
G2: 300MW at $35/MWh
BAA B
BAA A
L = 350 MW
None
Supply bids (incremental from base schedule):
Demand (incremental from base schedule):
G3: 100MW at $50/MWh
G4: 300MW at $55/MWh
Example 2: benefit from binding transfer
G1: 100 MW at $35/MWh
G2: 200 MW at $35/MWh
EIM dispatch and LMP:
G3: 50 MW at $50/MWh
G4: 0 MW at $50/MWh
Counter factual dispatch:
G3: 100 MW
G4: 250 MW
G1: 0 MW
G2: 0 MW
Transfer
300 MW
Transfer
0 MW
G1: 100MW at $30/MWh
G2: 200MW at $35/MWh
G3: 50MW at $50/MWh
Total EIM benefit (cost saving):
G3: 100MW at $50/MWh
G4: 250MW at $55/MWh
being replaced by
Cost saving = 100*50+250*55 -(100*30+200*35+50*50) = $6,250
BAA A benefit (profit):
being sold at $42.5=0.5*(35+50)
Profit = 300*42.5 -(100*30+200*35) = $2,750
G1: 100MW at $30/MWh
G2: 200MW at $35/MWh
BAA B benefit (cost saving):
being replaced by $42.5 transfer
Cost saving = 50*50+250*55 -(300*42.5) = $3,500
G3: 50MW at $50/MWh
G4: 250MW at $55/MWh

## Slide 7
B
A
Transfer limit
0 MW
G1: 300MW at $30/MWh (BS=100)
G2: 400MW at $35/MWh (BS=100)
BAA B
BAA A
L2 = 100 MW (BS=100)
Supply bids (including base schedule):
Demand (including base schedule):
G3: 200MW at $50/MWh (BS=100)
G4: 300MW at $55/MWh (BS=0)
Example 3: benefit from optimizing base schedules
G1: 200 MW at $30/MWh
G2: 0 MW at $35/MWh
EIM dispatch and LMP:
G3: 100 MW at $50/MWh
G4: 0 MW at $50/MWh
Counter factual dispatch:
G3: 100 MW
G4: 0 MW
G1: 100 MW
G2: 100 MW
Transfer
0 MW
Transfer
0 MW
G1: 200MW at $30/MWh
G3: 100MW at $50/MWh
Total EIM benefit (cost saving):
G1: 100MW at $30/MWh
G2: 100MW at $35/MWh
G3: 100MW at $50/MWh
being replaced by
Cost saving =
100*30 +100*35 +100*50-200*30+100*50)=$500
BAA B benefit (cost saving):
Cost saving = 100*50 -(100*50) = $0
G3: 100MW at $50/MWh
L1 = 200 MW (BS=200)
BAA A benefit (cost saving):
Cost saving = 100*30+100*35 -(200*30) = $500
G1: 100MW at $30/MWh
G2: 100MW at $35/MWh
G1: 200MW at $30/MWh
being replaced by
G3: 100MW at $50/MWh
being replaced by