## Slide 1: Cascade Natural Gas Corporation Integrated Resource Plan Technical Advisory Group Meeting #2
Tuesday, July 19, 2016
Seattle-Tacoma International Airport Conference Center

## Slide 2: Agenda
Introductions

## Slide 3: IRP Staffing and Support
Two positions added
Resource planning analysts
First new analyst starts late July
Have posted for the second new analyst
Hired Bruce Folsom as IRP consultant

## Slide 4: IRP CONSULTANT
Cascade has hired Bruce Folsom
23 years with Avista Corporation
8 years with the Washington Utilities and Transportation Commission (WUTC)
Bruce has a B.S. in Environmental Studies from the University of Washington and an MBA in Business Administration from Seattle University.

## Slide 5: Among consultant tasks and deliverables
Providing recommendations and guidance to internal IRP team, suggesting alternative solutions, identify potential regulatory solutions related to the IRP, and assist in the development of the narrative of the 2016 WA IRP and addressing the 2017 OR IRP Annual Update.
Produce a discussion narrative on Alternative Forecasting Methodologies
Produce a discussion narrative on price elasticity in the Pacific Northwest region
Produce a discussion narrative on carbon legislation impacts on price forecast, system, supplies and recommend how Cascade should describe its “carbon policy” as it relates to the IRP
Working with the internal IRP team on ensuring the Company meets all OR and WA IRP guidelines
Assist Cascade in addressing open OPUC DRs from the 2014 IRP.

## Slide 6: CASCADE DEMAND STUDY
Recap of the 20 Year demand forecast

## Slide 7: Overview
The Cascade demand forecast developed for the IRP is a forecast of customers, core natural gas demand, and core peak demand for the next 20 years.
Cascade’s core load consists of approximately 53% residential and 47% commercial and industrial.
Data Aggregation
Historical Weather
Historical Demand
Linear Regression Analysis
Demand vs Weather
Non-Weather Dependent Demand Analysis
Growth
W&P Pop/Eco Growth
Forecast
Monthly Demand Forecast
Annual Peak Demand Day Forecast
Growth Scenarios
Annual Premise Count Projection
Weather Scenarios

## Slide 8: Overview
Forecast demand at the CityGate and CityGate Loop level.
CityGate Loops are a group of CityGates that service a similar area that are forecasted together due to pipeline operations.
CNGC forecast model is flexible giving Cascade the ability to:
  Update input data (gas demand and weather)
  Modify assumptions
  Modify CityGates and loops to be forecasted
  Run several scenarios

## Slide 9: Key Assumptions
  Seven weather locations effectively cover Cascade’s service territory.
  Using population growth assumes 1% increase in population translates to a 1% increase in residential customer count.
  Using employment growth assumes 1% increase in employment translates to a 1% increase in commercial and industrial customer count.

## Slide 10: Key Points
Cascade’s demand is principally weather and customer driven; the colder the weather or greater the customer count, the greater the demand.
This forecast uses 30 years of recent weather history as the “normal” temperatures.
Forecasted under various weather and growth scenarios – average year, cold year, warm year, extreme cold day, high growth, low growth, etc.
Analyze weather and demand for each of 55 CityGates and CityGate Loops that serve Core customers.
Growth factors are applied to each of the 20 years in the forecast for each CityGate.
  Heating demand does not appreciatively start until average temps dip below 60° F, therefore a 60° F threshold is used.

## Slide 11: Input Data
Historical Demand
  Pipeline actuals
  Gas Management System (GMS)
  Customer Care and Billing (CC&B)
Weather
  Schneider Electric
Population and Economic
  Woods & Poole
  Acquiring local market intelligence
Customer Count
  CC&B

## Slide 12: Demand Data
Historical core monthly demand by CityGate was primarily drawn from:
  Pipeline actuals from Electronic Bulletin Board (EBB)
  Cascade’s own Gas Management System (GMS)
Also examined CC&B (Customer Care and Billing) for data verification and premise count information.
Analyzing demand data from 2004 to 2015.

## Slide 13: Weather Data
Define weather in terms of HDDs (Heating Degree Day).
30 years of weather data for seven weather stations was used to make weather scenarios.
Weather data is from Schneider Electric.
Assign a weather station to each CityGate or CityGate Loop.

## Slide 14: Weather Stations
The seven weather stations are shown on the map.
Cascade’s customer base is shaded in aqua.
Each CityGate and loop is assigned to a weather station.

## Slide 15: New Linear Regression Analysis
Weather and Customers are the input variables and gas demand is the output:
Where b is demand/HDD/Customer and C is the constant baseload demand/Customer.
Goal is to predict demand at each CityGate/loop based on given weather (HDD) and customer.
Perform a linear regression or best fit analysis of monthly gas demand versus monthly HDDs and customers at each citygate for the past 12 years of data.

## Slide 16: Linear Regression Analysis for new model

## Slide 17: Heating Degree Day (HDD)
Heating degree day is used as the unit of measure for weather in the linear regression analysis .
Heating degree day is calculated by:
  Determine average high and low temperature for a given day.
  Daily average is subtracted from an HDD threshold (for example 60°F).
  If this produces a negative number, a value of zero is assigned.
Example:
  Daily high temperature = 60°F; Daily low temperature = 50°F
  Calculate average  55°F
  Subtract from HDD threshold (we will use 60): 60-55 = 5
  This example day has 5 HDD

## Slide 18: 65 vs 60 HDD Threshold
The historical threshold for calculating HDD has been 65°F .
It was determined that lowering the threshold to 60°F produces better results for Cascade’s service territory.
The graph shows that heating demand does not begin to increase until an HDD of five if the traditional 65°F is utilized.

## Slide 19: Acme Therms/HDD with 60 degree reference temperature

## Slide 20: Forecast Scenarios
Base case is normal weather with expected customer growth.
Sensitivity capability for cold and warm weather.
Sensitivity for low and high customer growth.

## Slide 21: Weather Scenarios
For weather scenarios, system wide HDDs are used by giving appropriate weight to the weather stations that have greater impact on system wide demand.
To determine the high case HDD weather scenario, the six coldest years were selected (20% of the coldest years out of 30). These years have the highest yearly total of HDDs.
To determine the low case HDD weather scenario, the six warmest years were selected (20% of the warmest years out of 30). These years have the lowest yearly total of HDDs.

## Slide 22: Weather Scenarios
High Demand High HDD (Cold)
Average Demand Average HDD
Low Demand Low HDD (Mild)

## Slide 23: Growth Data
Woods & Poole State Profile data is used for customer forecast.
Population data is used for the Residential Customers.
Commercial and Industrial growth factors used Farm, Construction, and Manufacturing earnings in previous model.
New model uses: Farm Employment, Forestry, Fishing, Related Activities & Other, Mining Employment, Utilities Employment, Construction Employment, Manufacturing Employment, Wholesale Trade Employment, Retail Trade Employment, Transportation & Warehousing Employment, Information Employment, Arts, Entertainment, & Recreation Employment, Finance & Insurance Employment, Real Estate, Rental & Leasing Employment, Professional & Technical Services Employment, Administrative & Waste Services Employment, Educational Services Employment, Health Care & Social Assistance Employment, Federal Civilian Government Employment, State & Local Government Employment, and Federal Military Government Employment

## Slide 24: Residential Growth Formulas

## Slide 25: Commercial and Industrial Growth formulas

## Slide 26: Final Demand Forecast
The Monthly Demand Forecast by year, month, rate schedule and CityGate was based upon:
  The calculated forecast for weather dependent load plus the most recent year’s (2015) non weather dependent core load with applied growth factors.
  Core load was forecasted by CityGate by rate schedule.

## Slide 27: Peak Day Forecast
3 Peak Day Scenarios:
  Average Peak Day
  Max Peak Day
  CityGate Peak Day
HDD weighting
  To determine the peak day HDDs Cascade had to weight each HDD based on weather location.
    Held customer count to the December 2015 actual and used the coefficient b in the linear regressions.
    The amount of demand at each weather location based on an increase in 1 HDD determined how each weather location should be weighted.

## Slide 28: Average Peak Day Forecast
The Average Peak Day Forecast ensures that Cascade can plan for the expected peak day during a year.
  Using the weighted HDDs, Cascade found the coldest day in each of the most recent 30 years (1986-2015).
  Using those HDDs, Cascade averaged each day for each weather location to come up with 7 HDDs.
  Those HDDs were then applied to the regressions to come up with an average peak day forecast.

## Slide 29: Max Peak Day Forecast
The Max Peak Day Forecast allows Cascade to plan for the coldest day in the past 30 years with today’s usage rates and customer counts.
  Using the weighted HDDs, Cascade found the coldest day from the past 30 years (This is December 21st, 1990).
  The HDDs for each weather location from this day were used in the regressions to come up with the Max Peak Day Forecast.

## Slide 30: CityGate Peak Day Forecast
The CityGate Peak Day Forecast allows Cascade to plan for the coldest day in the past 30 years at each individual weather location.
  Using weather location HDDs, Cascade found the coldest HDD in the past 30 years for each individual weather location.
  The HDDs for each weather location were used in the regressions to come up with the CityGate Peak Day Forecast.

## Slide 31: Max and CityGate Peak HDDs

## Slide 32: Average Peak Demand Day Forecast

## Slide 33: Max Peak Demand Day Forecast

## Slide 34: CityGate Peak Demand Day Forecast

## Slide 35: Total System

## Slide 36: Washington

## Slide 37: Oregon

## Slide 38: Total System Peak Day Comparison to previous IRP’s

## Slide 39: Washington Peak Day Comparison to previous IRP’s

## Slide 40: Oregon Peak Day Comparison to previous IRP’s

## Slide 41: Total System Tariff Breakout

## Slide 42: Washington Tariff Breakout

## Slide 43: Oregon Tariff Breakout

## Slide 44: Zone 10

## Slide 45: Zone 11

## Slide 46: Zone 20

## Slide 47: Zone 24

## Slide 48: Zone 26

## Slide 49: Zone 30-S

## Slide 50: Zone 30-W

## Slide 51: Zone GTN

## Slide 52: Zone ME-OR

## Slide 53: Zone ME-WA

## Slide 54: Sumas SPE Loop with Normal Weather

## Slide 55: Sumas SPE Loop with High and Low Weather Scenarios

## Slide 56: Tariff Breakout

## Slide 57: Sumas SPE Loop Peak Day

## Slide 58: Sedro-Woolley Loop With Average Weather

## Slide 59: Sedro-Woolley Loop with High and Low Weather Scenarios

## Slide 60: Tariff Breakout

## Slide 61: Sedro-Woolley Loop Peak Day

## Slide 62: Bremerton (Shelton) With Average Weather

## Slide 63: Bremerton (Shelton) with High and Low Weather Scenarios

## Slide 64: Tariff Breakout

## Slide 65: Bremerton (Shelton) Peak Day

## Slide 66: Wenatchee With Average Weather

## Slide 67: Wenatchee with High and Low Weather Scenarios

## Slide 68: Tariff Breakout

## Slide 69: Wenatchee Peak Day

## Slide 70: Yakima Loop with Normal Weather

## Slide 71: Yakima Loop with High and Low Weather Scenarios

## Slide 72: Tariff Breakout

## Slide 73: Yakima Loop Peak Day

## Slide 74: Average HDD by month for each Weather Station (30 year history)

## Slide 75: Cold Scenario HDD by month for each Weather Station (6 years out of 30 year history)

## Slide 76: Warm Scenario HDD by month for each Weather Station (6 years out of 30 year history)

## Slide 77: Summary

## Slide 78: Cascade Gas Supply Overview Current Resources

## Slide 80: System Overview

## Slide 81: Transport

## Slide 82
EXAMPLE OF POSSIBLE CNGC WINTER TRANSPORT CAPACITY FLOW

## Slide 83
NWP Transport
CONTRACT |  |  | Jan-16 | Feb-16 | Mar-16 | Apr-16 | May-16 | Jun-16 | Jul-16 | Aug-16 | Sep-16 | Oct-16 | Nov-16 | Dec-16
DESCRIPTION | RECEIPT | DELIVERY | 31 | 29 | 31 | 30 | 31 | 30 | 31 | 31 | 30 | 31 | 30 | 31
NWP |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Contract #100002 | all rec | all del | 205123 | 205123 | 205123 | 205123 | 205123 | 205123 | 205123 | 205123 | 205123 | 205123 | 205123 | 205123
Contract #135384 | jackson prairie | bremerton/mt vernon | 30420 | 30420 | 30420 | 30420 | 30420 | 30420 | 30420 | 30420 | 30420 | 30420 | 30420 | 30420
Contract #135558 | sumas | stanfield/portland west | 25400 | 25400 | 25400 | 25400 | 25400 | 25400 | 25400 | 25400 | 25400 | 25400 | 25400 | 25400
Contract #139382 | sumas | sedro wooley | 6191 | 6191 | 6191 | 6191 | 6191 | 6191 | 6191 | 6191 | 6191 | 6191 | 6191 | 6191
Contract #139383 | sumas | sedro wooley | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050 | 1050
Contract #139384 | sumas | sedro wooley | 3259 | 3259 | 3259 | 3259 | 3259 | 3259 | 3259 | 3259 | 3259 | 3259 | 3259 | 3259
Contract #100134 | sumas/ignacio | burbank/yakima/aberdeen | 330 | 330 | 330 | 330 | 330 | 330 | 330 | 330 | 330 | 330 | 330 | 330
Contract #100149 | sumas/ignacio | walla walla | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75
Contract #100150 | sumas/ignacio | menan starch | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160
Contract #100064 | sumas | hermiston/pasco | 1078 | 1078 | 1078 | 1078 | 1078 | 1078 | 1078 | 1078 | 1078 | 1078 | 1078 | 1078
Contract #132329 | sumas | kern river | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000
Contract #139090 | sumas | plymouth/umatilla/bellingham | 27063 | 27063 | 27063 | 27063 | 27063 | 27063 | 27063 | 27063 | 27063 | 27063 | 27063 | 27063
Contract #139637 | sumas | hermiston/oak harbor/selah | 7241 | 7241 | 7241 | 7241 | 7241 | 7241 | 7241 | 7241 | 7241 | 7241 | 7241 | 7241
Contract #139630 | stanfield | durkee/pendelton/mission | 7,450 | 7,450 | 7,450 | 7,450 | 7,450 | 7,450 | 7,450 | 7,450 | 7,450 | 7,450 | 7,450 | 7,450
Contract #140047 | sumas | bellingham/ferndale | 15,000 | 15,000 | 15,000 | 15,000 | 15,000 | 15,000 | 15,000 | 15,000 | 15,000 | 15,000 | 15,000 | 15,000
Contract #140748 | Opal | Portland West/Scappoose | 1,000 | 1,000 | 1,000 | 1,000 | 1,000 | 1,000 | 1,000 | 1,000 | 1,000 | 1,000 | 1,000 | 1,000
 |  |  | 335,840 | 335,840 | 335,840 | 335,840 | 335,840 | 335,840 | 335,840 | 335,840 | 335,840 | 335,840 | 335,840 | 335,840

## Slide 84
GTN Transport
CONTRACT |  |  | Jan-16 | Feb-16 | Mar-16 | Apr-16 | May-16 | Jun-16 | Jul-16 | Aug-16 | Sep-16 | Oct-16 | Nov-16 | Dec-16
DESCRIPTION | RECEIPT | DELIVERY | 31 | 29 | 31 | 30 | 31 | 30 | 31 | 31 | 30 | 31 | 30 | 31
GTN |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#17037 | kingsgate | malin | 23,980 | 23,980 | 23,980 | 23,980 |  |  |  |  |  |  | 23,980 | 23,980
#17019 | kingsgate | Spokane NPC | 11,558 | 11,558 | 11,558 | 11,558 | 11,558 | 11,558 | 11,558 | 11,558 | 11,558 | 11,558 | 11,558 | 11,558
#17021 | kingsgate | Kosmos Farm | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200
#17022 | kingsgate | Stanfield City | 232 | 232 | 232 | 232 | 232 | 232 | 232 | 232 | 232 | 232 | 232 | 232
#17023 | kingsgate | Madras | 2,078 | 2,078 | 2,078 | 2,078 | 2,078 | 2,078 | 2,078 | 2,078 | 2,078 | 2,078 | 2,078 | 2,078
#17025 | kingsgate | Prineville | 2,984 | 2,984 | 2,984 | 2,984 | 2,984 | 2,984 | 2,984 | 2,984 | 2,984 | 2,984 | 2,984 | 2,984
#17026 | kingsgate | Redmond | 2,734 | 2,734 | 2,734 | 2,734 | 2,734 | 2,734 | 2,734 | 2,734 | 2,734 | 2,734 | 2,734 | 2,734
#17028 | kingsgate | Bend | 8,927 | 8,927 | 8,927 | 8,927 | 8,927 | 8,927 | 8,927 | 8,927 | 8,927 | 8,927 | 8,927 | 8,927
#17031 | kingsgate | Stearns | 2,189 | 2,189 | 2,189 | 2,189 | 2,189 | 2,189 | 2,189 | 2,189 | 2,189 | 2,189 | 2,189 | 2,189
#17033 | kingsgate | LaPine | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45
#17034 | kingsgate | Gilchrist | 313 | 313 | 313 | 313 | 313 | 313 | 313 | 313 | 313 | 313 | 313 | 313
#17036 | kingsgate | Chemult | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75
#17023 | kingsgate | Madras | 331 | 331 | 331 |  |  |  |  |  |  |  | 331 | 331
#17025 | kingsgate | Prineville | 827 | 827 | 827 |  |  |  |  |  |  |  | 827 | 827
#17026 | kingsgate | Redmond | 662 | 662 | 662 |  |  |  |  |  |  |  | 662 | 662
#17028 | kingsgate | Bend | 4,137 | 4,137 | 4,137 |  |  |  |  |  |  |  | 4,137 | 4,137
#17031 | kingsgate | Stearns | 1,241 | 1,241 | 1,241 |  |  |  |  |  |  |  | 1,241 | 1,241
#17034 | kingsgate | Gilchrist | 248 | 248 | 248 |  |  |  |  |  |  |  | 248 | 248
#13687 | turqouise flats | stanfield | 10,000 | 10,000 | 10,000 | 10,000 | 10,000 | 10,000 | 10,000 | 10,000 | 10,000 | 10,000 | 10,000 | 10,000
#13688 | turqouise flats | stanfield | 5,000 | 5,000 | 5,000 | 5,000 | 5,000 | 5,000 | 5,000 | 5,000 | 5,000 | 5,000 | 5,000 | 5,000
 |  |  | 77,761 | 77,761 | 77,761 | 70,315 | 46,335 | 46,335 | 46,335 | 46,335 | 46,335 | 46,335 | 77,761 | 77,761

## Slide 85
Other Transport
CONTRACT |  |  | Jan-16 | Feb-16 | Mar-16 | Apr-16 | May-16 | Jun-16 | Jul-16 | Aug-16 | Sep-16 | Oct-16 | Nov-16 | Dec-16
DESCRIPTION | RECEIPT | DELIVERY | 31 | 29 | 31 | 30 | 31 | 30 | 31 | 31 | 30 | 31 | 30 | 31
FOOTHILLS |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(CNG FS-2) | AB/C border | kingsgate | 3,126 | 3,126 | 3,126 | 3,126 | 3,126 | 3,126 | 3,126 | 3,126 | 3,126 | 3,126 | 3,126 | 3,126
(CNG FS-3) | AB/C border | kingsgate | 21,583 | 21,583 | 21,583 | 21,583 | 21,583 | 21,583 | 21,583 | 21,583 | 21,583 | 21,583 | 21,583 | 21,583
(CNG FS-1) | AB/C border | kingsgate | 7,602 | 7,602 | 7,602 |  |  |  |  |  |  |  | 7,602 | 7,602
 |  |  | 32,311 | 32,311 | 32,311 | 24,709 | 24,709 | 24,709 | 24,709 | 24,709 | 24,709 | 24,709 | 32,311 | 32,311
NOVA |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(NOVA) (#2003039348-1) | NIT | AB/C border | 21,973 | 21,973 | 21,973 | 21,973 | 21,973 | 21,973 | 21,973 | 21,973 | 21,973 | 21,973 | 21,973 | 21,973
SPECTRA |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(#FI-2583-B-00) | station 2 | huntingdon | 20,000 | 20,000 | 20,000 | 20,000 | 20,000 | 20,000 | 20,000 | 20,000 | 20,000 | 20,000 | 20,000 | 20,000
RUBY PIPELINE LLC |  |  |  |  |  |  |  |  |  |  |  |  |  | 
#61036000B | pearl creek | turqouise flats | 15,000 | 15,000 | 15,000 | 15,000 |  |  |  |  |  |  | 15,000 | 15,000

## Slide 86
Chart: Transport Summary
| AECO | KINGSGATE | STA 2 | NWP SUMAS/HUNT | NWP N OF GREEN | NWP S OF GREEN
 | 21973 | 46428 | 1000 | 137957 | 27292 | 36824

## Slide 87: Impact of Constraints, OFO’s and Entitlements
Tools used by the pipeline to ensure appropriate pressure , flow and deliveries.
NWP will use line pressure and storage volumes to balance deliveries with receipts of gas.
Entitlement Examples
  If pressures sag and deliveries are low- Entitlement may be called. (NWP Storage Level is Critical)
  Entitlement places penalties on shipper to stay within a tolerance.
  Same scenario can apply in reverse- pressure too high
  Places Penalties on Shippers for non-compliance
OFO Examples
  Pricing may be low in the Rockies.
  Shippers modify behavior to take advantage of pricing.
  This cause a displacement of more flows from South to North
  Constraints come into Play- ie.Kemmerer
  NWP may issue OFO from Sumas south to alleviate shortfall in the north.
NWP may use Proposed Entitlements or OFO’s as warnings.
  NWP will use their own resources first.
  Notices may be issued to attempt shipper to modify behavior
  OFO and Entitlements used as last resort.

## Slide 88: Asset Management Agreement
Tenaska Marketing Ventures-
  Transport and Supply Released to Tenaska in exchange for annual payment made to CNG
  Provide Scheduling Services
  Market Analysis as needed
  Can help to Isolate CNG from Cuts and potential Pipeline Operational issues.
  Tenaska is very familiar with our assets – extracting maximum value from our assets. Competitive pricing for AMA compared to others.
  Privately help company that assumes more risk that CNG can tolerate.
  Expertise that Cascade doesn’t currently poses.

## Slide 89: Storage Resources
Jackson Prairie-
  4 account with 1,235,593 Dth Capacity
  We were approximately 90% Cycled over the past winter season
  CNGC remains committed to cycling or Jackson Prairie
Plymouth-
  2 accounts with 662,200 Dth Capacity
  New account of 100,000 Dth added for the upcoming season
  In addition to above we acquired TF-2 (Firm Redelivery Transportation) of 10,675
  Plymouth returned to fully functional operation for 04/01/2016.
  CNGC remains committed to using Plymouth as a peaking resource.

## Slide 90: Supply

## Slide 91: HIGHLIGHTS FOR THE 2016 PORTFOLIO DESIGN
PORTFOLIO PROCURMENT DESIGN BASED ON A DECLINING PERCENTAGE EACH YEAR, ACCORDINGLY: Approximately Year 1: 80% of annual requirements; Year 2: 40%, Year 3: 20%.
  80% allows more flexibility operationally
  Allows us to be in the market monthly through FOM purchase or Day Gas purchases
GSOC would consider a modification from a three year rolling portfolio if: 1) reasonable concerns exist regarding the availability of supply in a particular basin; 2) the outer year 3 year forward price is 20% higher/lower than the front month over a reasonably sustained period.
Hedged Percentages (fixed-price physical) Currently max 40% of annual requirements. Second year should be set at 25%, and 20% hedged volumes for year three.
GSOC would consider a modification of this plan if the outer year 3 year forward price is 20% higher/lower than the front month over a reasonably sustained period.
Annual load expectation (Nov-Oct) is approximately 30,000,000 dths, consistent with recent load history.
GSOC has requested a review of possible 5 year deal at AECO. Gas Supply currently analyzing scenarios.

## Slide 92
Chart: TOTAL RFP's
| Nov16-Oct17 | Nov17-Oct18 | Nov18-Oct19 | TOTALS
NWP SUMAS/HUNT | 6380000 | 2656000 | 1509000 | 10545000
NWP N OF GREEN | 2860000 | 830000 | 720000 | 4410000
NWP S OF GREEN | 592000 | 457000 | 0 | 1049000
AECO | 1507500 | 2130000 | 905000 | 4542500
KINGSGATE | 1820000 | 155000 | 460000 | 2435000
STA 2 | 0 | 365000 | 0 | 365000

## Slide 93
Chart: INDEX RFP's
| Nov16-Oct17 | Nov17-Oct18 | Nov18-Oct19 | TOTALS
NWP SUMAS/HUNT | 4405000 | 2056000 | 604000 | 7065000
NWP N OF GREEN | 2860000 | 605000 | 720000 | 4185000
NWP S OF GREEN | 592000 | 457000 | 0 | 1049000
AECO | 305000 | 1375000 | 905000 | 2585000
KINGSGATE | 1820000 | 155000 | 460000 | 2435000
STA 2 | 0 | 365000 | 0 | 365000
INDEX RFP's | 1

## Slide 94
Chart: FIXED RFP's
| Nov16-Oct17 | Nov17-Oct18 | Nov18-Oct19 | TOTALS
NWP SUMAS/HUNT | 1975000 | 600000 | 905000 | 3480000
NWP N OF GREEN | 0 | 225000 | 0 | 225000
NWP S OF GREEN | 0 | 0 | 0 | 0
AECO | 1202500 | 755000 | 0 | 1957500
KINGSGATE | 0 | 0 | 0 | 0
STA 2 | 0 | 0 | 0 | 0

## Slide 95
Chart: RFP Percentage by Month
| Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
Year 1 Percentage | 0 | 0 | 0 | 0.25286 | 0.19758 | 0.23519 | 0.14225 | 0.17212
3 yr Total | 0 | 0 | 0 | 6427500 | 6370000 | 5650000 | 2329000 | 2570000

## Slide 96
Chart: Percentage by Basin Currently Contracted
| AECO | KINGSGATE | STA 2 | NWP SUMAS/HUNT | NWP N OF GREEN | NWP S OF GREEN
 | 4555000 | 0 | 365000 | 6467500 | 1695500 | 180000

## Slide 97
Chart: Percentage by Basin 2016 RFP + Current Supply
| AECO | KINGSGATE | STA 2 | NWP SUMAS/HUNT | NWP N OF GREEN | NWP S OF GREEN
 | 9097500 | 2435000 | 730000 | 17012500 | 6105500 | 1229000

## Slide 98
Chart: 
| November | December | January | Febuary | March
Current Supply | 41000 | 56000 | 56000 | 48000 | 41000
RFP Supply | 55000 | 75000 | 80000 | 62500 | 37500
Storage | 4233.1771 | 4908.9842 | 5222.0433 | 4815.6937 | 3189.157
Spot | 14603.0587 | 6688.2271 | 8493.299 | 231.9204 | 9336.9305

## Slide 99
Chart: 
Current Supply | 56000
RFP Supply | 80000
FOM Spot Gas | 10000
SGS Storage | 56366
Daily Spot Gas | 10000
Peaking Deal | 20000
3rd Party Citygate | 10000
Pipeline Pack | 8156.07
LS Storage | 78125

## Slide 100: Cascade Gas Supply Overview Alternative Resources

## Slide 101: Proposed Natural Gas Infrastructure Projects (source: Northwest Gas Association draft 2016 Outlook)

## Slide 102: Washington Expansion Project
In response to a request for an incremental 750 million cubic feet per day (MMcf/d) of capacity, Williams Northwest Pipeline (NWP) is planning to construct the Washington Expansion Project.
140 miles of 36-inch diameter loop to be constructed in 10 different segments in or near NWP’s existing right-of-way along the I-5 corridor between Sumas and Woodland, WA, plus additional compression at five existing compressor stations.
In conjunction with this project, NWP is also proposing an incremental scalable expansion from Sumas to markets in the I-5 corridor as far south as Molalla, OR.
This phase of the project is not contingent upon the aforementioned expansion and could go in service fall of 2018.
Opportunity to potentially address any shortfalls along the I-5 corridor

## Slide 103: Northwest Market Access Expansion (NWP N-MAX)/Trail West (aka Palomar)
NWP is working with NW Natural and TransCanada GTN
In conjunction with an expansion of the existing NWP system. The project would consist of a 106-mile, 30-inch diameter pipeline that would run from GTN’s mainline in central Oregon to a NW Natural/NWP hub near Molalla — enhancing delivery capacity to the I-5 Corridor.
Project’s initial design capacity is 300 MMcf/d, expandable to 750 MMcf/d. It would be linked to the N-MAX project on the NWP system to deliver gas to other markets along the I-5 corridor.
Potential to make additional supplies available to Central Oregon
Potential to move supplies to I-5 corridor

## Slide 104: Spectra T-South Expansions
Spectra Energy continues to evaluate expansion of its T-South system to provide incremental delivery options for growing Western Canada gas supply to markets in the Pacific Northwest.
All expansions on T-South would require pipeline looping and compression and can be brought into service between 2018-2020.
T-South expansion options include the following from Station 2:
  to Sumas delivering gas to the BC Lower Mainland and Northwest Markets
  to Kingsvale delivering up to 450 MMcf/day gas to Fortis Energy’s Southern Crossing system;
  to Summit Lake delivering gas to PNG’s pipeline system

## Slide 105: FortisBC Kingsvale–Oliver Reinforcement Project (KORP)
Expanding Fortis Energy’s existing bi-directional Southern Crossing system (connecting Spectra’s T-South system at Kingsvale, BC, to TransCanada’s system at Yahk, BC)
Would facilitate access to an additional 300-400 MMcf/d of AECO priced gas supply for westbound delivery to markets in the Lower Mainland of BC and the I-5 corridor where several new large industrial projects are proposed.
The expansion of the Southern Crossing system will require a 100-mile pipeline-looping project on the Kingsvale to Oliver, BC, segment, as well as an expansion of Spectra’s T-South system from Kingsvale to Huntingdon to meet the incremental flow.

## Slide 106: Pacific Connector Gas Pipeline Project (PCGP)
The Pacific Connector Gas Pipeline Project (PCGP) is a 232-mile 36-inch diameter pipeline extending from Malin to Coos Bay, OR.
Williams and Veresen, Inc. are proposing PCGP to serve the Jordan Cove LNG export terminal, as well as potential regional markets between Malin and Coos Bay.
PCGP includes 41,000 horsepower of compression to be installed near Malin yielding a total project design capacity of 1.06 Bcf/d.
PCGP will provide access to supplies from Western Canada and the U.S. Rockies via interconnections with Gas Transmission Northwest and the Ruby Pipeline.
This could be a potential source of additional supplies for the distribution system

## Slide 107: Regional Storage

## Slide 108: AECO Hub Storage
The AECO Hub™, Niska’s commercial natural gas storage business in Alberta, Canada, is comprised of two gas storage facilities:
  Suffield (South-eastern Alberta)
  Countess (South-central Alberta)
Although the two AECO facilities are geographically separated across Alberta, the toll design of the NOVA (NGTL) system means that they are both, commercially, at the same point.
Total gas storage and deliverability capacity of the AECO Hub™:
  Working Gas Capacity 154 BCF
  Peak Withdrawal Rate 3.05 BCF per day
  Peak Injection Rate 2.75 BCF per day
Capacity at one of the facilities are possibilities as alternative resources. Currently, there is no open season planned. However, some services are available for limited periods of time. Incremental transport involving Nova, Foothills, GTN and possibly NWP would be necessary.

## Slide 109: Wild Goose Storage
Wild Goose is located north of Sacramento in northern California and was the first independent storage facility built in the state. The facility commenced full commercial operations in April 1999 and in April 2004 completed its first expansion. Customers have direct access to Pacific Gas and Electric’s (PG&E) backbone system.
Total gas storage and deliverability capacity at Wild Goose currently is as follows:
Working Gas Capacity: 75.0 Bcf
Peak Withdrawal Rate 950 mmcf/d
Peak Injection Rate 525 mmcf/d
Key Features
Citygate pricing, liquidity, arbitrage opportunities;
the ability to manage OFO/EFO’s on the PG&E system; and
supply reliability

## Slide 110: Gill Ranch Storage
Gill Ranch Storage is an underground intra-state natural gas storage facility near Fresno, Calif. It includes a pipeline that links the facility to Pacific Gas & Electric Company's (PG&E) mainline transmission system, allowing it to serve customers throughout California.
GRS has the capacity to ultimately provide approximately 20 billion cubic feet (Bcf) of underground natural gas storage.
The facility is located about 25 miles west of Fresno and includes an approximately 27-mile, 30-inch pipeline, which is connected to the PG&E Line 401 north of Panoche, Calif.
The premium storage location offers a unique opportunity to access five interconnects.
The site was developed in a joint agreement by Gill Ranch Storage, LLC, a subsidiary of NW Natural, and PG&E.
The site has potential for future expansion.

## Slide 111: Mist
NW Natural Gas Company, the owner and operator of the Mist underground storage facility near Portland, Ore., is investigating a potential expansion project to be completed in 2016-2017.
We are modeling the assessing the cost-effectiveness of leasing storage capacity beginning November 2018, once Mist is built.
This would also require expansion of NWP’s interstate along the I-5 corridor and possibly across the Columbia Gorge. We may be able to acquire discounted winter only capacity from a third party from Mist to our citygates if NWP their system from Sumas to Portland (NWP I-5 expansion)

## Slide 112: Clay Basin
Questar Pipeline owns and operates the Clay Basin storage facility in Daggett County, Utah. This reservoir stores gas during the summer for withdrawal in the winter.
Earlier this year Shell Energy offered to temporarily or permanently assign to CNGC their Clay Basin capacity prior to notice period.
QPC stated they would accept a 1 year extension vs. the 3yr previously discussed, and CNGC would obtain annual renewal rights thereafter.
Clay Basin would require incremental capacity from Overthrust Pipeline. Ruby was willing to consider allowing Cascade to re-align portions of our seasonal Ruby capacity to move gas during the heating season.
We elected to pass on the opportunity at the time. First, we still have long-term concerns regarding Kemmerer constraints to address on NWP. Most importantly, we didn’t know if we could make the case for Washington to absorb the bulk of Clay Basin’s expense; OPUC would still ask why is Washington getting yet more storage when Oregon is still lacking a significant storage resource.
We will consider Clay Basin again with the 2016 IRP.

## Slide 113: Ryckman Creek Storage
Ryckman Creek Resources, LLC, a wholly-owned subsidiary of Peregrine Midstream Partners, LLC
Ryckman Creek is located in Uinta County, Wyoming, near the Opal Hub.
Ryckman Creek has converted a partially depleted oil and gas reservoir into a gas storage facility with 35 BCF of working gas and a maximum daily withdrawal rate of 480,000 Dths/d.
Ryckman Creek Gas Storage Facility is located near the town of Evanston, Wyoming and approximately twenty-five miles southwest of the Opal Hub.
Ryckman Creek currently has interconnects with Questar Gas Pipeline, Kern River Transmission, Questar Overthrust Pipeline, Ruby Pipeline and Northwest Pipeline.
Previously conducted a non- binding Open Season to determine the interest of prospective customers in contracting for up to 8 BCF of firm working gas storage capacity beginning April 1, 2013.
Ryckman still has a bit of proving to do regarding reliability since the NRU fire a few years ago; the facility is up and running. Ryckman Creek began commercial operations in August 2012. The facility currently has approximately 25 Bcf under contracts of varying lengths (longest belonging to Anadarko through March 2023). A lengthy force majeure at Ryckman was lifted in January 2016.
Still, even with the combination of plunging gas prices, bankruptcy and a fire the facility is still open. Ryckman is currently flowing about 60-70,000 dths day to Ruby.

## Slide 114: Conclusions about the proposals
Historically, our incremental storage focus has been directed at providing Oregon with a larger storage resource other than the 10% of JP/LS they currently have.
All the alternatives except Ryckman require incremental GTN capacity.
Ryckman storage would utilize our 15,000 dths/day of winter only capacity that would be used for both storage activities and regular nomination activities.
The two California storage alternatives would also require California Gas Transmission capacity to Malin. The demand charge is huge - $1.68 p/dth
  Ruby still is an option for the California storage, but due to rate stacking Ruby would be at a lower contracted level, primarily for the purposes of injecting Rockies gas and to provide supply diversity in the storage facility.
Ryckman Creek appears to be the least expensive and most flexible option; however, Ryckman’s on-going operational difficulties are a concern.
All storage alternatives will be modeled for the 2016 IRP. Resource Planning will provide an update on modeling results at a GSOC meeting later this summer

## Slide 115: Major resource issues on the horizon
Addition alternatives to be considered during IRP process
  NWP I-5 Expansion
  Realignment of MDDOs to citygates
  Palomar/Cross Cascades
  Pacific Connector
  Incremental Nova
  Incremental Foothills
  Incremental GTN (north to south)
  Biofuel
  Satellite LNG
  Mist Storage
  AECO Storage
  Wild Goose Storage
  Gill Ranch Storage
  Ryckman Creek Storage
Began discussions with Niska Partners to gather information to model AECO Hub Storage in the 2016 IRP. In addition, we will be considering Wild Goose, Gill Ranch, Mist and Ryckman Creek storage
Working with GTN to develop a narrative to explain how our long path capacity can be used to meet peak day shortfalls.

## Slide 116: NEXT STEPS?

## Slide 117: Cascade Natural Gas Corporation Integrated Resource Plan Technical Advisory Group Meeting #2
Tuesday, July 19, 2016
Seattle-Tacoma International Airport Conference Center