## Slide 1: Cascade Natural Gas Corporation Integrated Resource Plan Technical Advisory Group Meeting #5
Friday, October 14th 2016
CNGC Headquarters
Via WebEx

## Slide 2: AGENDA
Safety and housekeeping items
Introductions
Model Selection and Explanation of Resources Taken
Monte Carlo Discussion
Results
Action Plan
2016 IRP Timeline
Adjournment

## Slide 3: Current Resources
Our current resources models our system over a 20 year period which includes:
  Current Supply Sources.
  Current Storage.
  Current Transport – Note: for modeling purposes we assume all existing transportation contracts will be renewed if they expire over the 20 year time horizon.
This run allows the company to see what the model does without the alternative resources attached. It sets a bench mark to test the validity of the information (for instance comparing first year system cost to the most recent PGA).

## Slide 4: Types of Supply - Summary
Base – Can be listed as “Base” or “Fixed” this is an annual supply that we must take if we contract it.
Winter – This is another supply that we must take, but is only available during the winter season (November-March).
Day Gas – Can be broken down by winter and summer day gas. We only have to take what we need of this type of gas, and because it is more flexible, it is more expensive than Base or Winter gas.
Peak – Used to serve demand when all other options are exhausted. It is also the most expensive type of gas.

## Slide 6: Assumptions
Incremental Transport
Incremental Storage
All In
Expected Case

## Slide 7: Incremental Transport
Incremental Transport is tested next as it was our belief that this was the main shortfall.
All Incremental Transports began on Nov. 2017 Except:
  NWP East OR which begins Nov 2021.
  I-5 Expansion begins Nov 2020, with realignment of MDDOs to 30-W starting Nov 2017.
Anticipate rates will be negotiated, however we will provide incremental transport rates under confidential treatment.
Transport is only sized once over the simulation.

## Slide 10: Incremental Transport – An Example

## Slide 11: Incremental Storage
We model 4 different potential storage facilities to check for potential price opportunities, as well as to meet load.
All storages are modeled to begin in April 2018.
Anticipate rates will be negotiated, however we will provide incremental storage rates under confidential treatment.
Storage is only sized once over the simulation.

## Slide 13: All In Scenario
In addition to Incremental Transport and Storage, we include:
  Yakima satellite LNG Facility to serve additional unserved demand.
  Opal Incremental Supply to see if it would interact with storage.
This scenario serves as the foundation for us to see what resources are taken to meet system demand with the least cost mix of natural gas supply and conservation.1

## Slide 16: Expected Scenario
Re-Run the optimization removing the resources SENDOUT does not select in the All-In case.
  Allows us to confirm that removing these resources does not impact the amount of served demand.
  Removes fixed costs associated with the resources not taken to provide a true total system cost.

## Slide 18: Total System Costs ($000)

## Slide 19: Alternative Resources Selected
Transport:
  Incremental GTN – Allows us to continue to serve customers as we grow in Citygates that are fed by our GTN capacity, specifically around Bend, Oregon where we expect shortfalls.
  I-5 Expansion – Allows us to continue to serve customers as we grow around the I-5 corridor, specifically in the Sumas area.
  Wenatchee Expansion – Allows us to continue to serve customers as we grow in Central Washington.
  Spokane Expansion – Allows us to continue to serve customers as we grow in Eastern Washington.
  Incremental Starr Road – Allows us the flexibility to move gas off of GTN and onto NWP through Starr Road when needed, displacing potential incremental NWP capacity.
  Eastern Oregon Expansion – Allows us to move gas from NWP to serve Eastern Oregon.

## Slide 20: Alternative Resources Selected
Supply:
  Yakima Satellite LNG Plant – Allows us the opportunity to serve demand in a cost effective way directly to Yakima, WA without new transport, which in turn helps increase served demand system wide through a displacement of Maximum Daily Delivery Obligations (MDDOs) among existing contracts.

## Slide 21: Alternative Resources Not Selected
Transport
  Incremental NOVA/Foothills – There is currently no incremental NOVA capacity available. In addition, SENDOUT did not believe there was a cost effective opportunity presented by moving gas along these contracts to Kingsgate versus buying gas at Kingsgate directly.
  Incremental Ruby / Turquoise Flats – SENDOUT determined it was more cost effective to use incremental transport along GTN to serve the incremental demand these contracts would serve.
Storage
  Ryckman Creek, Gill Ranch, Wild Goose, AECO Hub – No incremental storage taken – None of the storage facilities modeled were cost effective, or led to an increase in served demand.

## Slide 22: Alternative Resources Not Selected
Supply
  Opal Incremental – Since SENDOUT determined it was best to serve increasing demand through a GTN Expansion, there was no need to purchase additional gas to move along Ruby.

## Slide 23: Monte Carlo Simulations
Monte Carlo – NYMEX price
Monte Carlo – Weather
Why not Monte Carlo on both together?
Results

## Slide 24: Monte Carlo – NYMEX Price
Using our 20 year price forecast as the mean value for the NYMEX market, we had SENDOUT run 200 simulations to stress test our expected case over a variety of different scenarios.
We also modeled how our expected case would fare with 5 difference assumptions: Low Growth, High Growth, a 10% Carbon Adder, a 20% Carbon Adder, and a 30% Carbon adder.
This ensures that our expected resource portfolio is still the optimal choice even in extreme pricing situations.

## Slide 27: Monte Carlo – Weather
Using historical weather, we had SENDOUT run 200 simulations to stress test our expected case over a variety of different scenarios.
We also modeled how our expected case would fare with 5 difference assumptions: Low Growth, High Growth, a 10% Carbon Adder, a 20% Carbon Adder, and a 30% Carbon adder.
This ensures that our expected resource portfolio is still the optimal choice even in extreme weather situations.

## Slide 28: Monte Carlo Weather – Normal Distribution

## Slide 29: Monte Carlo Weather – Normal Distribution
When following a normal distribution your data will follow the 68%, 95%, 99.7% rule like in the below diagram.

## Slide 30: Monte Carlo Weather – Normal Distribution
To build our monthly inputs for SENDOUT we analyze our 30 data samples for each weather location which are the monthly HDD totals for the years 1986-2015. After getting the Mean and standard deviation we can compute how many data samples fall within each range of standard deviations.

## Slide 34: Why not Monte Carlo Price AND Weather?
What happens when we look at drawing on both price and weather at the same time?
We can imagine a 3 dimensional histogram, instead of the 2 dimensional histograms on the previous pages. Filling this in takes many more draws.
200 draws of weather on the X axis and 200 draws of price on the Y axis might need 200 x 200 = 40,000 draws to fill in a histogram like this…

## Slide 35: Rmix Decision - Storage

## Slide 36: Rmix Decision - Transport

## Slide 40: Action Plan

## Slide 41: Action Plan – Cont.

## Slide 42: 2016 IRP Timeline

## Slide 43: NEXT STEPS?

## Slide 44: Cascade Natural Gas Corporation Integrated Resource Plan Technical Advisory Group Meeting #5
Friday, October 14th 2016
CNGC Headquarters
Via WebEx