## Slide 1: Cascade Natural Gas Corporation Integrated Resource Plan Technical Advisory Group Meeting #6
Thursday November 17th, 2016
CNGC Headquarters
Via WebEx

## Slide 2: AGENDA
Safety and housekeeping items
Introductions
What is SENDOUT?
History of Cascade’s use of SENDOUT
Current Methodology for SENDOUT
Simulation Examples
Results/Analysis – Plan to address shortfalls
Conclusion
Adjournment

## Slide 3: What is SENDOUT?
Cascade utilizes SENDOUT™ for resource optimization.
This model permits the Company to develop and analyze a variety of resource portfolios to help determine the type, size, and timing of resources best matched to forecast requirements.
SENDOUT™ is very powerful and complex. It operates by combining a series of existing and potential demand side and supply side resources and optimizes their utilization at the lowest net present cost over the entire planning period for a given demand forecast.

## Slide 4: What is SENDOUT? – Cont.
SENDOUT™ utilizes a linear programming approach.
The model knows the exact load and price for every day of the planning period based on the analyst’s input and can therefore minimize costs in a way that would not be possible in the real world.
Therefore, it is important to acknowledge that linear programming analysis provides helpful but not perfect information to guide decisions.

## Slide 5: SENDOUT CONFIGURATION CHANGES
2004 NWP AND GTN CENTERS
2006 NWP AND GTN CENTERS/STATE
2008 DISTRICT AND ZONAL
2010 DISTRICT AND ZONAL
2012 DISTRICT AND ZONAL
2014 LOAD CENTER/GATE STATION, ZONAL
2016 LOAD CENTER/GATE STATION, RATE SCHEDULE, ZONAL

## Slide 6: IRP HISTORY OF SOLVES (HIGH LEVEL)

## Slide 7
2008 IRP SENDOUT NETWORK DIAGRAM

## Slide 8
2010 IRP SENDOUT NETWORK DIAGRAM

## Slide 9
2014 IRP SENDOUT NETWORK DIAGRAM

## Slide 10
2016 IRP SENDOUT NETWORK DIAGRAM

## Slide 11: Current Methodology – Flow Chart

## Slide 12: Base Case Sendout Inputs
Supply
Storage
Transportation
Demand
Weather

## Slide 13: Supply
Cascade can purchase gas at 3 markets; AECO, SUMAS, and OPAL.
At each market Cascade can purchase gas at different locations along the pipeline.
For the first year, Cascade uses all current contracts for Supply inputs.
For years 2-20, Cascade uses Base, Fixed, Winter base, Summer and Winter day gas, and Peak day incremental supplies as inputs.
The contracts for years 2-20 are renewed in November and April.

## Slide 14: Supply

## Slide 15: Supply Base and Fixed
Supply Base and Fixed are the baseline supply contracts that are contracted every 12 months.
A base contract has a basis rate. This is defined as the price of gas at a given market (ie, AECO base is the expected cost of gas at NYMEX plus the basis for AECO, for a given month).
A fixed contract has a fixed rate.
A penalty is applied to each contract when the contracted amount of gas is not taken for a day. This type of penalty forces these types of contracts to take the optimal amount of gas to serve the base demand.

## Slide 16: Supply Example

## Slide 17: Base Supply cont’d

## Slide 18: Winter base Supply
Winter base supply is contracted supply with a premium charge that is slightly higher than base gas.
The Maximum Daily Quantity (MDQ) is optimally set by SENDOUT.
Winter supply is renewed every November and completes at the end of March.
Winter Supply is additional baseline supply on top of the base or fixed supplies for the winter months.
There is a penalty associated to this contract to force SENDOUT to take the optimal amount of additional winter base gas.

## Slide 19: Winter base Supply cont’d

## Slide 20: Day Supply (Winter)
Winter Day supply is gas that is R-mixed at the beginning of November each year.
The R-mix function takes into account the fixed and variable costs of a resource to determine the proper amount to take in a given period.
Winter day gas has a MDQ cap but is not a must take supply.
If a winter day supply has an MDQ of 10000 dth then it can take anywhere from 0 to 10000 dth’s of gas on any given day in the winter.
Winter day supply has a slightly higher premium than winter base supply and it can be contracted from November to April.

## Slide 21: Day Supply (Winter) cont’d

## Slide 22: Day Supply (Summer)
Summer day supply is gas that is R-mixed at the beginning of April each year.
Summer day gas has a MDQ cap but is not a must take supply.
If a summer day supply has an MDQ of 10000 dth then it can take anywhere from 0 to 10000 dth’s of gas on any given day in the summer.
Summer day supply has a slightly lower cost than base supply and it can be contracted from April to November.

## Slide 23: Day Supply (Summer)

## Slide 24: Peak Supply
Peak supply is gas purchased on high demand days where base, index, winter base, or day supply cannot accommodate.
Peak supply has a slightly higher premium to buy than day supply.
As long as Cascade has the transport capacity, we can purchase as much peak supply as needed to meet peak demand.

## Slide 25: Total Supply

## Slide 26: Storage
Cascade leases storage at 2 locations: Jackson Prairie (JP) and Plymouth.
Cascade has 4 storage contracts with JP and 2 contracts with Plymouth.
Storage injections targets are set at 35% by the end of June, 80% by the end of August, and 100% by the end of September.
These targets are set by our Gas Supply Oversight Committee.
Cascade can withdrawal approximately 56,000 dth’s per day from JP and 78,000 dth’s per day from Plymouth for a total of approximately 134,000 dth’s per day.

## Slide 27: Storage Example

## Slide 28: Storage Example 2

## Slide 29: Transportation
Transportation contracts are the means of how Cascade gets the gas from the supplier to the end user.
Cascade has multiple types of transportation:
  A single delivery point.
  Multiple delivery points.
The multiple delivery point contracts gives Cascade the flexibility to move the gas where it’s most needed.
On GTN, transportation goes to the Citygate level as MDDO’s cannot be reallocated within the GTN zone.
On NWP, transportation goes to the zone level because MDDO’s can be reallocated within a zone to the Citygate.

## Slide 30: Transportation cont’d
Transportation has an MDQ, a D1 rate, a transportation rate, and a fuel loss percentage.
A maximum delivery quantity (MDQ) which is the maximum amount of gas Cascade can move on the pipeline on a single day.
A D1 rate which is the reservation rate to have the ability to move the MDQ amount on the pipeline.
A transportation rate which is the rate per dekatherm that is actually moved on the pipeline.
The fuel loss percentage is the statutory percent of gas based on the tariff from the pipeline that is lost and unaccounted for from the point of where the gas was purchased to the Citygate.

## Slide 31: Transport Example

## Slide 32: Transport Example

## Slide 33: Delivery Rights vs Receipt Rights
Cascade has more Delivery Rights than Receipt Rights.
Approximately 457,000 Dth of Delivery Rights.
Approximately 360,000 Dth of Receipt Rights.
The excess Delivery Rights allow Cascade to be flexible with the 360,000 Dth of Receipt gas.

## Slide 34: Example of delivery right flexibility
All of the following must be true

## Slide 35: Example of delivery right inflexibility
2.5 MDTs
1 MDT
0.5 MDTs

## Slide 36: Location of Zones

## Slide 37: Zone 26 on Peak Day for Transport 135558

## Slide 38: Zone 30-S on Peak Day for Transport 135558

## Slide 39: Zone 30-W on Peak Day for Transport 135558

## Slide 40: Transport Contract 135558 on Peak Day

## Slide 41: Example of delivery right flexibility

## Slide 42: Demand Behind the Gate
Cascade has strived over the last several years to make the IRP forecast and resource analysis to get to as granular a level as possible using the available data.
Attempts to forecast demand behind the gate using existing forecasting methodology has been challenging.
Customer billing data does not have daily meter reads for core customers making regression analysis on a use per HDD per customer difficult.
Given Cascade is not a contiguous system, DSM by gate is currently is an ongoing complication
  This year we have added the Climate Zone
  Future IRPs will try and address the gate station level
Some towns can be served by multiple pipelines and the mix can change over time.
As part of the rate case settlement, Cascade is committed to performing a robust citygate study.

## Slide 43: Demand
Demand is forecasted at the Citygate level by rate schedule.
For NWP, each Citygate’s demand is associated with the zone.
For GTN, each Citygate’s demand is associated with it’s respective Citygate interconnect.
Demand Inputs
  Forecast type (Monthly amount or Regressions)
  Monthly projected customers for 20 years.
  Regression coefficients if using the Regression forecast type.
  If using a monthly number, it is the 2015 demand for that month with a growth factor.

## Slide 44: Demand Example

## Slide 45: Demand Example 2

## Slide 46: Weather
Weather inputs for SENDOUT include:
  Monte Carlo
  Historical
  Normal
Monte Carlo inputs include mean, standard deviation, max and minimum.
Historical data is used to build weather profiles for Monte Carlo.
Normal weather is the daily average of the 30-year most recent history (1986-2015).

## Slide 47: Weather Example – Monte Carlo

## Slide 48: Current Methodology – Flow Chart

## Slide 49: Results/Analysis – As Is
As Is Case: Using currently available Supplies, Transportation, and DSM, this scenario informs us where we expect deficiencies.
For modeling purposes, we assume all contracts run through the 20 year planning horizon.
Goal is to find the optimal mix of incremental supply, storage, transportation and other resources to “solve” for the best way to eliminate deficiencies at the lowest reasonable cost.
While Cascade aims to serve the demand of all of its customers, we take the approach that we will not pick up incremental transportation if the sole purpose of it is to serve customers on an interruptible tariff.
The mix of existing and incremental resources that SENDOUT selects as the optimal solve for our deficiencies is defined as our expected scenario.

## Slide 50: Results/Analysis – As Is
Load Centers with Potential Peak Day Unserved Demand in dekatherms– As Is Scenario

## Slide 51: Results/Analysis – Incremental Resources -
Incremental Transportation & Supply Acquired, in dekatherms

## Slide 52: Results/Analysis – Incremental Resources Selected
Transport
3rd Party Citygate Deliveries – Allows Cascade to purchase delivered natural gas from a 3rd party. 6,144 dth/day.
Incremental GTN – Allows Cascade to continue to serve customers as the Company’s core load grows in citygates that are fed by GTN capacity, specifically around Bend, Oregon where the Company expects shortfalls. 32,285 dth/day.
I-5 Expansion – Allows Cascade to continue to serve customers as the Company’s core load grows around the I-5 corridor, specifically in the Sedro-Woolley area. 10,000 dth/day.
Wenatchee Expansion – Allows Cascade to continue to serve customers as the Company’s core load grows in Central Washington in areas such as Wenatchee and Yakima. 7,310 dth/day.
Zone 20 Expansion – Allows Cascade to continue to serve customers as the Company’s core load grows in Eastern Washington in areas such as Kennewick. 6,560 dth/day.
Incremental Starr Road – Allows Cascade the flexibility to move gas off of GTN and onto NWP through Starr Road when needed, displacing the need for potential incremental NWP capacity. 9,326 dth/day.
Eastern Oregon Expansion – Allows Cascade to move gas from NWP to serve Eastern Oregon in areas such as Nyssa-Ontario. 3,950 dth/day.

## Slide 53: Results/Analysis – Incremental Resources Selected
Supply
Yakima Satellite LNG Plant – Allows Cascade the opportunity to serve demand in a cost effective way directly to Yakima, WA without new transport, which in turn helps increase served demand system wide through a displacement of Maximum Daily Delivery Obligations (MDDOs) among existing contracts. 5,000 dth/day.

## Slide 54: Results/Analysis – Impact of Additional Transport/supply

## Slide 55: Conclusion – Expected Scenario
Load Centers with Potential Peak Day Unserved Demand in dekatherms – Expected Scenario

## Slide 56: Conclusion
Cascade has identified potential deficiencies starting in 2017
From 2017-2020, Cascade uses 3rd Party Citygate deliveries to solve this shortfall
From 2020 through the end of the planning horizon, Cascade uses a mix of incremental Transportation and Supply to solve the deficiency
With the resource mix that is designated the “Expected Scenario” Cascade projects that there will only be a slight deficiency in 2036, all of which is from customers on an interruptible tariff.

## Slide 57: NEXT STEPS?

## Slide 58: Cascade Natural Gas Corporation Integrated Resource Plan Technical Advisory Group Meeting #6
Thursday November 17th, 2016
CNGC Headquarters
Via WebEx