## Slide 1: Demand Response Potential And Target Setting Workshop
June 8, 2020

## Slide 2: Current Clean Energy Rulemaking Overview
Upcoming Dates
June 10 - Markets Stakeholder Workgroup
June 16 - Joint UTC/Commerce incremental cost of compliance workshop
June 29 - Comments due on PoE rules
July 6 - Comments due on EIA rules
July 28 - EIA Adoption Hearing
Ongoing UTC Dockets
UE-190652
  Energy Independence Act (EIA)
UE-190698
  Integrated Resource Plan (IRP)
UE-190837
  Purchases of Electricity (PoE)
UE-191023
  Clean Energy Transformation Act (CETA)

## Slide 3: Workshop Goals
Integrated Resource Plan
UE-190698
Determine if guidance is needed for new requirement to:
Identify the potential cost-effective demand response and load management programs that may be acquired.
Clean Energy Implementation Plan
UE-191023
Determine if guidance is needed for new requirement to:
Propose specific targets that pursue all cost-effective, reliable, and feasible demand response.

## Slide 4: Today’s Agenda
1:30 Welcome and introduction
1:40 Potential for Load Flexibility – The Brattle Group
2:55 Ten minute break*
3:05 DR insights for the northwest – Pacific Northwest National Laboratory
4:00 Facilitated discussion on DR potential and CEIP targets
4:45 Next steps
* Additional 5 min bio breaks will be announced verbally

## Slide 5: Virtual Workshop Instructions
Do:
Try to participate using your computer.
Mute your mics and turn off your video camera.
Use Skype chatbox.
Wait to be called on to speak.
Respect the pause.
Ask clarifying questions during the presentation.
Don’t:
Hesitate to “raise your hand” or ask a question!
Speak over the presenter or a speaker who is voicing a question or thought.
Forget this is a public workshop. The presentation and comments will be recorded and posted.

## Slide 6: The Skype chat box
Look for this icon on your Skype window to open the meeting chat box.
Type “Raise hand” or type out question in chat box to ask questions during presentations.
“Raise hand” for discussion after the presentations.

## Slide 7: The Potential for Load Flexibility
PREPARED BY
  Ryan Hledik
  Ahmad Faruqui
    Washington UTC Demand Response Potential and Target Setting Technical Workshop
    June 8, 2019

## Slide 8: You can’t spell “DER” without “DR”
DR is the largest distributed energy resource (DER) in the U.S.
Total U.S. Installed Capacity (GW)
Notes:
EV charging demand assumes 6 kW charging demand per EV, does not account for coincidence of charging patterns. Rooftop solar PV estimate is installed capacity, does not account for derated availability during peak. Existing DR is the sum of retail DR from 2017 EIA-861 and wholesale DR from 2018 FERC Assessment of Demand Response and Advanced Metering; values are not modified to account for possible double-counting between wholesale and retail DR.

## Slide 9: DR capability varies significantly by state
2017 Demand Response Capability (% of System Peak)
Notes and sources: Brattle analysis of data from 2018 FERC Assessment of Demand Response and Advanced Metering and 2017 EIA-861. Wholesale DR capability from FERC Assessment allocated to states proportional to estimated state share of ISO peak demand (according to 2015-2017 EIA-861 data). Values are not modified to account for possible double-counting between wholesale and retail DR.
Significant new DR initiatives developing in Pacific Northwest (e.g., BPA CTA-2045 smart water heating demonstration project)
In CA, DR is increasingly deployed to address unexpected local capacity constraints; EV managed charging projects underway
NY utilities increasingly using DR for distribution purposes; also piloting natural gas DR programs
MN PUC Order requires significant DR additions; Xcel Energy developing innovative load flexibility portfolio
In Texas, retailers have begun to offer peak-time rebates to attract new customers
Pepco and BGE bid impacts of mass market DR programs directly into PJM capacity market
APS is piloting a program offering free electricity to loads that can be shifted to daytime hours with excess solar PV output
DR Capability (% of Peak)

## Slide 10: The “DR 1.0” market has matured
Once a rapidly growing resource, conventional DR is reaching a saturation point in markets where peak capacity needs have stalled
Total U.S. DR Peak Reduction Capability
Contributing Factors
  Increasingly stringent wholesale market participation rules
  Low capacity market prices
  Flat/depressed hourly energy price profile
  5+ years of excess peaking capacity projected by many utilities
Source: Brattle analysis of FERC Assessment of Demand Response and Advanced Metering reports (2006-2018) and EIA-861 Data (2005 – 2017). Post-2012 values are not modified to account for possible double-counting between wholesale and retail DR across data sources.

## Slide 11: “Load flexibility” provides improved system operational capabilities
DR can be repurposed to address three emerging industry megatrends
Mega-trend | Challenges
Renewables growth | Low net load leads to renewables curtailment and/or inefficient operation of thermal generation Intermittency in supply contributes to increased need for grid balancing
Grid modernization | Costly upgrades are needed to improve resiliency and accommodate growth in distributed energy resources
Electrification | Rapid growth in electricity demand may introduce new capacity constraints
Load Flexibility Solution
Electricity consumption can be shifted to times of low net load Fast-responding DR can provide ancillary services
Geographically-targeted DR can help to defer capacity upgrades
Controlling new sources of load can reduce system costs while maintaining customer comfort and adding value to smart appliances and EVs

## Slide 12: Quantifying Load Flexibility Potential

## Slide 13: Understanding load flexibility market potential & value
DR 1.0 market potential studies took a narrow view of DR capabilities. They need to be expanded to capture the full value of load flexibility.
Programs typically focus on demand reductions during a limited peak window and are constrained to a small number of hours per year
Quantified value and associated market potential are derived only from reductions in system peak demand
Scope of “DR 1.0” Market Studies
See appendix for a description of load flexibility programs.

## Slide 14: Understanding load flexibility market potential & value
First, consider innovative new applications of DR. Load flexibility will do more than just shave the peak.
Extend DR value streams
1
Several new uses of DR are possible, but existing programs are limited in their ability to provide those services
See appendix for a description of load flexibility programs.

## Slide 15: Understanding load flexibility market potential & value
Second, broaden the definition of DR. Load flexibility has the potential to provide higher value at a lower cost.
Broaden definition of DR
2
Extend DR value streams
1
See appendix for a description of load flexibility programs.

## Slide 16: Brattle developed the LoadFLEX model to comprehensively assess load flexibility potential

## Slide 17: The National Potential for Load Flexibility

## Slide 18: The national potential for load flexibility
A portfolio of load flexibility programs could triple existing DR capability, approaching 200 GW (20% of system peak) by 2030
Notes: Existing DR capability does not account for impacts of retail pricing programs, as fewer than 1% of customers are currently enrolled in dynamic pricing rates and the impacts of long-standing TOU rates are already embedded in utility load forecasts. See appendix for summary of key modeling assumptions.
Behavioral + Smart Tstat
DLC
Interruptible Tariff
Interruptible Tariff
Smart Thermostats
U.S. Cost-Effective Load Flexibility Potential
Existing Capability
2030 Potential
Expanded conventional programs
New load flexibility programs and value streams
2019-2030
market transition:
AMI deployment, EV adoption, customer growth, T&D expansion, renewables adoption
1
2
3
Smart Water Heating
Auto-DR
Dynamic Pricing
Demand Bidding + EV Charging

## Slide 19: Load flexibility value
Avoided generation costs are the largest source of load flexibility value under national average conditions. There is significant regional variation in this finding.
2030 Annual Benefits of National Load Flexibility Portfolio
Notes: Values shown in 2030 dollars. Values are gross benefits, before netting out costs of the load flexibility programs.
Avoided Generation Capacity
$9.4 billion/yr (57%)
Avoided T&D Capacity
$1.9 billion/yr (12%)
Ancillary Services
$0.3 billion/yr (2%)
Avoided Energy Costs
$4.8 billion/yr (29%)

## Slide 20: Regional differences
Our results are based on national average conditions. Conclusions will vary significantly by region and should be evaluated accordingly
Case Study: Comparing Minnesota and California
State | Primary drivers of need for load flexibility | Primary source of renewable generation additions | System value: Generation capacity | System Value: Energy (load shifting) | System Value: Ancillary services | System Value: T&D deferral | Load Flexibility Study
Minnesota | Pending retirement of 1,400 MW of coal generation | Wind |  |  |  |  | The Brattle Group, “The Potential for Load Flexibility in Xcel Energy’s NSP Service Territory,” June 2019
California | Renewables integration, local capacity constraints | Solar PV |  |  |  | Not Quantified | LBNL, “2015 California Demand Response Potential Study,” November 2016
= Primary source of value
= Moderate source of value
= Modest source of value

## Slide 21: Three predictions for the next decade
Utility load flexibility programs will get “smarter” before they get bigger
Residential load flexibility additions will exceed those of C&I
New regulatory incentives will drive growth in load flexibility

## Slide 22: Load flexibility assessment opportunities
Improved assessment of load flexibility opportunities can reduce system costs, facilitate grid modernization, and provide environmental benefits
Applications of Load Flexibility Market Assessment
Integrated Resource Plans | Ensures that the demand-side is fully reflected as a complementary alternative to generation resources
Renewables Integration Studies | Introduces load flexibility as an additional resource option for addressing supply intermittency challenges
Setting DR Targets / Policy Goals | Establishes achievable and cost-effective levels of load flexibility market penetration
“Value of DER” Proceedings | Provides a comprehensive framework for quantifying the value of a broad range of distributed energy resources

## Slide 23: The Transition: Potential  Pilots  Full Scale Deployment

## Slide 24: There have been four generations of pilots with time-varying rates
First generation: 1975 to 1981
Second generation: 2003-2009
Third generation: 2010-2016
Fourth generation: 2016 onwards

## Slide 25: These pilots have been designed with varying objectives in mind
Some have simply been demonstration projects
Others sought to measure the impact of time-varying rates
Some did not yield results because they were designed in haste
The best pilots conform to the scientific principles of experimental design, yielding results with both internal and external validity

## Slide 26: Six steps for developing a scientifically valid pilot design
Clearly articulate the pilot objectives
Ensure internal validity
Ensure external validity
Determine sampling frame/eligible population for the pilot
Undertake “statistical power calculations”
Incorporate attrition assumptions in the final sample sizes

## Slide 27: Different pilots have used different approaches to pilot design
Early pilots typically relied on random sampling with voluntary participation + randomly selected control groups
California Statewide Pricing Pilot, 2003-04; Baltimore Gas and Electric Smart Energy Pricing Pilot, 2007-10)
Some of the more recent pilots used “RCT” and “RED”
SMUD SmartPricing Pilot, 2014; Ontario RPP Pilots, 2018
However, practical considerations necessitated the use of random sampling with matched control group
PC44 TOU Pilot in Maryland, 2019; PowerPath DC Pepco Residential TOU Pilot, 2020; Alectra Advantage Power Pricing Pilot, 2017.

## Slide 28: Three ongoing TOU Pilots in Maryland (PC 44) are using the matching control group approach
BGE, Pepco and DPL are implementing the pilots
For all three utilities, the TOU rate is applied to both energy and delivery charges
Two year pilots commenced in June 1, 2019.
The peak to off-peak ratio is very pronounced and varies from ~5-to-1 to 6- to-1 across the utilities
The peak hours vary by season
  HE 15-19 on summer weekdays (June 1 – September 30)
  HE 7-9 on winter weekdays (October 1 – May 31)
The treatment customers also get behavioral messaging
The pilots were designed to allow impacts to differ between low- and medium-income (“LMI”) and non-LMI customers
Interim impact evaluation (using Summer 2019 data) yielded promising results; first year analysis will be completed in the summer of 2020

## Slide 29: Checklist for successful evaluation, measurement and verification (EM&V)
The experimental design of each pilot dictates the optimal evaluation method: differences-in-differences (ANOVA or ANCOVA); panel regressions (fixed-effects or random-effects); individual customer regressions
Decide on the evaluation approach based on the experimental design
Identify load impact metrics to be quantified (i.e. peak, mid-peak, off-peak impacts, average daily conservation impact, etc.)
Estimate alternative models and select the one that leads to most accurate predictions
Decide whether quantifying customers’ overall price responsiveness would be useful in the form of price elasticities, beyond the ex-post load impacts quantified in the pilot
  Own/daily price elasticity (captures the change in the level of overall consumption due to the changes in the average daily price
  Substitution price elasticity (captures customer’s ability to substitute inexpensive off-peak consumption for more expensive peak consumption)

## Slide 30: Five steps to full-scale deployment
  Design the rates
  Market the rates
  Include enabling technologies
  Provide behavioral messaging
  Roll out the new rates

## Slide 31: Brattle’s load flexibility expertise
Market sizing & resource planning
What is the potential size of the load flexibility resource?
Regulatory support
How can markets be more effectively opened to the demand-side?
Pilot program design and evaluation
How to design new pilots, programs, and participation incentives?
Strategy development
What are successful DR business models in other markets?
What is the potential value of the resource?
What barriers will prevent this potential from being realized?
What are the measured impacts of the new programs?
What business models have failed and why?
How should rates be redesigned to promote load flexibility?
Are new regulatory incentives needed?
What regulatory developments are on the horizon?
Is the organization aligned around a consistent view of DR value?
How to communicate these findings to regulators & policymakers?

## Slide 32: Selected Brattle load flexibility & DR work products
  The Potential for Load Flexibility in Xcel Energy’s Northern States Power Service Territory, prepared for Xcel Energy, June 2019.
  The Hidden Battery: Opportunities in Electric Water Heating, prepared for NRECA, NRDC, and PLMA, January 2016.
  Demand Response Market Research: Portland General Electric, 2016 to 2035, prepared for PGE, January 2016.
  Valuing Demand Response: International Best Practices, Case Studies, and Applications, prepared for EnerNOC, January 2015.
  Exploring the Role of Natural Gas and Renewables in ERCOT, Part III: The Role of DR, EE, and CHP, prepared for the Texas Clean Energy Coalition, May 2014.
  Demand Response Market Potential in Xcel Energy’s Northern States Power Service Territory, prepared for Xcel Energy, April 2014.
  PacifiCorp Demand-Side Resource Potential Assessment for 2015-2034, Volume 3: Class 1 and 3 DSM Analysis, prepared for PacifiCorp with EnerNOC Utility Solutions, May 2014.
  Estimating Xcel Energy’s Public Service Company of Colorado Territory Demand Response Market Potential, prepared for Xcel Energy with YouGov America, June 2013.
  Bringing Demand Side Management to the Kingdom of Saudi Arabia, prepared for ECRA with Global Energy Partners and PacWest Consulting, May 2011.
  The Demand Response Impact and Value Estimation (DRIVE) Model, developed for FERC, 2010. Available on FERC website.
  National Action Plan on Demand Response, prepared for FERC, June 2010.
  A National Assessment of Demand Response Potential, prepared for FERC with Freeman Sullivan and Global Energy Partners, June 2009.

## Slide 33: Other load flexibility potential studies
  Abdisalaam, Ahmed, Ioannis Lampropoulos, Jasper Frunt, Geert P.J. Verbong, and Wil L. Kling, “Assessing the economic benefits of flexible residential load participation in the Dutch day-ahead auction and balancing market,” Conference paper: 2012 9th International Conference on the European Energy Market, May 2012.
  Alstone, Peter, Jennifer Potter, Mary Ann Piette, Peter Schwartz, Michael A. Berger, Laurel N. Dunn, Sarah J. Smith, Michael D. Sohn, Arian Aghajanzadeh, Sofia Stensson, Julia Szinai, Travis Walter, Lucy McKenzie, Luke Lavin, Brendan Schneiderman, Ana Mileva, Eric Cutter, Arne Olson, Josh Bode, Adriana Ciccone, and Ankit Jain, “2025 California Demand Response Potential Study – Charting California’s Demand Response Future: Final Report on Phase 2 Results,” March 1, 2017.
  D’hulst, R., W. Labeeuw, B. Beusen, S. Claessens, G. Deconinck, and K. Vanthournout, “Demand response flexibility and flexibility potential of residential smart appliances: Experiences from large pilot test in Belgium,” Applied Energy, 155, 79-90, 2015.
  De Coninck, Roel and Lieve Helsen, “Bottom-up Quantification of the Flexibility Potential of Buildings,” Conference paper: Building Simulation, 13th International Conference of the International Building Performance Simulation Association, January 2013.
  Dyson, Mark, James Mandel, Peter Bronski, Matt Lehrman, Jesse Morris, Titiaan Palazzi, Sam Ramirez, and Hervé Touati, “The Economics of Demand Flexibility: How “flexiwatts” create quantifiable value for customers and the grid,” Rocky Mountain Institute, August 2015.
  Eto, Joseph, H., John Undrill, Ciaran Roberts, Peter Mackin, and Jeffrey Ellis, “Frequency Control Requirements for Reliable Interconnection Frequency Response,” prepared for the Office of Electric Reliability Federal Energy Regulatory Commission, February 2018.
  Goldenberg, Cara, Mark Dyson, and Harry Masters, “Demand Flexibility – The key to enabling a low-cost, low-carbon grid,” Rocky Mountain Institute, February 2018.
  Lopes, Rui Amaral, Adriana Chambel, João Neves, Daniel Aelenei, João Martins, “A literature review of methodologies used to assess the energy flexibility of buildings,” Energy Procedia, 91, 1053-1058, 2016.
  O’Connell, Sarah, and Stefano Riverso, “Flexibility Analysis for Smart Grid Demand Response,” 2017.
  Olsen, D. J., N. Matson, M. D. Sohn, C. Rose, J. Dudley, S. Coli, S. Kiliccote, M. Hummon, D. Palchak, J. Jorgenson, P. Denholm, O. Ma., “Grid Integration of Aggregated Demand Response, Part 1: Load Availability Profiles and Constraints for the Western Interconnection,” LBNL-6417E, 2013.
  Potter, Jennifer and Peter Cappers, “Demand Response Advanced Controls Framework and Assessment of Enabling Technology Costs,” prepared for the Office of Energy Efficiency and Renewable Energy U.S. Department of Energy, August 2017.
  Starke, Michael, Nasr Alkadi, and Ookie Ma, “Assessment of Industrial Load for Demand Response across U.S. Regions of the Western Interconnect,” prepared for the Energy Efficiency and Renewable Energy U.S. Department of Energy, ORNL/TM-2013/407, September 2013.
  Stoll, Brady, Elizabeth Buechler, and Elaine Hale, “The Value of Demand Response in Florida,” The Electricity Journal, 30, 57-64, 2017.

## Slide 34: Appendix

## Slide 35: Illustrating the potential for load flexibility
Electric water heating is a compelling example of load flexibility
Electric resistance water heating load can be controlled to provide several grid services. The thermal energy storage properties of the water tank work similar to a battery
While water heaters have been used to reduce peak capacity for decades, recent technological developments now allow for more flexibility in load control, including the provision of frequency regulation
In the past few years, “grid-connected water heating” programs have been introduced in Arizona, California, Hawaii, Minnesota, Oregon, Vermont, and across PJM
In recognition of the potential renewables integration benefits, 2015 federal legislation made grid-connected water heaters exempt from prohibitive energy efficiency standards
1
2
3
Water Heating Load Profile
1
2
3
Heating element controlled with near-instantaneous response to provide balancing services
Off-peak load building to reduce wind curtailments or reduce ramping of thermal generation
Peak demand reduction to reduce need for generation capacity and/or T&D capacity, and to avoid peak energy prices

## Slide 36: Consumer technologies drive the DR transition
Adoption of behind-the-meter (BTM) energy technology is accelerating; these technologies are enabling the provision of load flexibility
BTM Storage
(U.S. capacity, MW)
Smart Meters
(U.S. meters, millions)
Electric Vehicles
(U.S. annual sales)
Smart Appliances
(U.S. homes, millions)
Source: Estimated from Wood Mackenzie and Energy Storage Association, 2019
Source: Institute for Energy Innovation (IEI), 2017
Source: Edison Electric Institute and IEI, 2018
Source: Brattle estimate based on review of various sources
CAGR: 89% (2017-24)
85x total growth in 7 yrs
CAGR: 22% (2007-20)
13x total growth in 13 yrs
CAGR: 24% (2017-25)
6x total growth in 8 yrs
CAGR: 53% (2017-20)
4x total growth in 3 yrs

## Slide 37: The national potential for load flexibility
  Expanded conventional programs
    Existing conventional programs often have untapped potential that can be harnessed through revamped customer marketing and outreach, modified program rules, and redesigned incentive structures
    These programs generally only provide peak capacity value, but often can do so cost-effectively by leveraging existing program infrastructure
    Potential increase over existing DR capability: 16 GW (27% increase)
  New load flexibility programs
    Relative to existing conventional programs, new load flexibility programs capture additional value streams and leverage emerging load control technologies and sources of load
    Under current national average market conditions, the most significant cost-effective potential is in smart thermostat programs (residential) and dynamic pricing (all customer segments)
    Potential increase over existing DR capability: 40 GW (67% increase)
  Market transition impacts (2019 – 2030)
    Growth in adoption of AMI, EVs, smart thermostats and other smart appliances over the forecast horizon enables expanded participation in load flexibility programs
    Increased renewable generation development introduces more energy price variability and a greater need for ancillary services, increasing the value of load flexibility programs with fast-response capability
    Continued expansion and modernization of the T&D system introduces a growing opportunity for non-wires alternatives
    These market developments justify greater incentive payments for customer participation in load flexibility programs and also justify the introduction of robust smart water heating and Auto-DR programs, among others
    Potential increase over existing DR capability: 83 GW (140% increase)
1
Three factors drive the national potential estimate of 198 GW
2
3

## Slide 38: Load flexibility value
Avoided generation costs are the largest source of load flexibility value under national average conditions. There is significant regional variation in this finding.
2030 Annual Benefits of National Load Flexibility Portfolio
Avoided Generation Capacity,
$9.4 billion/yr (57%)
Value based on avoided cost of gas-fired combustion turbine, assuming no near-term peaking capacity need in some regions
Capacity remains the dominant source of load flexibility value through at least 2030
Capacity value will vary significantly by region; load flexibility poised to provide most capacity value in regions with pending capacity retirements, supply needs in transmission-constrained locations, or unexpected supply shortages
Avoided Transmission & Distribution Capacity, $1.9 billion/yr (12%)
Value includes system-wide benefits of peak demand reduction, plus added benefit of geographically targeted T&D investment deferral
Geo-targeted T&D deferral opportunities are typically high value but limited in quantity of near-term need; this value is likely to grow as utility T&D data collection and planning processes improve
Notes: Values shown in 2030 dollars. Values are gross benefits, before netting out costs of the load flexibility programs.
Ancillary Services, $0.3 billion/yr (2%)
Value accounts only for frequency regulation and assumes a need equal to 0.5% of system peak demand; additional value may exist if considering other ancillary services products
Frequency regulation provides very high value to a small amount of capacity; in our analysis, the full need for frequency regulation can be served through a robust smart water heating program
Avoided Energy Costs, $4.8 billion/yr (29%)
Value accounts for reduced resource costs associated with shifting load to hours with lower cost to serve; does not include consumer benefits from reductions in wholesale price of electricity
Energy value is best captured through programs that provide daily flexibility year-round, such as Auto-DR for C&I customers, TOU rates, EV charging load control, and smart water heating

## Slide 39: Operational implications
Deep load reductions will require significant changes to the way DR programs have been utilized historically
Utility Load Duration Curve (Top 1,000 Hours)
Required # Hours of Dispatch Over Year
15% reduction in system peak demand from load flexibility portfolio
106 hours of DR dispatch required to flatten peak
Notes: Based on actual load data for a large Midwestern utility during a year with a hotter-than-normal summer.
Implications: Load flexibility programs will need to be dispatched much more frequently and during a broader window of hours of the day. This requires new customer engagement initiatives and advanced portfolio dispatch strategies.
Max consecutive hours of dispatch required in one day to achieve 15% peak reduction = 12 hrs

## Slide 40: Policy & market developments
The constantly evolving policy and market landscape will define new load flexibility opportunities and challenges
Policies are increasingly opening wholesale markets to demand-side participation (e.g., FERC Order 745)
Existing market rules still undervalue load flexibility (e.g., year-round, 10-hour performance requirement for capacity credit)
Wholesale Market Design
The transition to a fully decarbonized and electrified economy will create massive fluctuations in power supply and load, emphasizing the value of load flexibility
Seasonal mismatches between supply and demand will be difficult to mitigate through load flexibility alone
Deep Decarbonization Policies
Performance incentive mechanisms will provide utilities with a financial incentive to pursue load flexibility as an alternative to capital investment in grid infrastructure
Without accompanying incentives, traditional cost-of-service regulation discourages utility investment in demand-side resource options
Regulatory Incentives
Standards such as CTA-2045 can significantly reduce load flexibility technology costs for consumers
Policies prohibiting programs that promote electrification, such as the Three Prong Test in California, will inhibit adoption of load flexibility technologies
Codes and Standards
Cost declines for smart home technologies and EVs could accelerate load flexibility adoption
Batteries and solar PV could soon become the technology that load flexibility competes with, rather than combustion turbines
Emerging Technologies
Some utilities are using increasingly sophisticated modeling techniques to account for the unique value of load flexibility, putting it on a level playing field with conventional generation resources in planning activities
Most traditional off-the-shelf resource planning approaches de-emphasize load flexibility
Resource Planning

## Slide 41: The role of retail pricing
There are two competing views on how to incentivize load flexibility
 | Method 1: Dynamic retail rates (“Prices-to-Devices”) | Method 2: Participation incentives (“Flexibility Payments”)
Example of load flexibility incentive | Sub-hourly real-time pricing with locational price variation | Fixed monthly incentive payment to participate in smart thermostat program
Role of retail rates | Rates are the primary driver of customer investment in various load flexibility technologies and/or arrangements with third-party load flexibility service providers, in order to capture electricity bill savings | Simple dynamic pricing rates are offered as complementary, voluntary alternatives to various incentive-based programs
Advantages | Equitable: All load flexibility is treated equal; no need to develop program-specific incentive payments Efficient: Once the necessary infrastructure is in place (a big hurdle), ongoing implementation cost is relatively low Dynamic: Real-time prices could provide a financial incentive that is more closely aligned with the value of load flexibility to the system | Simple: Fixed payments are predictable and easy for customers to understand Tailored: Each program can be designed to optimize the characteristics of the specific end-use it targets Practical: Does not involve massive IT investments or political complexity of implementing highly granular retail pricing
Implications: Both methods can be used to achieve the potential identified in this study. Utilities & regulators must determine their preferred position on the spectrum of options.

## Slide 42: Description of load flexibility programs
Direct load control (DLC): Participant’s central air-conditioner is remotely cycled using a switch on the compressor.
Smart thermostats: An alternative to conventional DLC, smart thermostats allow the temperature setpoint to be remotely controlled to reduce A/C usage during peak times. Customers could provide their own thermostat, or purchase one from the utility.
Interruptible rates: Participants agree to reduce demand to a pre-specified level and receive an incentive payment in the form of a discounted rate.
Demand bidding: Participants submit hourly curtailment schedules on a daily basis and, if the bids are accepted, must curtail the bid load amount to receive the bid incentive payment or may be subject to a non-compliance penalty.
Time-of-use (TOU) rate: Static price signal with higher price during peak hours (assumed 5-hour period aligned with system peak) on non-holiday weekdays. Modeled for all customers as well as for EV charging.
Critical peak pricing (CPP) rate: Provides customers with a discounted rate during most hours of the year, and a much higher rate (typically between 50 cents/kWh and $1/kWh) during peak hours on 10 to 15 days per year.
Behavioral DR: Customers are informed of the need for load reductions during peak times without being provided an accompanying financial incentive. Customers are typically informed of the need for load reductions on a day-ahead basis and events are called somewhat sparingly throughout the year. Behavioral DR programs have been piloted by several utilities, including Consumers Energy, Green Mountain Power, the City of Glendale, Baltimore Gas & Electric, and four Minnesota cooperatives.

## Slide 43: Description of load flexibility programs (cont’d)
EV managed charging: Using communications-enabled smart chargers allows the utility to shift charging load of individual EVs plugged-in at home from on-peak to off-peak hours. Customers who do not opt-out of an event receive a financial incentive.
Timed water heating: The heating element of electric resistance water heaters can be set to heat water during off-peak hours of the day. The thermal storage capabilities of the water tank provide sufficient hot water during peak hours without needing to activate the heating element.
Smart water heating: Offers improved flexibility and functionality in the control of the heating element in the water heater. Multiple load control strategies are possible, such as peak shaving, energy price arbitrage through day/night thermal storage, or the provision of ancillary services such as frequency regulation. Modeled for electric resistance water heaters, as these represent the vast majority of electric water heaters and are currently the most attractive candidates for a range of advanced load control strategies.
Ice-based thermal storage: Commercial customers shift peak cooling demand to off-peak hours using ice-based storage systems. The thermal storage unit acts as a battery for the customer’s A/C unit, charging at night (freezing water) and discharging (allowing ice to thaw to provide cooling) during the day.
C&I Auto-DR: Auto-DR technology automates the control of various C&I end-uses. Features of the technology allow for deep curtailment during peak events, moderate load shifting on a daily basis, and load increases and decreases to provide ancillary services. Modeled end-uses include HVAC and lighting (both luminaire and zonal lighting options).

## Slide 44: The LoadFLEX modeling framework

## Slide 45: Load flexibility analytical challenges & solutions
Load Flexibility Analytical Challenge | LoadFLEX Approach | Illustration
Reliably estimating impacts of nascent programs & technologies | Brattle maintains a database of load flexibility programs and their associated costs, impacts, and adoption rates Supplementary interviews are conducted to fill in gaps where publicly available data is limited Primary market research can establish tailored estimates of customer adoption Participation is modeled as a function of the cost-effective participation incentive payment level Probabilistic analysis (i.e., Monte Carlo simulation) can account for uncertainty | 
Accounting for “depth” of resource need | Some of the new load flexibility value streams are sensitive to the quantity of the DR resource that is participating; for instance, frequency regulation is valuable but has very limited need on most systems Modeling establishes the “depth” of each value opportunity and quantifies the relationship between incremental value and DR resource additions | 
DR Enrollment vs Incentive Payment
DR Value vs Quantity

## Slide 46: Load flexibility analytical challenges & solutions
Load Flexibility Analytical Challenge | LoadFLEX Approach | Illustration
Quantifying deferred distribution capacity value | Distribution capacity deferral is a highly system-specific calculation, requiring locational assessment of utility distribution system data Initial screening identifies grid locations at risk of capacity constraints The performance profile of the load flexibility resource is compared to the load profile of the distribution system component Capacity deferral value is assigned based on the probability that constraints can be relieved through deployment of the load flexibility resource | 
Accounting for “stacked value” | Load flexibility can provide multiple sources of value, but analysis must account for realistic operational constraints associated with capturing this value Each value stream is converted to an hourly price series based on assessment of appropriate cost drivers Load flexibility resource is “dispatched” against the price series based on realistic utilization algorithms | 
DR Impact on Distribution System
DR Stacked Value (Illustrative)

## Slide 47: Key modeling assumptions
To illustrate the national potential for load flexibility, we modeled the potential for a utility with characteristics that are roughly representative of the national average. Results were then scaled up to the national level.
 | 2019 | 2030
Power Supply Mix | 74% fossil, 15% nuclear, 9% renewable, 2% hydro | 54% fossil, 29% renewable, 12% nuclear, 2% hydro, 3% EE
Henry Hub Gas Price | $3/MMBtu | $8/MMBtu
U.S. System Peak Demand | 881 GW | 987 GW
Marginal Generation Capacity Cost | $45/kW-yr Allocated across top 100 hours of hourly system load shape | $74/kW-yr Allocated across top 100 hours of hourly system load shape
Marginal Energy Cost | Forecasted hourly prices Average: $25/MWh | Forecasted hourly prices Average: $41/MWh
Avoided System-wide T&D Cost | $10/kW-yr | Same as 2019
Geo-targeted Distribution Investment Deferral Value | $35/kW-yr average, limited to 8,800 MW | $45/kW-yr average, limited to 29,600 MW (2019 – 2030)
Frequency Regulation Value | $11/MWh average, limited to 2,400 MW | $14/MWh average, limited to 5,300 MW
DR Technology Costs | Varies by technology | 30% reduction from current levels

## Slide 48: Key modeling assumptions (cont’d)
  Eligibility: Determined based on a review of appliance saturation data and independent forecasts.
    E.g., 19 million EVs on the road by 2030, 64% of households with central A/C, 75% of households with AMI
  Participation: Based on a review of market research studies, actual participation in existing DR programs, and assumptions from various DR potential studies. Participation is calibrated to the maximum incentive payment level that allows the program to pass the benefit-cost screen. At the portfolio level, participation is reduced to account for overlap that would otherwise exist in competing programs.
    E.g., Approximately 70% of eligible customers participating in smart thermostat program (i.e., those with smart thermostat and central A/C), 14% of eligible customers participating in opt-in CPP (i.e., those with AMI)
  Program performance: Operational parameters (hourly load impacts, allowed timing and frequency of dispatch events) based on review of pilot studies and full-scale utility programs
    E.g., 0.34 kW avg peak impact from residential CPP, based on simulation using Brattle’s Arcturus database, with up to 75 hours of dispatch per summer
  Program costs: Include startup costs, marketing and customer recruitment, utility share of equipment and installation, program administration and overhead, churn, and participation incentives. Based on review of utility programs, demonstration projects, and conversations with vendors.
    E.g., Smart thermostat program/equipment cost of $27/participant-year and incentive cost of $25/participant-year
  Dispatch: Simulated using Brattle’s LoadFLEX model. Load flexibility programs are dispatched against the “stacked” marginal hourly cost series to maximize benefits, subject to each program’s unique operational constraints.
For additional information about the LoadFLEX modeling methodology, see The Brattle Group, “The Potential for Load Flexibility in Xcel Energy’s Northern States Power Service Territory,” prepared for Xcel Energy, June 2019.

## Slide 49: Three commonly used approaches to pilot design
Source: Sergici et al., “Evaluation, Measurement and Verification Plan for the PC44 TOU Pilots,” prepared for PC44 Rate Design Work Group, June 2018.

## Slide 50: Five steps to full-scale deployment

## Slide 51: Five steps to full-scale deployment

## Slide 52: Presenter Information
Ryan Hledik
Principal │ San Francisco, CA
ryan.hledik@brattle.com
415.217.1029
Ryan Hledik specializes in regulatory and planning matters related to the emergence of distributed energy technologies.
Mr. Hledik has consulted for more than 50 clients across 30 states and eight countries. He has supported his clients in matters related to energy storage, load flexibility, distributed generation, electrification, retail tariff design, energy efficiency, and grid modernization.
Mr. Hledik’s work has been cited in regulatory decisions establishing procurement targets for energy storage and demand response, authorizing billions of dollars in smart metering investments, and approving the introduction of innovative rate designs. He is a recognized voice in debates on how to price electricity for customers with distributed generation. He co-authored Saudi Arabia’s first Demand Side Management (DSM) plan, and the Federal Energy Regulatory Commission’s landmark study, A National Assessment of Demand Response Potential.
Mr. Hledik has published more than 25 articles on retail electricity issues and has presented at industry events throughout the United States as well as in Brazil, Belgium, Canada, Germany, Poland, South Korea, Saudi Arabia, the United Kingdom, and Vietnam. His research on the “grid edge” has been cited in The New York Times and The Washington Post, and in trade press such as GreenTech Media, Utility Dive, and Vox. He was named to Public Utilities Fortnightly’s Under Forty 2019 list, recognizing rising stars in the industry.
Mr. Hledik received his M.S. in Management Science and Engineering from Stanford University, where he concentrated in Energy Economics and Policy. He received his B.S. in Applied Science from the University of Pennsylvania, with minors in Economics and Mathematics. Prior to joining Brattle, Mr. Hledik was a research assistant with Stanford’s Energy Modeling Forum and a research analyst in Charles River Associates’ Energy Practice.
The views expressed in this presentation are strictly those of the presenter(s) and do not necessarily state or reflect the views of
The Brattle Group, Inc. or its clients.

## Slide 53: Presenter Information
Ahmad Faruqui
Principal │ San Francisco, CA
Ahmad.Faruqui@brattle.com
415.217.1029
Ahmad Faruqui is an internationally recognized authority on the design, evaluation and benchmarking of tariffs. He has analyzed the efficacy of tariffs featuring fixed charges, demand charges, time-varying rates, inclining block structures, and guaranteed bills. He has also designed experiments to model the impact of these tariffs and organized focus groups to study customer acceptance. Besides tariffs, his areas of expertise include demand response, energy efficiency, distributed energy resources, advanced metering infrastructure, plug-in electric vehicles, energy storage, inter-fuel substitution, combined heat and power, microgrids, and demand forecasting. He has worked for nearly 150 clients on 5 continents, including electric and gas utilities, state and federal commissions, governments, independent system operators, trade associations, research institutes, and manufacturers.
Ahmad has testified or appeared before commissions in Alberta (Canada), Arizona, Arkansas, California, Colorado, Connecticut, Delaware, the District of Columbia, FERC, Illinois, Indiana, Kansas, Maryland, Minnesota, Nevada, Ohio, Oklahoma, Ontario (Canada), Pennsylvania, Saudi Arabia, and Texas. He has presented to governments in Australia, Egypt, Ireland, the Philippines, Thailand, New Zealand and the United Kingdom and given seminars on all 6 continents. He has also given lectures at Carnegie Mellon University, Harvard, Northwestern, Stanford, University of California at Berkeley, and University of California at Davis and taught economics at San Jose State, the University of California at Davis, and the University of Karachi.
His research been cited in Business Week, The Economist, Forbes, National Geographic, The New York Times, San Francisco Chronicle, San Jose Mercury News, Wall Street Journal and USA Today. He has appeared on Fox Business News, National Public Radio and Voice of America. He is the author, co-author or editor of 4 books and more than 150 articles, papers and reports on energy matters. He has published in peer-reviewed journals such as Energy Economics, Energy Journal, Energy Efficiency, Energy Policy, Journal of Regulatory Economics and Utilities Policy and trade journals such as The Electricity Journal and the Public Utilities Fortnightly. He is a member of the editorial board of The Electricity Journal. He holds BA and MA degrees from the University of Karachi, both with the highest honors, and an MA in agricultural economics and a PhD in economics from The University of California at Davis, where he was a research fellow.
The views expressed in this presentation are strictly those of the presenter(s) and do not necessarily state or reflect the views of
The Brattle Group, Inc. or its clients.

## Slide 54: Demand Response Insights for the Northwest
Juliet Homer; Josh Butzbaugh; Dhruv Bhatnagar
Pacific Northwest National Laboratory
Notes: Stock Image

## Slide 55: Outline
Load Shifting in Residential Buildings: Grid-connected Heat Pump Water Heaters (HPWH) in the Pacific Northwest (PNW) – Josh Butzbaugh
Olympic Peninsula GridWise Demo, Portland General Electric Demand Response Testbed, and Other Considerations for the PNW – Juliet Homer
Demand Response in Hawaii and Massachusetts – Dhruv Bhatnagar

## Slide 56: Load Shifting in Residential Buildings: Grid-Connected Heat Pump Water Heaters in the Pacific Northwest
Presenter: Josh Butzbaugh
Team: Cheryn Metzger, Josh Butzbaugh, Walt Hunt, Travis Ashley, Ebony Mayhorn, Sam Rosenberg,Jaime Kolln, and Michael Baechler
Notes: Stock Image

## Slide 57: Project Goals: Grid-Connected HPWHs
Determine the kW reduction (on-peak) between electric resistance (ERWHs) and connected heat pump water heaters (HPWHs)
Demonstrate a 24x7 control paradigm for shifting load to align with renewable generation (e.g., loading up during solar bulge in late afternoon or high-wind-power periods in early morning)
Evaluate customer acceptance/impact of 24x7 demand response operation of their water heater
Compare data reported from the universal communication modules to sub-metered data to determine accuracy

## Slide 58: Overview
Water heating is the second largest energy use in U.S. residences
Heat pump water heaters (HPWH) can save 60% of electric water heating energy
  Only 70,000 shipments per year (1.5% market share of electric water heaters)
  Market share has been flat since 2009 despite more than 180 models in the market
Opportunity to demonstrate the viability of HPWH in providing load shifting
  Pacific Northwest – region is active and committed to studying energy efficiency and load shifting strategies to integrate into existing utility programs
  Southeast or Mid-Atlantic – regions with high potential for energy efficiency and load shifting, need technology demonstration to justify launching new programs and/or revising state policies
  Transfer lessons learned and best practices from PNW study to a field study based in the Southeast

## Slide 59: The Secret Sauce
CTA-2045
Manufacturer only supplies standard port
Others can pay additional costs to make devices “connected”
Interface supports every type of communication method
  Physical layer (e.g. Wi-Fi, 4G LTE, etc.)
  Command layer (e.g. SEP, OpenADR, etc.)
Heat Pump Water Heaters
  3-5 year payback
  Reduce peak loads
  Interactions with interior temperatures are minimal 1
  NEEA Advanced Water Heater Spec
    Cold-climate compressor cut-off temperature
    Maximum decibel requirements
    CTA-2045 or equivalent
1Widder et al. Interaction between HPWH or Other Internal Point Source Loads and a Central Heating System. NEEA/PNNL https://neea.org/img/uploads/interaction-between-heat-pump-water-heaters-and-heating-system.pdf

## Slide 60: How It Really Works

## Slide 61: Roles and Responsibilities
  Bonneville Power Administration: Initial funder of NW efforts
  Portland General Electric: Lead utility
  U.S. Department of Energy: Funder of PNNL work
  Northwest Energy Efficiency Alliance: Market analysis
  PNNL: Data analysis and reporting
  Other Utilities: Recruitment of homes for study
    Puget Sound Energy
    Tacoma Power
    Franklin PUD
    Emerald PUD
    Clark PUD

## Slide 62: Northwest Field Validation
Project Scope
145 HPWH (~40 sub-metered)
86 Electric Resistance Water Heaters
10 weeks of data per season
2 load shifting events per day during peak hours
Control group and event group flip-flop each week
Date | Event Description | Duration | Start Time | End Time
Feb. 19th | Load Up | 1 hr | 5:00 | 5:59
Feb. 19th | Shed | 3 hrs | 6:00 | 9:00
Feb. 19th | Load Up | 1 hr | 16:00 | 16:59
Feb. 19th | Shed | 3 hrs | 17:00 | 20:00
Load Up Event = Command water heater to energize and reach set point
Shed Event = Command water heater to turn off as long as customer still has hot water (exact definition of “hot water” is determined by manufacturer/algorithm)
Example Event Schedule for One Day

## Slide 63: Average Peak kW Reduction during Shed Events per Water Heater
Many ways to determine the average kW reduction
Baseline 1: Event Group vs. Control Group during same week
Baseline 2: Event Group compared to its previous week as the Control Group
Baseline 3: Full Season Average of all Event and Control power data
 | ERWH (Baseline) | Connected ERWH | HPWH | Connected HPWH | % Load Reduced Connected HPWH
Winter Morning | 616 | -374 | -310 | -533 | 87%
Winter Evening | 668 | -321 | -437 | -602 | 90%
Summer Evening | 474 | -347 | -365 | -448 | 95%
Full Season Average Watts Reduced per Hour of Shed Event (per Water Heater)

## Slide 64: What About the Consumer?
Opt-Outs allowed two ways:
  Button on the water heater (address run out in progress)
  Through the web portal (planned high demand period)
1,634 opt-out hours during the winter season
Out of 40,000 opportunities to opt-out (145 customers, about 28 event-hours per week)
Results in 4% opt-outs (relatively low!)
Most customers seem largely unaffected by the demand response program

## Slide 65: What’s Next?
Load Shifting with Heat Pump Water Heaters
  Field Validation in the Northwest
    Machine learning to optimize load shifting with occupant schedules
    Support for transferring knowledge to other regions
  Field Validation in the Southeast
    Recruiting, installing connection devices, collecting data
Load Shifting With Ductless Mini-Splits
  Taking advantage of CTA-2045 enabled devices that are already in the field
  First field validation study of HVAC/heat pump load management using CTA-2045

## Slide 66: Published Reports
BPA (Bonneville Power Administration). 2018. CTA-2045 Water Heater Demonstration Report Including A Business Case for CTA-2045 Market Transformation. https://www.bpa.gov/EE/Technology/demand-response/Documents/Demand%20Response%20-%20FINAL%20REPORT%20110918.pdf
Metzger, CE, Ashley T, Bender, S, Morris, S, Kelsven P, Urbatsch E, Kelly N, Eustis, C. 2018. Large Scale Demand Response with Heat Pump Water Heaters. ACEEE (American Council for an Energy Efficient Economy). http://iframes.aceee.org/confpanel.cfm?&ConferencePanelID=291
Metzger, CE, Kelsven P, Ashley T, Bender, S, Kelly N, Eustis, C. 2019. Not Your Father’s Water Heater Demand Response Program: Measuring Impacts from an Innovative Load Shifting Pilot. International Energy Program Evaluation Conference. August 2019. https://www.iepec.org/2019_proceedings/#/paper/event-data/055-pdf
Widder, S, Metzger CE, Petersen, J, McIntosh, J. 2017. Interaction between Heat Pump Water Heaters or Other Internal Point Source Loads and a Central Heating System. NEEA, August 2017. https://neea.org/img/uploads/interaction-between-heat-pump-water-heaters-and-heating-system.pdf

## Slide 67: Other Opportunities
Building on this work with BPA, combining technologies: space conditioning, water heating, pool pumps, spas/hot tubs, other equipment?
Building on Fault Detection and Diagnostics for residential
Previous Lab Homes work:
  Electric vehicle/appliance interaction under Rick Pratt
  Cyber Security of Connected Devices under Penny McKenzie

## Slide 68: Olympic Peninsula GridWise Demo, Portland General Electric Demand Response Testbed, and Other Considerations for the PNW
Juliet Homer
Pacific Northwest National Laboratory
Notes: Stock Image

## Slide 69: Olympic Peninsula GridWise Demo Project
Established viability of transactive decision- making to achieve multiple objectives
  Peak load, distribution constraints, wholesale prices
  Residential, commercial, & municipal water pumping loads, distributed generation
Conducted in 2006-2007
Notes: Conducted in 2006-2007; oldie but goodie

## Slide 70
70
0 6 12 18 24
IBM
ancillary services
distribution congestion
transmission congestion
wholesale cost
Johnson Controls
Invensys
$
MW
Clallam PUD & Port Angeles
112 homes, 0.5 MW DR
Clallam County
PUD Water
Supply District
0.2 MW DR
Internet broadband
communications
Market
Sequim Marine Sciences Lab
0.3 MW DR
0.5 MW DG

## Slide 71: Winter Load Shifting Results for Real-Time Pricing Customers
Winter peak load shifted by pre-heating
Resulting new peak load at 3 AM is non-coincident with system peak at 7 AM
Illustrates key finding that a portfolio of contract types may be optimal – i.e., don’t want to just create a new peak

## Slide 72: Flexible Loads to Manage Feeder Loading

## Slide 73: Olympic Peninsula Demo: Key Findings
Significant demand response was obtained:
  15% reduction of peak load
  Up to 50% reduction in total load for several days in a row during shoulder periods
Response to wholesale prices + transmission congestion + distribution congestion
Able to cap net demand at an arbitrary level to manage local distribution constraint
Short-term response capability could provide regulation, other ancillary services add significant value at very low impact and low cost
Same signals integrated commercial & institutional loads, distributed resources (backup generators)

## Slide 74: Portland General Electric (PGE) Demand Response Testbed
From PGE 2019 Smart Grid Report Update to Oregon PUC July 2019
Grew from PGE’s 2016 IRP
PGE hired a consultant to conduct a demand response potential study
Oregon Public Utility Commission (OPUC) Staff were concerned PGE’s DR targets in IRP were too far below potential study targets
OPUC required PGE to develop a DR review committee and select potential areas for a DR testbed
Objective of testbed was to inform DR planning, accelerate DR implementation, and drive market maturity
Notes: Role of DR review committee - Assist PGE staff with Test Bed development decisions, program development decisions, budget development, communication of the project, identifying costs and benefits for customers, PGE, the region and the Commission.

## Slide 75: DR Testbed Hypotheses to Test
Can customers be recruited in sufficient numbers to achieve more significant peak demand offsets and renewable integration cost benefits?
Forecast ultimate penetration and time periods to achieve them?
Will customers who sign up for DLC programs accept it being dispatched with the frequency and duration needed to achieve substantial reductions in peak loads for the system as a whole or local T&D systems?
Do pricing-based programs mitigate mandatory dispatch issues for consumers?
Do portfolios of DR offerings increase recruiting?
How much more cost effective is DR, and what level of increased penetration rate can be achieved, by programs targeting new buildings?
Replacement programs, working with supply chain partners.
Regional branding program.
Joint EE/DR programs.
Determine the level of customer service staff and program operating staff needed?

## Slide 76
From PGE 2019 Smart Grid Report Update to Oregon PUC July 2019

## Slide 77: Portland General Electric DR Test Bed
2.5 year pilot; $5.9 million; funded through deferral and R&D funds
Program is evolving from behavioral demand response of Peak Time Rebate (PTR) to direct load control (DLC)
Opt-Out Peak-Time Rebate – 16,000 participants; ~3% unenrollments
Optional Direct Load Control offerings
  Heat pump water heater control research, testing customer-hosted Wi-Fi, cellular LTE, and radio frequency mesh network;
  Ductless mini-split controls, in collaboration with the Energy Trust to better understand how energy efficiency and demand response can be “stacked”
  A solar smart inverter for flexible grid services
  EV chargers
  A “whole house” bring your own device pilot where customers may enroll and manage multiple appliances with one platform.
Testing recruitment messaging:
  Monetary, giving back, carbon, renewable energy
Notes: With peak-time rebate, PGE pays a $/kWh to customers relative to a pre-established baseline; no negative repercussions if they don’t participate.

## Slide 78: Other Considerations for the NW
Peak concerns in the Northwest aren’t the same as peak issues in other systems because of the hydro system
Northwest peaks may last 3-5 consecutive days and occur every five years; not typical hot or cold weather annual “needle peaks”
Northwest peaks stem from extreme weather/demand during a low water year at a time when reservoirs are filling slowly (can be summer or winter)
Library of Congress/Corbis/VCG via Getty Images
Notes: Growing capacity problem in the Northwest isn’t the typical needle peak (hydro can solve this)
Two flavors of peak:
  Hot summer day where DR is cheaper than buying on the market
  Adequacy problems in the region and DR is there
Hydro does a good job solving the “needle peak” from a super hot day.
Key time of concern is where reservoirs don’t refill in the summer and winter
Not a yearly occurrence; may happen once every five years, in winter or summer
Longer and more protracted problems in winter, than a typical summer needle peak.
Two different flavors of peak: hot summer day where it is cheaper than buying on the market or adequacy problems in the region and DR is there. 7th Plan showed some winter adequacy issues . With climate change and more summer problems than winter problems, aligns with niche of more traditional demand response

## Slide 79: Other Considerations for the NW, cont.
What does this mean for demand response potential studies and programs?
Each utility is unique; Understanding the exact nature of a utility’s peak problem will help define the type of DR that can help solve it
Individual utilities need to look at nature of their particular peak(s) of concern
Key question for utilities to ask: What is the specific problem I am trying to solve with my DR?
  Identify where peak problems are and how long they last
  Identify exactly why are they short? (hydro, forced outages, natural gas storage)
To identify peak issues, need models that run hourly and chronologically
In modeling, need to evaluate water and weather stochastically
Deterministic models will not reveal the need and potential value of DR
Typical consultant studies may not pick up the nuance of NW peak needs and opportunities if methodology used elsewhere is simply replicated
Notes: Growing capacity problem in the Northwest isn’t the typical needle peak (hydro can solve this)
Two flavors of peak:
  Hot summer day where DR is cheaper than buying on the market
  Adequacy problems in the region and DR is there
Hydro does a good job solving the “needle peak” from a super hot day.
Key time of concern is where reservoirs don’t refill in the summer and winter
Not a yearly occurrence; may happen once every five years, in winter or summer
Longer and more protracted problems in winter, than a typical summer needle peak.
Two different flavors of peak: hot summer day where it is cheaper than buying on the market or adequacy problems in the region and DR is there. 7th Plan showed some winter adequacy issues . With climate change and more summer problems than winter problems, aligns with niche of more traditional demand response

## Slide 80: Insurance Perspective
In the Northwest Power and Conservation Council’s 7th Power Plan, models selected DR almost as an insurance product; DR was deployed as if it were operating reserves in the model
The big risk in the NW is the hydro risk; in a bad hydro year, DR can help
The second worst hydro year on record was 2001, the year of the CA Energy Crisis; lack of available hydro was a major contributor to the crisis
In a bad hydro year with a forced outage and high load event, DR would be very valuable
  This type of value is revealed through stochastics
Utilities and the WUTC could develop a consistent methodology that each utility could incorporate into their own models
For smaller utilities, a simplified approach could be established
Notes: Traditionally, BPA has been the insurance for the region.
Don’t want to wait until the need is upon us. The story of the trapper that said it’s not cold yet, so he didn’t cut any wood and then he froze to death.
Black swan events happen.
Stochastic analysis and hydro risk: UTC can require DR be considered in this way. Good for utilities and regulators to discuss this. Sometimes “insurance” products aren’t popular with regulators.
Example: World’s biggest lithium ion battery (100 MW/129 MWh) in Australia recouped its $67 million capital costs in two years due to tornado that took down transmission lines while savings customers $100 million

## Slide 81: DR and Markets
Some utilities don’t need capacity now – hard to justify spending $$ on DR
Explore opportunities for DR to be offered in a market between IOUs
What about using DR to free up generation that could be bid into the EIM?
What about DR opportunities in resilience hubs and ecodistricts?
Meanwhile, you have that DR resource that one day you really need!
While DR is relatively new in the Northwest, that’s not the case everywhere.
  Large DR programs bid into PJM and New England ISO forward capacity markets
  At times, upwards of 70% of market is being met by DR
  Verification requirements exist
Day-ahead notification products are cheaper than 15-minute, hour-ahead or real-time products; in planning and procurement, utilities should consider the right product to get the job done at least cost

## Slide 82: Other Value Streams to Consider
Savings to distribution, transmission, and generations systems, including avoided losses or non-wires alternatives
Temporal and locational aspects of value
Value associated with interactions with other grid resources and other DERs
Account for benefits across full effective useful life of the resource
Insurance/risk reduction value
Emissions avoidance value
Opportunities related to increased technology or service-based customer engagement
Recent Tom Eckman and LBNL report: Determining Utility System Value of Demand Flexibility from Grid-Interactive Efficient Buildings
Notes: Customers want what they want. They want choices and in some areas technology and engagement through technology is key. This could in some ways limit future risks associated with community choice/ municipal aggregation models.
Could be capital investment opportunities for utilities.
Utility DR needs are very utility specific. Consistency with methodology rather than results, Incoproate and use it to the best of their models’ abilty to use it.

## Slide 83: Resources
In 2019 Regional Technical Forum Demand Response Subcommittee looked at demand response equipment and technical feasibility for:
  Commercial lighting controls
  Residential water heaters
  Connected thermostats
  EV battery chargers
  Irrigation pump controls
  Refrigeration controls

## Slide 84: Demand Response in Hawaii and Massachusetts
Dhruv Bhatnagar
June 8, 2019
Washington Utilities and Transportation Commission
Stakeholder Meeting on Demand Response

## Slide 85: Existing Demand Response: EnergyScout
Large Customers
42 customers, ~12 MW
Technology: diesel generators, HVAC
Dispatch, 1 hr. notification, underfrequency load shed at 59.5 Hz
Facility’s EMS carries out the predetermined directives
Utility sends an alert via a 3rd party paging service
One-way paging
Load Control Receiver receives the alert
LCR
EnergyScout Program
EMS
3rd party
paging service
Programs are dispatched by system operations on a frequent basis, ~ 1-4 dispatch events per month
Small & Medium Business
200 customers, ~1 MW
Technology: HVAC
Dispatch, 1 hr. notification, and underfrequency load shed at 59.7 Hz
Residential
30,000 customers, ~8 MW
Technology: electric water heaters
Dispatch, notification at time of event, and underfrequency load shed at 59.7 Hz

## Slide 86: Existing Demand Response: FastDR
Fast DR “Pilot”
  ~7 MW, 38 customers subscribed
  Technology: largely backup generation, 2 energy storage participants, some customers are just HVAC response
  Responsive to
    Under-frequency load shed (59.7Hz)
    10 minute utility dispatch
Fast DR Pilot (10 min reserve)
OpenADR 2.0b gateway device receives the alert
Facility’s EMS carries out the predetermined directives
EMS
Gateway
Utility sends an alert via Internet
3rd party OpenADR 2.0b
VTN

## Slide 87: Grid-Interactive Water Heater
Grid-Interactive Water Heater (GIWH): is a “thermal battery” for storing energy, having the ability to follow locational marginal pricing, providing fast regulation service and better integrating renewable energy, thereby effectively reducing the carbon footprint of the appliance. (Source: PLMA GIWH Interest Group)
Notes: HECO, the use case is to evaluate the effectiveness of residential water heater controllers for providing grid services such as frequency regulation and under-frequency response. In order to explore this capability, HECO deployed 499 electric resistance water heaters with grid-interactive controllers at an apartment complex. This provided a large demonstration group with which to explore the effectiveness and limitations of a grid-interactive water heating technology.
a field evaluation of frequency regulation and a lab evaluation of under-frequency response
electric resistance 50-gallon tanks that were retrofitted by Steffes with advanced sensing and control technology. A mixing valve was installed to allow the water heater to increase the internal temperature up to 150°F

## Slide 88: GIWH Regulation: Test 18: 8 hours (“Bad” day)

## Slide 89: Under Frequency Response (UFR) Laboratory Testing for Water Heater Controllers
The under-frequency response (UFR) test is designed to determine how accurately a load controller turns off a load in response to an under-frequency event.
The controller must monitor the frequency locally at the device-level and respond autonomously without connection to the internet
UFR Testing Conducted by EPRI

## Slide 90: Controller Testing Results
Steffes (GIWH):
Performed as intended, average frequency of past 10 cycles was exactly 59.700 Hz.
The controller ramped the load back up to full output over the course of 1-2 minutes once the frequency returned to 60 Hz
Mosaic Power (controller):
Performed as intended, average frequency of past 12 cycles from shutoff was 59.687 Hz
The controller turned the load back on after 30 minutes
14,000 water heaters providing frequency regulation in PJM
Shifted Energy (controller):
Performed as intended, average frequency of past 12 cycles from shutoff was 59.685 Hz
The controller turned the load back on after a set amount of time once the frequency returned 60.0 Hz
Source: Angela Cheung, EPRI

## Slide 91: New Integrated DR Portfolio: Hawaiian Electric Grid Services
Capacity (Load Reduction and Load build)
  Load Build: 10:00AM – 2:00PM, 8 hr. notification
  Load Reduction: 5:00PM – 9:00PM, 10 min. notification
Fast Frequency Response (FFR)
  Autonomously triggered due to an under frequency excursion
  Trigger: 59.7Hz, 12 cycle response
Regulating Reserve/Regulation (secondary frequency regulation)
  Response to a set-point regulation signal (AGC: automatic generation control)
Replacement Reserve
  10-30 minute response after notification, 1-2 hour duration

## Slide 92: Grid Service Participation Paths
Hawaiian Electric Companies’ Programs
Aggregators (third-party)
Self-Aggregators
Programs offered directly to customers through a Utility Tariff
Contract directly with aggregators.
Third Party recruits and contracts with customers to operate customer loads in a “Portfolio”
Contract directly with Hawaiian Electric.
Utility negotiate directly with customer for delivery of services at large or multiple site facilities
Customer wanting turn-key services as part of larger group in portfolio
Options Now
Future Additions
For professionally managed customers providing more control and greater total financial incentive
Alternate contracting path to directly participate in a Utility Tariff
Notes: Grid Service Type
Oahu
~1,200 MW Peak
Maui
~200 MW Peak
Fast Frequency Response
36 MW
0
Capacity (Load Reduction)
44 MW
9.8 MW
Capacity (Load Build)
44 MW
8.9 MW

## Slide 93: Initial Targets for Grid Services
Aggregators will be utilized to achieve the target levels starting 2019 and contract committed until 2023 under a standard form Grid Services Purchase Agreement
Self-aggregators will also be utilized to achieve these target levels
As necessary, utilities will deploy their own programs
All programs are intended to be technology neutral: water heaters, HVAC, building controls, pumps, batteries, existing distributed generation, electric vehicles etc.
Grid Service Type | Oahu ~1,200 MW Peak | Maui ~200 MW Peak
Fast Frequency Response | 36 MW | 0
Capacity (Load Reduction) | 44 MW | 9.8 MW
Capacity (Load Build) | 44 MW | 8.9 MW

## Slide 94: Massachusetts DR: ISO
ISO-NE Active Demand Resource Program
Resources that are actively dispatched by the ISO when needed. Example: powering down an energy-intensive machine to comply with a dispatch instruction.
These resources are fully integrated into the ISO-NE energy, capacity, and reserve markets.
Load reduction is offered in the day-ahead market and dispatched in real-time
ISO-NE Passive Demand Resource Programs
Non-dispatchable resources that provide energy efficiency and save electricity over time. Example: Solar array generating electricity for a facility.
On-Peak Resources: Incentivized for energy saved during summer and winter peak load hours (1-5 p.m. Summer and 5-7 p.m. Winter)
Seasonal-Peak resources: Incentivized for energy saved during summer and winter weekdays when the real-time system hourly load is equal to or greater than 90% of the most recent system peak 50/50 load forecast for the applicable season.
Parameter | Value
Minimum Size | 100 kW
Participation Months | Summer (Jun-Nov) & Winter (Dec-Mar)
Required Availability | 24/7 during applicable months + two 1-hour performance tests each year
Incentive | $/kW monthly incentive for availability based on Forward Capacity Market $/kWh for actual performance at real-time energy market prices.
Eligible Participants | Distributed dispatchable generation or load curtailment
Parameter | Value
Minimum Size | 100 kW load reduction
Participation Months | Summer (Jun-Nov, April-May) & Winter (Dec-Mar)
Incentive | $/kW monthly payment based on Forward Capacity Market and demonstrated load reduction.
Eligible Participants | Energy efficiency projects and distributed generation that contributes to load reduction
https://cpowerenergymanagement.com/wp-content/uploads/2019/02/ISONE_Snapshots_22719.pdf

## Slide 95: MA: Mass Save and ConnectedSolutions
Integration of MA energy efficiency (Mass Save) program with demand response
  Residential and small business: existing EE program administrator sales teams
  C&I: EE program administrator sales teams and third-party curtailment service providers (C&I) to sign customers up for DR
Funding: energy efficiency surcharge (bill surcharge)
Energy efficiency measures installed as a function of Mass Save are eligible for DR participation (previously installed and co-marketing to new participants)
  Smart thermostats can receive enrollment ($25) and annual participation ($20) incentives to allow program administrators (the distribution utilities) control during peak hours
  Higher incentives for energy storage participation (can be partially funded through the EE HEAT loan) Summer and winter

## Slide 96: Massachusetts DR (cont.)
Energy suppliers in MA (National Grid, Eversource, Unitil, and Cape Light Compact) offer Connected Solutions to their customers - a collection of residential and commercial DR programs.
Battery Program
Thermostat Program
Performance Incentive | $25 instant, $20 annual
Events per Summer | 15 on average, 3 hours each
Months Events can Occur | June through September
Time Discharge Events Can Occur | 2 p.m. to 7 p.m.
https://www.nationalgridus.com/MA-Home/Connected-Solutions/ConnectedSolutions
EV Charger Program (Eversource only)
Performance Incentive | $150 instant, $50/annual for 3 year commitment
Participating in both the Summer and Winter programs can count towards the Solar Massachusetts Renewable Target (SMART) program’s full cycle equivalent dispatch requirement in order to obtain additional battery adder incentives within the SMART program.
Residential Programs:
For Cape Light Compact customers there is an additional $65/kw-summer to the Targeted Dispatch Summer incentive and $25/kW-winter for Targeted Dispatch Winter Incentive for using battery storage.
Commercial & Industrial Programs
https://www.nationalgridus.com/media/pdfs/bus-ways-to-save/connectedsolutions-ciprogrammaterials.pdf

## Slide 97: Baltimore Gas & Electric: Peak Time Rebate
Smart Energy Rewards Program (peak time rebate)
  Automatic enrollment, customers receive a notification (day before) an event to reduce load
  Rewarded with an incentive of $1.25/kWh
  Savings are monetized in the PJM Energy and Capacity markets
BGE estimated $93M of avoided transmission capital expenditures and $72M of avoided distribution capital expenditures as a result of the SER program from 2013 to 2015
Source: AEE Institute https://info.aee.net/hubfs/MD%20DR%20Final.pdf

## Slide 98: Thank You
Dhruv Bhatnagar
dhruv.bhatnagar@pnnl.gov

## Slide 99: Demand Response
The Smart Electric Power Alliance has adopted the following working definition for demand response:
  Changes in the electric load—such as reductions, increases, or shifts—by end-use customers from their normal consumption patterns in response to specific market or system conditions. Such conditions could include time-varying changes in the cost of producing energy, shortages of distribution, transmission, or generation capacity, or unusually high or low voltage or frequency.
  This could also be customer generation (export beyond a customer’s load)
Utility DR Offerings in the United States (2017 SEPA/Navigant Survey):
  41% of utilities offer AC switch programs
  16% offer water heater programs
  24% of utility respondents offer thermostat programs
  9% offer behavioral programs to their residential customers

## Slide 100: General Trends from HPWH Pilot

## Slide 101: Results: Single Day Example
Chart: All Groups, Single Day (Feb 19th, 2018)
| 43150 | 43150.041666666664 | 43150.083333333336 | 43150.125 | 43150.166666666664 | 43150.208333333336 | 43150.25 | 43150.291666666664 | 43150.333333333336 | 43150.375 | 43150.416666666664 | 43150.458333333336 | 43150.5 | 43150.541666666664 | 43150.583333333336 | 43150.625 | 43150.666666666664 | 43150.708333333336 | 43150.75 | 43150.791666666664 | 43150.833333333336 | 43150.875 | 43150.916666666664 | 43150.958333333336
HPWH Event | 110.5533 | 67.402 | 53.0507 | 39.2244 | 31.9893 | 98.1684 | 12.239 | 37.8085 | 170.3463 | 621.5101 | 396.1855 | 287.1966 | 300.5524 | 318.4068 | 172.9401 | 332.438 | 345.2157 | 96.5632 | 67.8813 | 128.8227 | 572.7679 | 356.6569 | 248.5784 | 200.2012
HPWH Control | 81.7868 | 101.6672 | 125.8221 | 126.7995 | 97.1165 | 47.8723 | 173.0897 | 260.3993 | 338.2805 | 322.5191 | 226.2657 | 299.4932 | 282.5509 | 231.5263 | 243.3947 | 280.3438 | 244.9069 | 307.01 | 262.0712 | 363.3794 | 341.7209 | 261.9133 | 245.7495 | 145.2244
ERWH Event | 148.4127 | 25 | 96.7918 | 145.6349 | 223.4127 | 454.2709 | 58.7121 | 61.2591 | 193.0993 | 1141.7933 | 534.6552 | 669.5833 | 529.5833 | 332.8947 | 445.8333 | 503.3333 | 670.4167 | 348.75 | 293.7088 | 480.303 | 1235.6061 | 307.9545 | 538.0435 | 428.0303
ERWH Control | 69.2308 | 341.6667 | 178.8462 | 161.5385 | 66.3462 | 28.8462 | 524.0385 | 258.0128 | 448.8375 | 716.721 | 942.3077 | 1128.3681 | 1289.4231 | 1103.8239 | 827.7903 | 1001.823 | 815.6667 | 766.3136 | 1075 | 807.8661 | 872.3333 | 742.0269 | 580.6919 | 543.3333
Low energy use by all groups at night
Grey bars = shed events

## Slide 102: Single Day Example
Chart: All Groups, Single Day (Feb 19th, 2018)
| 43150 | 43150.041666666664 | 43150.083333333336 | 43150.125 | 43150.166666666664 | 43150.208333333336 | 43150.25 | 43150.291666666664 | 43150.333333333336 | 43150.375 | 43150.416666666664 | 43150.458333333336 | 43150.5 | 43150.541666666664 | 43150.583333333336 | 43150.625 | 43150.666666666664 | 43150.708333333336 | 43150.75 | 43150.791666666664 | 43150.833333333336 | 43150.875 | 43150.916666666664 | 43150.958333333336
HPWH Event | 110.5533 | 67.402 | 53.0507 | 39.2244 | 31.9893 | 98.1684 | 12.239 | 37.8085 | 170.3463 | 621.5101 | 396.1855 | 287.1966 | 300.5524 | 318.4068 | 172.9401 | 332.438 | 345.2157 | 96.5632 | 67.8813 | 128.8227 | 572.7679 | 356.6569 | 248.5784 | 200.2012
HPWH Control | 81.7868 | 101.6672 | 125.8221 | 126.7995 | 97.1165 | 47.8723 | 173.0897 | 260.3993 | 338.2805 | 322.5191 | 226.2657 | 299.4932 | 282.5509 | 231.5263 | 243.3947 | 280.3438 | 244.9069 | 307.01 | 262.0712 | 363.3794 | 341.7209 | 261.9133 | 245.7495 | 145.2244
ERWH Event | 148.4127 | 25 | 96.7918 | 145.6349 | 223.4127 | 454.2709 | 58.7121 | 61.2591 | 193.0993 | 1141.7933 | 534.6552 | 669.5833 | 529.5833 | 332.8947 | 445.8333 | 503.3333 | 670.4167 | 348.75 | 293.7088 | 480.303 | 1235.6061 | 307.9545 | 538.0435 | 428.0303
ERWH Control | 69.2308 | 341.6667 | 178.8462 | 161.5385 | 66.3462 | 28.8462 | 524.0385 | 258.0128 | 448.8375 | 716.721 | 942.3077 | 1128.3681 | 1289.4231 | 1103.8239 | 827.7903 | 1001.823 | 815.6667 | 766.3136 | 1075 | 807.8661 | 872.3333 | 742.0269 | 580.6919 | 543.3333
Event groups use less energy during shed event

## Slide 103: Single Day Example
Chart: All Groups, Single Day (Feb 19th, 2018)
| 43150 | 43150.041666666664 | 43150.083333333336 | 43150.125 | 43150.166666666664 | 43150.208333333336 | 43150.25 | 43150.291666666664 | 43150.333333333336 | 43150.375 | 43150.416666666664 | 43150.458333333336 | 43150.5 | 43150.541666666664 | 43150.583333333336 | 43150.625 | 43150.666666666664 | 43150.708333333336 | 43150.75 | 43150.791666666664 | 43150.833333333336 | 43150.875 | 43150.916666666664 | 43150.958333333336
HPWH Event | 110.5533 | 67.402 | 53.0507 | 39.2244 | 31.9893 | 98.1684 | 12.239 | 37.8085 | 170.3463 | 621.5101 | 396.1855 | 287.1966 | 300.5524 | 318.4068 | 172.9401 | 332.438 | 345.2157 | 96.5632 | 67.8813 | 128.8227 | 572.7679 | 356.6569 | 248.5784 | 200.2012
HPWH Control | 81.7868 | 101.6672 | 125.8221 | 126.7995 | 97.1165 | 47.8723 | 173.0897 | 260.3993 | 338.2805 | 322.5191 | 226.2657 | 299.4932 | 282.5509 | 231.5263 | 243.3947 | 280.3438 | 244.9069 | 307.01 | 262.0712 | 363.3794 | 341.7209 | 261.9133 | 245.7495 | 145.2244
ERWH Event | 148.4127 | 25 | 96.7918 | 145.6349 | 223.4127 | 454.2709 | 58.7121 | 61.2591 | 193.0993 | 1141.7933 | 534.6552 | 669.5833 | 529.5833 | 332.8947 | 445.8333 | 503.3333 | 670.4167 | 348.75 | 293.7088 | 480.303 | 1235.6061 | 307.9545 | 538.0435 | 428.0303
ERWH Control | 69.2308 | 341.6667 | 178.8462 | 161.5385 | 66.3462 | 28.8462 | 524.0385 | 258.0128 | 448.8375 | 716.721 | 942.3077 | 1128.3681 | 1289.4231 | 1103.8239 | 827.7903 | 1001.823 | 815.6667 | 766.3136 | 1075 | 807.8661 | 872.3333 | 742.0269 | 580.6919 | 543.3333
Large peak reduction
with connected ERWH

## Slide 104: Single Day Example
Chart: All Groups, Single Day (Feb 19th, 2018)
| 43150 | 43150.041666666664 | 43150.083333333336 | 43150.125 | 43150.166666666664 | 43150.208333333336 | 43150.25 | 43150.291666666664 | 43150.333333333336 | 43150.375 | 43150.416666666664 | 43150.458333333336 | 43150.5 | 43150.541666666664 | 43150.583333333336 | 43150.625 | 43150.666666666664 | 43150.708333333336 | 43150.75 | 43150.791666666664 | 43150.833333333336 | 43150.875 | 43150.916666666664 | 43150.958333333336
HPWH Event | 110.5533 | 67.402 | 53.0507 | 39.2244 | 31.9893 | 98.1684 | 12.239 | 37.8085 | 170.3463 | 621.5101 | 396.1855 | 287.1966 | 300.5524 | 318.4068 | 172.9401 | 332.438 | 345.2157 | 96.5632 | 67.8813 | 128.8227 | 572.7679 | 356.6569 | 248.5784 | 200.2012
HPWH Control | 81.7868 | 101.6672 | 125.8221 | 126.7995 | 97.1165 | 47.8723 | 173.0897 | 260.3993 | 338.2805 | 322.5191 | 226.2657 | 299.4932 | 282.5509 | 231.5263 | 243.3947 | 280.3438 | 244.9069 | 307.01 | 262.0712 | 363.3794 | 341.7209 | 261.9133 | 245.7495 | 145.2244
ERWH Event | 148.4127 | 25 | 96.7918 | 145.6349 | 223.4127 | 454.2709 | 58.7121 | 61.2591 | 193.0993 | 1141.7933 | 534.6552 | 669.5833 | 529.5833 | 332.8947 | 445.8333 | 503.3333 | 670.4167 | 348.75 | 293.7088 | 480.303 | 1235.6061 | 307.9545 | 538.0435 | 428.0303
ERWH Control | 69.2308 | 341.6667 | 178.8462 | 161.5385 | 66.3462 | 28.8462 | 524.0385 | 258.0128 | 448.8375 | 716.721 | 942.3077 | 1128.3681 | 1289.4231 | 1103.8239 | 827.7903 | 1001.823 | 815.6667 | 766.3136 | 1075 | 807.8661 | 872.3333 | 742.0269 | 580.6919 | 543.3333
Larger peak reduction when switching to (“dumb”) HPWH

## Slide 105: Single Day Example
Chart: All Groups, Single Day (Feb 19th, 2018)
| 43150 | 43150.041666666664 | 43150.083333333336 | 43150.125 | 43150.166666666664 | 43150.208333333336 | 43150.25 | 43150.291666666664 | 43150.333333333336 | 43150.375 | 43150.416666666664 | 43150.458333333336 | 43150.5 | 43150.541666666664 | 43150.583333333336 | 43150.625 | 43150.666666666664 | 43150.708333333336 | 43150.75 | 43150.791666666664 | 43150.833333333336 | 43150.875 | 43150.916666666664 | 43150.958333333336
HPWH Event | 110.5533 | 67.402 | 53.0507 | 39.2244 | 31.9893 | 98.1684 | 12.239 | 37.8085 | 170.3463 | 621.5101 | 396.1855 | 287.1966 | 300.5524 | 318.4068 | 172.9401 | 332.438 | 345.2157 | 96.5632 | 67.8813 | 128.8227 | 572.7679 | 356.6569 | 248.5784 | 200.2012
HPWH Control | 81.7868 | 101.6672 | 125.8221 | 126.7995 | 97.1165 | 47.8723 | 173.0897 | 260.3993 | 338.2805 | 322.5191 | 226.2657 | 299.4932 | 282.5509 | 231.5263 | 243.3947 | 280.3438 | 244.9069 | 307.01 | 262.0712 | 363.3794 | 341.7209 | 261.9133 | 245.7495 | 145.2244
ERWH Event | 148.4127 | 25 | 96.7918 | 145.6349 | 223.4127 | 454.2709 | 58.7121 | 61.2591 | 193.0993 | 1141.7933 | 534.6552 | 669.5833 | 529.5833 | 332.8947 | 445.8333 | 503.3333 | 670.4167 | 348.75 | 293.7088 | 480.303 | 1235.6061 | 307.9545 | 538.0435 | 428.0303
ERWH Control | 69.2308 | 341.6667 | 178.8462 | 161.5385 | 66.3462 | 28.8462 | 524.0385 | 258.0128 | 448.8375 | 716.721 | 942.3077 | 1128.3681 | 1289.4231 | 1103.8239 | 827.7903 | 1001.823 | 815.6667 | 766.3136 | 1075 | 807.8661 | 872.3333 | 742.0269 | 580.6919 | 543.3333
Even greater peak load reduction with connected HPWH

## Slide 106: Full Season Results
Average Hourly Peak (Watts) during Shed Events per Water Heater
Average Peak Reduction from Baseline (Watts Reduced) during Shed Events Per Water Heater
 | ERWH (Baseline) | Connected ERWH | HPWH | Connected HPWH
Winter Morning | 616 | 242 | 306 | 83
Winter Evening | 668 | 348 | 232 | 66
Summer Evening | 474 | 127 | 109 | 26
 | ERWH (Baseline) | Connected ERWH | HPWH | Connected HPWH | %Reduced Compared to Baseline
Winter Morning | 616 | 374 | 310 | 533 | 87%
Winter Evening | 668 | 321 | 437 | 602 | 90%
Summer Evening | 474 | 347 | 365 | 448 | 95%

## Slide 107: Total Energy Shifted
Season | HPWH Energy Shifted Per Event (Wh) | Average Event Length (Hours) | ERWH Energy Shifted Per Event (Wh) | Average Event Length (Hours)
Winter | 300 | 2 | 600 | 2
Spring | 250 | 2 | 1050 | 2
Summer | 350 | 4 | 1300 | 4
Approximate Energy Shifted During Peak Afternoon Hours (Average of Baselines, Rounded to the Nearest 50 W, Multiplied by the Average Number of Hours per Event for that Season)

## Slide 108
Winter Peak Load Reduction | ER BL (W/Hour of DR Event) | ER BL – ER with DR (W/Hour of DR Event) | ER BL – HPWH Control (W/Hour of DR Event) | ER BL – HPWH with DR (W/Hour of DR Event) | % Savings for Switching to HPWH with DR (W)
Morning Peak | 616 | 374 | 310 | 533 | 87%
Evening Peak | 668 | 321 | 437 | 602 | 90%
~90% of evening peak load power can be reduced by switching from uncontrolled ERWHs to Connected HPWHs
Reduced Risk for Utilities, Reduced Cost to Consumers
Acronyms: ER = electric resistance, BL= Baseline, W = watt, DR = demand response, CI = confidence interval, ERWH = electric resistance water heater, HPWH = heat pump water heater
Notes: 66% can be eliminated by just switching to HPWHs.

## Slide 109
Winter Peak Load Reduction | ER BL (W/Hour of DR Event) | ER BL – ER with DR (W/Hour of DR Event) | ER BL – HPWH Control (W/Hour of DR Event) | ER BL – HPWH with DR (W/Hour of DR Event) | % Savings for Switching to HPWH with DR (W)
Morning Peak | 616 | 374 | 310 | 533 | 87%
95% CI for Morning Peak | 85 | 79 | 83 | 84 | N/A
Evening Peak | 668 | 321 | 437 | 602 | 90%
95% CI for Evening Peak | 57 | 77 | 65 | 58 | N/A
~90% of evening peak load power can be reduced by switching from uncontrolled ERWHs to Connected HPWHs
Reduced Risk for Utilities, Reduced Cost to Consumers
Acronyms: ER = electric resistance, BL= Baseline, W = watt, DR = demand response, CI = confidence interval, ERWH = electric resistance water heater, HPWH = heat pump water heater
Notes: 66% can be eliminated by just switching to HPWHs.

## Slide 110: Average kW Reduction During Shed Events (for each water heater type)
Many ways to determine the average kW reduction
  Baseline 1: Event Group vs. Control Group
  Baseline 2: Prior- Week Baseline
  Baseline 3: Full Season Baseline
Chart: Baseline 1: Event Group vs. Control Group
Unpredictable behavior is expected in this baseline

## Slide 111
Many ways to determine the average kW reduction
  Baseline 1: Event Group vs. Control Group
  Baseline 2: Prior- Week Baseline
  Baseline 3: Full Season Baseline
Chart: Baseline 2: Prior-Week Baseline
Unpredictable behavior is averaged out in this baseline
Weekend days
Average kW Reduction During Shed Events (for each water heater type)

## Slide 112: Average kW Reduction During Shed Events (For each water heater type)
Many ways to determine the average kW reduction
  Baseline 1: Event Group vs. Control Group
  Baseline 2: Prior- Week Baseline
  Baseline 3: Full Season Baseline
Chart: Baseline 3: Full Season Baseline
Baseline 3 trends toward a typical hot water load profile
Event

## Slide 113: kW Reduction Using All Shed Events
 | Heat Pump Water Heaters (n=145) |  |  | Electric Resistance (n=86) |  | 
Baseline # | Base 1 | Base 2 | Base 3 | Base 1 | Base 2 | Base 3
Average Impact from 10pm to 5am | 84 | 95 | 84 | 133 | 146 | 194
Std. Dev.1 from 10pm to 5am | 34 | 25 | N/A2 | 81 | 59 | N/A
Average Impact from 6am to 10am | 201 | 196 | 232 | 337 | 318 | 444
Std. Dev. from 6am to 10am | 45 | 45 | N/A | 67 | 121 | N/A
Average Impact from 11am to 4pm | 170 | 148 | N/A3 | 322 | 329 | N/A
Std. Dev. from 11am to 4pm | 47 | 29 | N/A | 114 | 133 | N/A
Average Impact from 5pm to 9pm | 142 | 161 | 167 | 328 | 312 | 316
Std. Dev. from 5pm to 9pm | 47 | 46 | N/A | 85 | 99 | N/A
1. Standard deviation provides information about the variation of the average impact between the 10 weeks studied in the season
2.Only the last week of the season is part of this event group
3. No events occurred during this time for the week of March 26th

## Slide 114: Recovery Time/Energy: HPWH
Challenges
  Unknown recovery energy associated with draws during shed period
  Unknown recovery energy associated with draws during recovery period
Orange Region = the Load Up Period, Grey Region = the Shed Period

## Slide 115: Recovery Time/Energy: ERWH
Challenges
  Unknown recovery energy associated with draws during shed period
  Unknown recovery energy associated with draws during recovery period
Orange Region = the Load Up Period, Grey Region = the Shed Period

## Slide 116: Stakeholder Discussion
For new topics: “Raise hand – Topic”
For responses to current topic: “Raise hand – Response”
Raise hand – Topic
Raise hand – Response
Raise hand – Response
Raise hand – Topic

## Slide 117: Discussion Questions on DR Potential
Identify the potential cost-effective demand response and load management programs that may be acquired in the integrated resource plan.
Which values of demand response are utilities currently incorporating into the IRP to identify cost-effective demand response?
What additional values need to be included to ensure all utility system costs and symmetrical nonutility impacts are accounted for?
Which values can be identified directly within the IRP modeling process and which need to be included in the demand response potential assessment?
What type and level of guidance around demand response potential assessments would be useful?

## Slide 118: Discussion Questions on DR Target Setting
Propose specific targets that pursue all cost-effective, reliable, and feasible demand response in the Clean Energy Implementation Plan.
Should DR targets in the CEIP be the same as the potential in the IRP? How should they be different?
How should DR pilots be treated in CEIP targets?
What type and level of guidance around setting demand response CEIP targets would be useful?

## Slide 119: Next Steps
Staff will:
Draft the next round of demand response rule language based on the information received during this workshop and in other written comments
Utilities will:
Identify DR potential in current IRP
Propose a DR target in the CEIP
Stakeholders will:
Provide comments about DR in the next round of CEIP and IRP rule language

## Slide 120: Thank You!
Jennifer Snyder
Regulatory Analyst
jennifer.snyder@utc.wa.gov