## Slide 1: Cascade Natural Gas Corporation 2016 Integrated Resource Plan Presentation to WUTC Commissioners and Stakeholders
Wednesday, March 29, 2017
WUTC
Olympia, WA

## Slide 2: AGENDA
  OPENING REMARKS
  PURPOSE OF IRP
  PROCESS FOLLOWED
  DEMAND FORECAST
  GAS SUPPLY OVERVIEW
  ENVIRONMENTAL CONSIDERATIONS
  AVOIDED COST
  DEMAND SIDE MANAGEMENT
  DISTRIBUTION SYSTEM PLANNING
  INTEGRATION RESULTS
  ADDITIONAL QUESTIONS

## Slide 3: Purpose of the IRP Process
Bruce Folsom
Bruce W Folsom Consulting LLC
March 29, 2017

## Slide 4: All Formal Explanations Aside…
The purpose of an IRP is to depict the overall company plan more transparently …
  For immediately-contemplated actions (i.e., in the next two years),
  To characterize emerging issues and related approaches for mitigation, if necessary, and
  To outline the long-term direction a company is headed vis-a-vis the industry, including economic trends, industry structure (partners such as the pipeline(s) and their impact/actions), technology, customer usage, etc.

## Slide 5: IRP Objectives
Present a transparent roadmap of the overall corporate plan per the previous slide
Promote internal coordination
Describe to key stakeholders and the public the complex utility system unique to the local distribution company and management decision-making processes
Provide previews of future projects and issues which can lead to improved regulatory filings
Meet regulatory requirements

## Slide 6: Benefits
A company can describe its unique circumstances, opportunities and challenges over the planning horizon
More specifically, while commissions do not approve the IRP—and, hence future actions—the description of potential actions generally provides for an improved process of future filings, because stakeholders have a basis, in advance, for what is driving those decisions

## Slide 7: In Conclusion
An IRP Provides an understanding of industry and utility-specific practices
That the Commission acknowledges the plans, rather than approve them, does not lessen the process’s regulatory importance
The commitment from Cascade’s senior leadership has been outstanding and recognized by stakeholders

## Slide 8: Process Followed

## Slide 9
IRP GUIDELINES AND CONTENT
WASHINGTON
IRP Guidelines from WUTC WAC 480-90-238
CASCADE’S PHILOSOPHY
Primary purpose of Cascade’s long-term resource planning process has been, and continues to be, to inform and guide the Company’s resource acquisition process, consistent with state regulatory requirements.
Input and feedback from the Company’s Technical Advisory Group (TAG) is an important resource to help ensure that CNGC’s IRP is developed from a broader perspective than Cascade could have on its own.
In response to the issues identified with the 2014 IRP, Cascade has strengthened its commitment to securing and supporting the appropriate internal and external resources necessary to work with all stakeholders to produce a 2016 Integrated Resource Plan that meets the requirements of Washington Administrative Code 480-90-238.

## Slide 10: Stakeholder Engagement Process
Input and feedback from Cascade’s Technical Advisory Group (TAG) is an important resource to help ensure the IRP includes perspectives external to the Company and is responsive to stake-holders.
Six TAG meetings were held in SeaTac and Kennewick.
Multiple opportunities for public participation were available.
Several walkthroughs of technical components (e.g SENDOUT® modeling) were conducted upon request.

## Slide 12
RESOLVING THE 2014 ISSUES WITH THE 2016 IRP
The lack of clear explanation of the timing of resource needs and how capacity deficits at specific city gates would be met (WAC 480-90-238(3)(g))
  CASCADE WORKED WITH STAKEHOLDERS TO CLEARLY IDENTIFY THE SPECIFIC TIMING, POTENTIAL EXCEPTIONS, AND METHOD OF DEALING WITH UPSTREAM PIPELINE CAPACITY DEFICITS AT DEMAND AREAS IN TAG 5 .
The lack of detailed load forecast information by class and state (WAC 480-90-238 (3)(a))
  DURING TAG 2, CASCADE WORKED WITH STAKEHOLDERS TO DEFINE THE SPECIFIC EXPECTATIONS FOR THIS ISSUE.
Insufficient analysis and explanation of conservation potential (WAC 480-90-238 (3)(b))
  CASCADE WORKED WITH STAKEHOLDERS DURING THE 2016 IRP PROCESS TO IDENTIFY STAFF’S SPECIFIC CONCERNS REGARDING THE INSUFFICIENT ANALYSIS AND EXPLANATION OF CONSERVATION POTENTIAL.

## Slide 13
RESOLVING THE 2014 ISSUES WITH THE 2016 IRP
The lack of a description of the company’s stakeholder engagement process (WAC-480-90-238(5))
  WITH THE PUBLICATION OF THE 2016 IRP, CASCADE HAS PROVIDED AN IMPROVED DESCRIPTION OF THE STAKEHOLDER PARTICIPATION PROCESS THROUGH INCLUSION OF TAG MEETING PRESENTATIONS, MINUTES AND RESPONSES TO COMMENTS.
Unclear explanation of the company’s risk management rationale and hedging strategy (WAC 480-90-238(3)(f))
  ON MARCH 13, 2017 CASCADE RECEIVED THE WUTC POLICY & INTERPRETIVE STATEMENT ON HEDGING (DOCKET UG-132019). CASCADE WILL BE WORKING WITH STAFF, STAKEHOLDERS AND OTHER LDCS ON HOW BEST TO IMPLEMENT THE EXPECTATIONS THE COMMISSION IDENTIFIED IN THE POLICY. THE COMPANY WILL CONTINUE TO PARTICIPATE IN ANY FUTURE UG-132019 ACTIVITIES. PER THE WUTC POLICY, CASCADE WILL PROVIDE THE COMPANY’S INITIAL HEDGING PLAN WITH THE FILING OF THE 2017 PGA
In addition to the above-listed rule requirements, the commission also identified a general lack of organization and presentation that made the plan difficult to read and understand
  CASCADE IS COMMITTED TO WORKING ON AN IMPROVED NARRATIVE TAKING INTO ACCOUNT COMMENTS MADE BY STAKEHOLDERS IN REFERENCE TO THE 2014 IRP. THE NARRATIVE IN THE 2016 IRP IS A SIGNIFICANT IMPROVEMENT.

## Slide 14
“Original” 2016 IRP TIMELINE
Date | Process Element | Location (Subject to change)
Thursday, June 09, 2016 | TAG 1 slides distributed to stakeholders | 
Thursday, June 16, 2016 | TAG 1: Process, Key Assumptions, IRP Team, Timeline, Latest Economic Indicators, Price Forecast and Demand Forecast, Plan for dealing with issues raised in 2014 IRP | 
Thursday, July 14, 2016 | TAG 2 slides distributed to stakeholders | 
Tuesday, July 19, 2016 | TAG 2: Drilling down into segments of demand forecast, Current Supply Resources, Transport Issues, Alternative Resources, Update on 2 Year Plan | Seattle Airport Conference Center
Friday, August 12, 2016 | TAG 3 slides distributed to stakeholders | 
Thursday, August 18, 2016 | TAG 3: Conservation, Distribution System Planning, Planned Scenarios and Sensitivities | Seattle Airport Conference Center
Thursday, September 08, 2016 | TAG 4 slides distributed to stakeholders | 
Thursday, September 15, 2016 | TAG 4: Preliminary Resource Integration Results, Avoided Costs, Proposed new 2 year Plan | Seattle Airport Conference Center
Tuesday, October 04, 2016 | TAG 5: Final Integration Results, finalization of plan components | Seattle Airport Conference Center
Monday, October 17, 2016 | Draft of 2016 IRP distributed | Kennewick, WebEx
Monday, November 07, 2016 | Comments due on draft from all stakeholders | 
Thursday, November 17, 2016 | TAG 6, if needed | Seattle Airport Conference Center
Wednesday, November 23, 2016 | Final IRP goes to press | 
Thursday, December 01, 2016 | Executive Summary Presentation to Senior Management | Kennewick, WebEx
Thursday, December 15, 2016 | IRP filing in Washington | 

## Slide 15: Demand Forecast

## Slide 16: Current Methodology – Flow Chart

## Slide 17: Forecast Model
The Company currently utilizes an ordinary least squares (OLS) regression to predict customer usage.
Cascade uses a 60 degree reference temperature to calculate HDDs.
Multiple scenarios are analyzed such as high/low growth, warm/cold weather, peak day events, etc.
Cascade analyzes 3 peak day events; average peak day, system-wide peak day, and max at each weather location peak day.
The Company utilizes an average year of demand with a system-wide peak event for deterministic analysis in SENDOUT®.

## Slide 20: Scenarios

## Slide 21: Peak Day Scenarios

## Slide 22
Cascade expects system load growth to be 1.25% per year, or 26.6% over the 20 year planning horizon.

## Slide 23
Usage expects to be approximately 308 million therms in 2017 and grow to just under 400 million therms in 2036.

## Slide 24: System Tariff Breakout

## Slide 25: Cascade Gas Supply Overview

## Slide 26
EXAMPLE OF POSSIBLE CNGC WINTER TRANSPORT CAPACITY FLOW

## Slide 27
Chart: Transport Summary
| AECO | KINGSGATE | STA 2 | NWP SUMAS/HUNT | NWP N OF GREEN | NWP S OF GREEN
 | 21973 | 46428 | 1000 | 137957 | 27292 | 36824

## Slide 28: Storage Resources
Jackson Prairie-
  4 accounts with 1,235,593 dths capacity
  CNGC cycled approximately 90% of Jackson Prairie storage over the past winter season
  CNGC remains committed to cycling Jackson Prairie
Plymouth-
  2 accounts with 662,200 dths capacity
  New account of 100,000 dths added for the upcoming season
  In addition to above we acquired TF-2 (Firm Redelivery Transportation) of 10,675 dths
  Plymouth returned to fully functional operation on 04/01/2016.
  CNGC remains committed to using Plymouth as a peaking resource.

## Slide 29: HIGHLIGHTS FOR THE 2016 PORTFOLIO DESIGN
PORTFOLIO PROCUREMENT DESIGN BASED ON A DECLINING PERCENTAGE EACH YEAR, ACCORDINGLY: Year 1: Approximately 80% of annual requirements; Year 2: 40%, Year 3: 20%.
  80% allows more flexibility operationally
  Allows us to be in the market monthly through FOM purchase or Day Gas purchases
Hedged Percentages (fixed-price physical) Currently max 40% of annual requirements. Second year should be set at 25%, and 20% hedged volumes for year three.
CNGC’s Gas Supply Oversight Committee (GSOC) would consider a modification of this plan if the outer year 3 year forward price is 20% higher/lower than the front month over a reasonably sustained period.
Annual load expectation (Nov-Oct) is approximately 30,000,000 dths, consistent with recent load history.

## Slide 30
Chart: TOTAL RFP's
| Nov16-Oct17 | Nov17-Oct18 | Nov18-Oct19 | TOTALS
NWP SUMAS/HUNT | 6380000 | 2656000 | 1509000 | 10545000
NWP N OF GREEN | 2860000 | 830000 | 720000 | 4410000
NWP S OF GREEN | 592000 | 457000 | 0 | 1049000
AECO | 1507500 | 2130000 | 905000 | 4542500
KINGSGATE | 1820000 | 155000 | 460000 | 2435000
STA 2 | 0 | 365000 | 0 | 365000

## Slide 31
Chart: RFP Percentage by Month
| Mar | Apr | May | Jun | Jul | Aug | Sep | Oct
Year 1 Percentage | 0 | 0 | 0 | 0.25286 | 0.19758 | 0.23519 | 0.14225 | 0.17212
3 yr Total | 0 | 0 | 0 | 6427500 | 6370000 | 5650000 | 2329000 | 2570000

## Slide 32
Chart: Percentage by Basin 2016 RFP + Current Supply
| AECO | KINGSGATE | STA 2 | NWP SUMAS/HUNT | NWP N OF GREEN | NWP S OF GREEN
 | 9097500 | 2435000 | 730000 | 17012500 | 6105500 | 1229000

## Slide 34
Chart: 
Current Supply | 56000
RFP Supply | 80000
FOM Spot Gas | 10000
SGS Storage | 56366
Daily Spot Gas | 10000
Peaking Deal | 20000
3rd Party Citygate | 10000
Pipeline Pack | 8156.07
LS Storage | 78125

## Slide 35: Environmental Considerations
Presented by Allison Spector
Mgr., Energy Efficiency Policy

## Slide 36: Purpose of Environmental Considerations
Demonstrates Cascade’s awareness of any legislation, policy, or rules that might impact the carbon scenarios modeled by the Company
  Discusses GHG policies mandated at the state and federal level that have the potential to impact Cascade as a natural gas distribution company, as well as presence of regional and national environmental regulations as required.
  Examines methodologies for applying a cost of carbon in the Company’s IRP planning efforts.
  Reports voluntary efforts to address GHG emissions.

## Slide 37: Regulations
IRP acknowledges presence of environmental rules and guidelines including:
  Clean Power Plan (CPP)
  Oregon’s “Coal to Clean” legislation (SB 1547)
  Washington Clean Air Rule (CAR) - WAC-173-422, and
  Northwest Power & Conservation Council's Seventh Power Plan
No direct impacts from electric rules, but were listed per previous UTC expectation
  Company incorporated Northwest Power & Conservation Council Plan’s survey of approaches, sensitivity analyses, and scenarios for modeling cost of carbon.
  CO2 costs used in modeling cost impacts with Carbon Cost Risk at $0 - $110/ton.

## Slide 38: Clean Air Rule (CAR)
On September 15, 2016, Washington Dept of Ecology issued the final CAR (WAC-173-442) to reduce GHG emissions
CAR requires GHG reductions from three classes of entities in Washington
  Stationary sources
  Natural gas distributors
    Indirect CO2 emissions from end-use customers’ combustion of natural gas
  Petroleum product producers in or importing to Washington
Cascade Natural Gas has an obligation to serve and will need to purchase emissions offsets for compliance with required emissions reductions:
  In-state emission reduction units (“ERUs”)
  Limited out-of-state allowances from states or provinces that have established multi-sector greenhouse gas programs (availability reduces over time)

## Slide 39: CAR (Cont.)
On September 27, 2016, and September 30, 2016, Cascade and three other natural gas distribution utilities jointly filed complaints in the United States District Court for the Eastern District of Washington and the State of Washington Thurston County Superior Court, respectively, challenging the legal underpinnings of CAR
  Ecology does not have authority to regulate non-emitting sources for their customers’ emissions
  Ecology does not have authority to implement a program to limit statewide greenhouse gas emissions, particularly a trading program based on ERUs

## Slide 40: CAR (Cont.)
In 2017, CAR is projected to cap CO2 emissions for Cascade at about 2 million metric tons – Cascade’s Baseline Emissions Value
  Baseline Emissions Value for Cascade is the annual average CO2 emissions from the combustion of natural gas supplied to end-use customers between 2012 and 2016
  Subtract out emissions from customers that are covered parties themselves
  Pending consultation with Ecology in 2017 on adjustment of EITE industry emissions responsibility in 2017-2019 compliance period
In 2018 to 2035, Cascade’s emissions reduction pathway decreases 1.7% each year from its baseline emissions value
In 2036 and beyond, the emissions reduction pathway is equivalent to 2035’s emission reduction pathway

## Slide 41
Cascade's Preliminary Emissions Reduction Obligation Projection Under CAR
Chart: Metric Tons, CO2
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Projected CNGC Emissions with 1.25% Annual Growth, MT CO2 | 2294671.1701 | 2323354.5597 | 2352396.4917 | 2381801.4479 | 2411573.966 | 2441718.6405 | 2472240.1236 | 2503143.1251 | 2534432.4142 | 2566112.8193 | 2598189.2296 | 2630666.595 | 2663549.9274 | 2696844.3015 | 2730554.8552 | 2764686.7909 | 2799245.3758 | 2834235.943 | 2869663.8923
Projected Large Customer Emissions - already covered parties themselves (>70,000 MT CO2) | 2776508.5522 | 2811214.9091 | 2846355.0954 | 2881934.5341 | 2917958.7158 | 2954433.1997 | 2991363.6147 | 3028755.6599 | 3066615.1057 | 3104947.7945 | 3143759.6419 | 3183056.6374 | 3222844.8454 | 3263130.406 | 3303919.5361 | 3345218.5303 | 3387033.7619 | 3429371.6839 | 3472238.83
Allowed Emissions, MT CO2 | 2277546.4793 | 2238828.1891 | 2200109.899 | 2161391.6088 | 2122673.3187 | 2083955.0285 | 2045236.7384 | 2006518.4482 | 1967800.1581 | 1929081.868 | 1890363.5778 | 1851645.2877 | 1812926.9975 | 1774208.7074 | 1735490.4172 | 1696772.1271 | 1658053.8369 | 1619335.5468 | 1580617.2566

## Slide 42: CAR (Cont.)
Compliance period is a three-year period
Compliance must be demonstrated at the end of each compliance period
Cascade must submit compliance reports within a year after the end of each three-year compliance period.
Each report must include third party verification that sufficient qualifying ERUs have been purchased to cover emissions above Cascade’s emission reduction pathway.

## Slide 43: CAR (Cont.)
Cascade will continue to evaluate options for purchasing ERUs and allowances to cover emissions above the projected emission reduction pathway.
Cascade notes that the price of ERUs is unknown at this time and that Ecology’s constraints on ERUs makes it difficult to project their cost.
As an alternative, Cascade has applied NPCC’s prices to model preliminary cost impacts from CAR.

## Slide 44: Fugitive Methane Emissions
There is no EPA rule governing the reduction of methane emissions for natural gas distribution utilities, but fugitive emissions are of interest to our regulators
Cascade’s voluntary efforts in this area:
  In March, 2016 Cascade became a founding partner of EPA’s Natural Gas Star Methane Challenge Program
    Participating under Best Management Practice (BMP) Commitment – Excavation Damages
  Cascade is also exploring other voluntary actions which could reduce methane emissions resulting from excavation damage

## Slide 45: Carbon Cost Risk Approach
All Washington and Oregon LDCs follow the protocols of the Council’s Carbon Cost Risk approach
Utilized in the IRP
  Results in a $10/ton carbon cost adder to Cascade’s avoided costs in 2018
  Rising to $30/ton in 2035

## Slide 46: Carbon Cost Risk Approach (Cont.)
Since Cascade’s modeling applies a price of CO2 from NPCC analysis to all emissions from natural gas delivered to all customers while CAR only requires compliance with a portion of these emissions, Cascade’s modeling is expected to be conservative.
Cascade will further evaluate ERU and compliance costs as Ecology establishes Cascade’s baseline emissions value.
Further expansion of this analysis in future years is pending Washington Superior Court for Thurston County on the legality of CAR.

## Slide 47: Avoided Cost

## Slide 48: Overview
As part of the IRP process, Cascade calculates a 20‐year forecast and 45 years of avoided costs.
The avoided cost is an estimated cost to serve the next unit of demand with a supply side resource option at a point in time. This incremental cost to serve represents the cost that could be avoided through energy conservation.
The avoided cost forecast can be used as a guideline for comparing energy conservation with the cost of acquiring and transporting natural gas to meet demand.
Cascade evaluates the impact that a range of environmental externalities, including CO2 emission prices, would have on the avoided costs in terms of cost adders and supply costs.
We produce an expected avoided cost case based on the medium forecast (base case) peak day.

## Slide 49: Costs included in the avoided cost calculation
The long term gas price forecast compiled from a consultant’s gas price forecast (which is the majority of the cost)
A price for carbon included in the gas price forecast, which has been embedded by price forecast consultant
Gas storage variable and fixed costs
Upstream variable and fixed transmission costs
Peak related on‐system transmission costs and
A 10 percent adder for unidentified environmental benefits, as recommended by the Northwest Power and Conservation Council (NPCC).

## Slide 50: METHODOLOGY
The SENDOUT® resource planning model is used to generate the avoided costs.
SENDOUT® contains a marginal cost report which lists the daily incremental cost to serve the next unit of demand for each demand region.
The model determines the lowest cost method for serving the next unit of demand and computes a marginal cost.
ALTERNATIVE RESOURCES CONSIDERED
With regards to alternative resources considered in the optimization of the portfolio, there is a level of uncertainty as to when certain alternative supply side resources will materialize and yet a base case needs to be created to calculate the avoided cost.
Using the base case demand parameters as inputs, including the design weather pattern, and base case customer and gas price forecasts, in addition to existing supply side resources, the Company’s resource portfolio for purposes of the avoided cost calculation include:
  Incremental NGTL, Foothills, GTN and NWP transport (all of which are allocated between Oregon and Washington).
  Also, a small level of satellite LNG and biogas is also included in the base case—however; these two alternative resources are assigned directly to Washington.

## Slide 52: Demand Side Management
March 29th, 2017 @ 1:30pm IRP WUTC Presentation
Monica Cowlishaw MGR, Energy Efficiency & Community Outreach Monica.Cowlishaw@cngc.com Amanda Sargent Conservation Analyst III Amanda.Sargent@cngc.com

## Slide 53: Elements of the DSM Chapter
The DSM Chapter includes the following topics relevant to the Energy Efficiency programs:
  Overview
  Conservation Planning
  Pathways to achieve goals for the next 10 years
  A progress report of where we’ve been and where we’re going
  Goals at a glance (developed from the potential forecast) & abridged budget estimates
  Cost test and market segmentation information relevant to cost-effectiveness discussions
  Target Development (Climate Zone modeling) – discussed on next slide
  Assessing future potential
  Conservation 2- year action plan including paths to increase forecast precision
  Action Plan Addendum
    New Conservation Potential Assessment & revision/replacement of current modeling tool
  Outreach & Messaging
    Community Partnerships & Targeted Outreach

## Slide 54: Climate Zone Map

## Slide 55: Full Portfolio by Climate Zone

## Slide 56: Full Portfolio by Customer Class
The Cascade Conservation Potential is represented in the IRP under three levels of possible savings - with goals set at the Achievable level (dotted line)

## Slide 57: Action Plan Addendum
Q2 – 2017 – Develop an RFP (in consultation with the CAG) for a new CPA (Conservation Potential Assessment) paired with a new or revised modeling tool using the Northwest Power & Conservation Council’s methodology
Q4 – 2017 - The Company will submit a work plan with the Commission outlining the method for assessing potential resources, including conservation
Q1- 2018 – Consultant will finalize the CPA which will be included in the 2018 IRP
Q2 – 2018 – Using the NPCC methodology Cascade will calculate its economic potential within the IRP. The Company will work with its CAG to evaluate moving towards using the TRC and will incorporate the TRC in its model revisions.
Cascade filed the Addendum to the 2016 Action Plan on March 10th, 2017 after discussions with Staff

## Slide 58: Distribution System Planning
Chris Bolton, Engineer II
WUTC IRP Presentation
March 29th, 2017

## Slide 59: Summary
Company overview
Interstate Pipeline Companies
Network Design Fundamentals
Synergi Modeling Software
    Input Data  Model Output
System Enhancement Techniques
Future Projects

## Slide 60: Synergi Outputs
            Calibrated model – model to represent a specific date and time
            Design Day Model – Uses the peak HDD for selected areas to simulate a cold weather day (worst case scenario)
            Growth model - Uses design day model along with growth data to predict future constraints

## Slide 61: System Modeling (cont.)
All customers are loaded based upon base and heat trend
Benefits of the models: - customer requests
- future planning
- system reliability
- optimizing potential reinforcement

## Slide 62: Synergi
Low pressure scenario
Possible Solutions ?
REGS?
PIPE?

## Slide 63: Synergi
Possible solutions – raising reg station set points

## Slide 64: Synergi
Reinforcement option #1

## Slide 65: Synergi
Reinforcement option #2


## Slide 66: Project Process Flow
Info & Data
Project & Schedules

## Slide 67: CNG Future Projects
Example upcoming growth projects
Location | 2017 | 2018 | 2019
Stanwood 4” PE Reinforcement | $116,130 |  | 
Manchester 4” PE Reinforcement |  | $245,870 | 
South Walla Walla Gate & HP Line |  | $3,356,259 | $2,190,610

## Slide 68: Integration Results

## Slide 69: Current Methodology – Flow Chart

## Slide 70: Integration Results – As Is
As Is Scenario: Using currently available Supplies, Transportation, and DSM, this scenario informs us where we expect deficiencies.
For modeling purposes, we assume all contracts run through the 20-year planning horizon.
Goal is to find the optimal mix of incremental supply, storage, transportation and other resources to “solve” for the best way to eliminate deficiencies at the lowest reasonable cost.
While Cascade aims to serve the demand of all of its customers, we take the approach that we will not pick up incremental transportation if the sole purpose of it is to serve customers on an interruptible tariff.
The mix of existing and incremental resources that SENDOUT® selects as the optimal solve for our deficiencies is defined as our expected scenario.

## Slide 71: Integration Results – As Is
Load Centers with Potential Peak Day Unserved Demand in dekatherms– As Is Scenario

## Slide 72: Integration Results – Incremental Resources
Incremental Transportation & Supply Acquired, in dekatherms

## Slide 73: Integration Results – Incremental Resources Selected
Transport
3rd Party Citygate Deliveries – Allows Cascade to purchase delivered natural gas from a 3rd party. 6,144 dth/day.
Incremental GTN – Allows Cascade to continue to serve customers as the Company’s core load grows in citygates that are fed by GTN capacity, specifically around Bend, Oregon where the Company expects shortfalls. 32,285 dth/day.
I-5 Expansion – Allows Cascade to continue to serve customers as the Company’s core load grows around the I-5 corridor, specifically in the Sedro-Woolley area. 10,000 dth/day.
Wenatchee Expansion – Allows Cascade to continue to serve customers as the Company’s core load grows in Central Washington in areas such as Wenatchee and Yakima. 7,310 dth/day.
Zone 20 Expansion – Allows Cascade to continue to serve customers as the Company’s core load grows in Eastern Washington in areas such as Kennewick. 6,560 dth/day.
Incremental Starr Road – Allows Cascade the flexibility to move gas off of GTN and onto NWP through Starr Road when needed, displacing the need for potential incremental NWP capacity. 9,326 dth/day.
Eastern Oregon Expansion – Allows Cascade to move gas from NWP to serve Eastern Oregon in areas such as Nyssa-Ontario. 3,950 dth/day.

## Slide 74: Integration Results – Incremental Resources Selected
Supply
Yakima Satellite LNG Plant – Allows Cascade the opportunity to serve demand in a cost effective way directly to Yakima, WA without new transport, which in turn helps increase served demand system wide through a displacement of Maximum Daily Delivery Obligations (MDDOs) among existing contracts. 5,000 dth/day.

## Slide 75: Integration Results– Impact of Additional Transport/supply

## Slide 76: Integration Results– Impact of Additional Transport/supply

## Slide 77: Conclusion – Expected Scenario
Load Centers with Potential Peak Day Unserved Demand in dekatherms – Expected Scenario

## Slide 78: INCREMENTAL RESOURCE COSTS and CHARACTERISTICS
Resource | Daily MDQ Acquired in 2017 for the Next 10 Years, in Dekatherms | Daily MDQ Acquired in 2020 for the Next 10 Years, in Dekatherms | Daily MDQ Acquired in 2030 for the Next 10 Years, in Dekatherms | Total Implementation Time (years) | Cost of Acquisition Over IRP Planning Horizon | Source
Incremental GTN - Daily MDQ | - | 20,472 | 11,814 | 1 | $ 2,356,878.00 | Capacity Available confirmed Nov 2016
I-5 Expansion - Daily MDQ | - | 990 | 9,010 | 3 | $ 37,412,500.00 | NWP Presentation April 8th, 2014
Wenatchee Expansion - Daily MDQ | - | 5,810 | 1,500 | 3 | $ 27,348,537.50 | NWP Presentation based on CNGC Capacity Presentation May 2014
Zone 20 Expansion - Daily MDQ | - | 440 | 6,120 | 3 | $ 24,542,600.00 | NWP Presentation based on CNGC Capacity Presentation May 2014
Incremental Starr Road - Daily MDQ | - | - | 9,327 | 2 | $ 2,553,266.25 | NWP Presentation based on CNGC Capacity Presentation May 2014
Eastern OR Expansion - Daily MDQ | - | 3,920 | 1,170 | 3 | $ 19,042,962.50 | NWP Presentation based on CNGC Capacity Presentation May 2014
Yakima LNG Plant - Daily MDQ | - | 5,000 | - | 2 | $ 20,500,000.00 | June 2005 Northstar Report
3rd Party Citygate Deliveries - Daily MDQ | 6,144 | - | - | N/A | N/A | N/A

## Slide 79: DSM RESOURCE COSTS AND CHARACTERISTICS
 | Estimated 2017 Dekatherms | Estimated 2020 Dekatherms | Estimated 2030 Dekatherms | Estimated 2017 Savings from DSM Source - Appendix H of CNGC 2016 IRP | Estimated 2020 Savings from DSM Source - Appendix H of CNGC 2016 IRP | Estimated 2030 Savings from DSM Source - Appendix H of CNGC 2016 IRP
DSM - Daily Allocation on Peak Day from Section 8-18 of CNGC 2016 IRP | 279 | 305 | 527 | $ 1,455 | $ 1,538 | $ 3,259
DSM - Annual Washington Achievable from Section 7-22 of CNGC 2016 IRP | 83,988 | 97,960 | 171,585 | $ 440,515 | $ 496,951 | $ 1,051,475

## Slide 80: Conclusions
Cascade has identified potential deficiencies starting in 2017.
From 2017-2020, Cascade uses 3rd party citygate deliveries to solve this shortfall.
From 2020 through the end of the planning horizon, Cascade uses a mix of incremental Transportation and Supply to solve the deficiency.
With the resource mix that is designated the “Expected Scenario” Cascade projects only a slight deficiency in 2036, all of which is from customers on an interruptible tariff.

## Slide 81: ADDITIONAL QUESTIONS?

## Slide 82: Cascade Natural Gas Corporation 2016 Integrated Resource Plan Presentation to WUTC Commissioners and Stakeholders
Wednesday, March 29, 2017
WUTC
Olympia, WA