## Slide 1: 2009 Integrated Resource Plan Summary
Washington Utilities and Transportation Commission
February 25, 2010
clint.kalich@avistacorp.com, 509.495.4532

## Slide 2: 2010 Hydro Conditions Update
  Latest Runoff Forecasts
    Columbia @ Dalles – 79%
    Clark Fork – 66%
    Spokane – 57%
  Impact on Avista
    Loss of ~45 aMW (8%)
    Could go lower or higher
    2009 was 33 aMW below average
  Weather Conditions
    Normal precipitation
    Warmer temperatures

## Slide 3: 2010 Hydro Conditions Update, Cont.
  Company’s hedging program is set up for just this type of circumstance.
  Hedge out 36 months ahead of time.
    Months N-36 to N-19 are used to make opportunistic transactions.
    Months N-18 to N-1 follow a rigorous schedule to close open positions (longs and shorts).
  Hydro variability is accounted for by Hydro Bias that reduces the amounts of hydro generation available for sale into the marketplace.
  Hydro Bias forces positions to close earlier and limits surplus sales for the event where hydro comes in lower than forecast (like 2009 and 2010).
  In a normal water year the Hydro Bias is rolled out of the position report as hydro conditions become known. We sell the length held back in case of poor hydro.

## Slide 4: 2010 Hydro Conditions Update, Cont.
  Hydro Bias equates to approximately 45 aMW, the average amount generation lost in all below-average water years.
  In 2010 it is likely that we will not end up selling any of the Hydro Bias length.
  Rates Are Set Based On Average Water Conditions.
  ERM Tracks Differences from Base Rates
    Any costs from below-average hydro purchases
    Any revenues from above-average hydro sales

## Slide 5: IRP Public Participation
  Six Technical Advisory Committee Meetings
    2008 Meetings: May 1, Aug 27, October 22
    2009 Meetings: January 28, March 25, June 24
  70 individuals from 46 organizations invited
    Commission Staff, academia, NW Power Council, government, consultants, peer utilities, Avista staff
  Other Collaborate Processes That Inform IRP Process
    External Energy Efficiency (Triple-E) Board
    Clark Fork Hydro Living License Collaboration
    Spokane River Hydro Relicensing Process
    Low Income Rate Assistance Program (LIRAP)
    Regional Planning
      WECC, NW Power Council, NWPP, PNUCC, ColumbiaGrid, Northwest Transmission Assessment Committee (NTAC), Seams Steering Group, NERC

## Slide 6: Avista Resources
AARG = 1.5%
Colstrip Coal Plant
Stateline Wind Farm
Kettle Falls Biomass
Coyote Springs 2 Gas CCCT
Boulder Park Reciprocating Gas Engines
Rathdrum Gas Peaking
Cabinet Gorge Hydro
Other Resources
Lancaster Gas CCCT
Northeast Gas Peaking
Spokane River Hydro
Mid-Columbia Hydro
Noxon Rapids Hydro
100 MW Contract

## Slide 7: Avista Generation Resources — 2011
Capability (capacity)
Expected Operations (energy)

## Slide 8: Loads (aMW)
AARG = 1.5%
AARG = 1.5%

## Slide 9: IRP Methods and Models
Resource Option Analysis
Mark to market all generation and conservation opportunities
Levelized Cost Calculation
Conservation
Costs
AURORAXMP
Base Case
Expected Fuel Prices, Load, Transmission, Resources
Develop Capacity Expansion for Western Interconnect
Generate electric price forecast
Intrinsic resource market valuation
Preferred Resource Strategy
Given constraints arrives at a least-cost solution defined in terms of present value of expected power supply expenses and risk, and generates an efficient frontier analysis.
Model selects resources and conservation measures to meet capacity and energy deficits, greenhouse gas limits, and renewable & conservation portfolio standards
Risk is defined as the variation in power supply expenses derived from stochastic studies
Market Futures
Stochastic
Load, fuel price, hydro, wind generation, emissions, thermal forced outages.
Market Scenario
Deterministic
Implicit market scenarios
Separate capacity expansion for each scenario
PRiSM 2.1

## Slide 10: Energy Efficiency – Overview
Avista has continuously provided energy efficiency programs since 1978
About 10% of the Company’s load is served by energy efficiency
Approximately 3,000 energy efficiency measures were evaluated in this IRP
7.5 aMW of local and 2.9 aMW of regional energy efficiency is expected to be acquired in 2010
Conservation additions provide 26% of new supplies through 2020
Chart: 
| High Efficiency Space and Water Heat | Conversions, Energy Star Homes, VSM | Weatherization (Insulation & Windows) | Total Annual Rebates
2006 | 2245 | 1068 | 2793 | 6106
2007 | 2573 | 1363 | 3392 | 7328
2008 | 4095 | 2057 | 4403 | 10555
2009 | 5218 | 2469 | 6471 | 14158

## Slide 11: Energy Efficiency -- Delivery Mechanisms
Standard Offers (“Prescriptive”) for residential & small commercial customers through mass marketing
Custom (“Site Specific”) for commercial &industrial customers with one point of contact through our Account Executive Team
Low Income through community action agencies
Regional through the NW Energy Efficiency Alliance
Special projects—RFPs, Pilot Programs, etc.
Promotion of Codes and Standards

## Slide 12: Energy Efficiency – 2010 Initiatives
Compliance with targets (re new WAC 480-109 aka Renewable Portfolio Standards)
American Recovery and Reinvestment Act (ARRA) projects
o In-home energy audits
o Revolving loan funds
Execute new Evaluation, Measurement and Verification (EM&V) protocols

## Slide 13: Energy Conservation
AARG = 1.5%
AARG = 1.5%
2009 IRP identifies more conservation potential than 2007 IRP
More than 3,0000 energy efficiency measures were evaluated for the 2009 IRP
By end of IRP forecast, nearly 20% of load is being met with conservation resources
26% of load growth is met by conservation resources

## Slide 14: Avista Resources and Upgrades
Hydro resources included as resource options
Little Falls Unit #1 – 4 Upgrades
Post Falls Unit #6 Upgrade
Upper Falls Upgrade
Hydro resources considered for further study
Long Lake new unit and new powerhouse
Cabinet Gorge #5
Scheduled upgrades and resources presently included in the L&R
Noxon Rapids Units #1 – 4 Upgrades (2009 – 2012)
Lancaster Generation Facility Tolling Agreement (2010)
Nine Mile (2012)

## Slide 15: Efficient Frontier- Introduction
Risk
Expected Return
Stocks
Bonds
T-Bills

## Slide 16: Efficient Frontier- Introduction
Present Value of Cost
Market Risk
Nuclear
CCCT
Market/SCCT
Wind

## Slide 17: Efficient Frontier
Demonstrates the trade off of cost and risk
Avoided Cost Method
Risk
Least Cost Portfolio
Least Risk Portfolio
Find least cost portfolio at a given level of risk
Short-term Market Only
Market
Capacity
Risk
+
= Avoided Cost
+

## Slide 18: Preferred Resource Strategy
AARG = 1.5%
AARG = 1.5%

## Slide 19: Annual Energy L&R w/ New Resources
Existing Resources & Contacts
New Gas CCCT
Wind (350 MW)
Conservation
Little/Upper Falls Upgrades
Distribution Efficiencies
Avg Load at 80% Confidence & Hydro at 80 Percentile
Avg Load

## Slide 20: January Capacity L&R w/ New Resources
Existing Resources & Contracts
New Gas CCCT
Conservation
Little/Upper Falls Upgrades
Distribution Efficiencies
Peak Load + Planning Margin
Peak Load
Market Purchases

## Slide 21: Avista Generation Resources — 2029
Capability (capacity)
Expected Operations (energy)

## Slide 22: 2009 IRP Market Futures and Scenarios
  Futures
    Base Case: uses expected hydro, wind, load, fuel costs, and emission costs
    Unconstrained Carbon: quantifies CO2 emissions costs
  Scenarios
    Low Gas Prices
    High Gas Prices
    Solar Saturation

## Slide 23: Portfolio Cost/Risk Comparison
PVRR
Standard Deviation

## Slide 24: Capital Expense in Billions Dollars (Nominal 2010-29)
Avista is ~$1 billion company
(market capitalization and book value)

## Slide 25: Greenhouse Gas Emissions
AARG = 1.5%
AARG = 1.5%
Chart: short tons (millions)
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Existing Resources | 3169.0088 | 3276.9044 | 3269.7319 | 3337.7126 | 3385.5174 | 3206.1336 | 3045.286 | 3062.4783 | 2886.0385 | 2789.8062 | 2664.2859 | 2594.476 | 2405.4854 | 2408.3499 | 2363.4402 | 2324.4511 | 2321.4285 | 1439.1795 | 1401.0021 | 1348.0828
New Resources | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 647.1949 | 653.2592 | 649.5193 | 652.4888 | 661.0957 | 1312.8637 | 1308.5083 | 1960.6869 | 1979.0023 | 1937.9298
CO2 Reduced from Legislation | 32.5438 | 46.912 | 108.7942 | 122.5425 | 222.6931 | 317.9468 | 409.4504 | 447.0616 | 669.3874 | 776.4269 | 704.774 | 827.3576 | 1020.1054 | 837.3858 | 987.7866 | 1020.8387 | 755.3428 | 772.3047 | 716.5492 | 755.4316
Tons per MWh of Load | 0.31544 | 0.31966 | 0.31345 | 0.31715 | 0.31655 | 0.29266 | 0.2732 | 0.27134 | 0.25154 | 0.23987 | 0.28005 | 0.27135 | 0.25177 | 0.24882 | 0.24126 | 0.28611 | 0.27809 | 0.25702 | 0.25123 | 0.2417

## Slide 26: Future Power Supply Costs (Index: 2010= 100, real dollars)

## Slide 27: Market Price Forecasts -- Gas

## Slide 28: Market Price Forecasts – NW Power

## Slide 29: Flexible Strategy
What if large hydro
upgrades are viable?
What if non-wind
renewables are abundant?
Is Nuclear a solution?
What are the impacts
of load growth changes?
What are the tipping points
for key capital costs?
wind capital cost <$1,830/kW, build early
CCCT cost >$1,610/kW, consider SCCT
High: 260/100 MW more gas/wind next 10 years
Low: 250/50 MW less gas/wind in next 10 years
eliminate 50/100 MW of wind/gas over 20 years?
non-wind renewables replace some
wind; could reduce gas by 100 MW
least-cost if <=$4,000/kW (current range $5-$10k)

## Slide 30: Washington State RPS Compliance
Reardan
Clark Fork River Upgrades
Little/Upper Falls Upgrades
New Wind

## Slide 31: Total Cost of Carbon Legislation
Drivers of Higher Costs:
Reduction in Colstrip energy
Higher electric market prices
Higher natural gas prices
Potential to be 30% of Power Costs

## Slide 32: US WECC Greenhouse Gas Levels

## Slide 33: Greenhouse Gas Prices ($/Ton)

## Slide 34: Avoided Resource Cost
Levelized Costs
Mid-C: $68.22
Capacity: $11.66
RPS: $5.76
Carbon: $25.52
Total: $111.15

## Slide 35
Clint -
Here are some questions/comments.
Slide 3 - Don't you have additional resources, such as the Spokane falls and other hydro? Maybe these are just example representative resources?
Slide 4 - Is the pie on the left your capacity and the one on the right the expected energy delivered by those same resources? (same question for slide 15)
Slide 7 - You indicate that 20% of your load will be through conservation by 2028. What proportion of the load demand increase will conservation be by 2028? This would be in comparison to the newly adopted 6th NWPCC plan which indicates that 85% of the regions new demand can be met through conservation by 2030. And where does that
leave renewables? Perhaps slide 12 may address this issue in part, and
slide 13 seems to indicate that conservation will be much less than 85% of your new load.
Slides 9-11 - nice job with the efficiency frontier presentation. One thing I was curious about was the placement of Nuclear on slide 10 with low market risk. Not sure what you are considering market risk, mainly fuel costs. As there has not been a new nuke plant built in the US for about three decades, seems that there may be substantial market risk for construction costs of a plant today. Maybe that is too far into the weeds??
Slide 15 If I am interpreting the left pie correctly, it shows 11% renewable energy generation in 2029. This is less than the 15% required by I-937 by 2020. Is some of the renewable requirement in other slices of the pie chart, e.g. biomass, hydro upgrades, etc?
Slides 17 and 18 - It would be good to identify your acronymns; LCS, PVRR, PRS... Slide 18 units on vertical scale are probably not dollars as it currently indicates.
Slide 28 - is the box in the lower right the average cost for the 20 years or for a particular year?
Dave N