## Slide 1: Electric Vehicle Rate Design
Andy Satchwell
Berkeley Lab
Washington Utilities and Transportation Commission
EV/EVSE Workshop
January 15, 2025

## Slide 2: State policy-driven objectives may serve as the basis for rate design for EV charging
EV adoption
Grid management
System economic efficiency
Decarbonization
Equity

## Slide 3: EV rate design is typically comprised of 5 components
EV Rate Design
Metering Configurations
Temporal Differentiation
Locational Differentiation
Demand Charges
Charging Controls

## Slide 4: 1. Metering configurations
Whole home/facility consumption via account meter
EV charging consumption
via account meter
Submetering via EVSE or vehicle
*EVSE = Electric Vehicle Supply Equipment

## Slide 5: To submeter or not to submeter?
Rate applies to entire home electricity usage and demand
Does not require additional, separate meter installation or changes to utility data collection/billing systems
Can be a disincentive to EV charging if rate is tiered
Rate applies only to EV usage and demand
Requires a separate meter box and dedicated circuit, imposing additional costs to customer and/or utility
Rate design may send clearer cost-based price signal
Whole Home Rate
(Georgia Power)
EV Only Rate
(Austin Energy)

## Slide 6: 2. Temporal differentiation
Chart: August Day
 | 28286 | 27023 | 26150 | 25830 | 26229 | 27530 | 29470 | 30667 | 31753 | 32861 | 33234 | 33075 | 33400 | 34294 | 35778 | 37735 | 39527 | 40732 | 40914 | 40384 | 39751 | 37775 | 34643 | 31948
Chart: 
| 0.70833333333333337 | 0.71180555555555547 | 0.71527777777777779 | 0.71875 | 0.72222222222222221 | 0.72569444444444453 | 0.72916666666666663 | 0.73263888888888884 | 0.73611111111111116 | 0.73958333333333337 | 0.74305555555555547 | 0.74652777777777779 | 0.75 | 0.75347222222222221 | 0.75694444444444453 | 0.76041666666666663 | 0.76388888888888884 | 0.76736111111111116 | 0.77083333333333337 | 0.77430555555555547 | 0.77777777777777779 | 0.78125 | 0.78472222222222221 | 0.78819444444444453 | 0.79166666666666663 | 0.79513888888888884 | 0.79861111111111116 | 0.80208333333333337 | 0.80555555555555547 | 0.80902777777777779 | 0.8125 | 0.81597222222222221 | 0.81944444444444453 | 0.82291666666666663 | 0.82638888888888884 | 0.82986111111111116 | 0.83333333333333337 | 0.83680555555555547 | 0.84027777777777779 | 0.84375 | 0.84722222222222221 | 0.85069444444444453 | 0.85416666666666663 | 0.85763888888888884 | 0.86111111111111116 | 0.86458333333333337 | 0.86805555555555547 | 0.87152777777777779 | 0.875 | 0.87847222222222221 | 0.88194444444444453 | 0.88541666666666663 | 0.88888888888888884 | 0.89236111111111116 | 0.89583333333333337 | 0.89930555555555547 | 0.90277777777777779 | 0.90625 | 0.90972222222222221 | 0.91319444444444453
 | 32396 | 32328 | 32335 | 32462 | 32559 | 32697 | 32808 | 32922 | 33086 | 33115 | 33218 | 33283 | 33289 | 33126 | 33028 | 33069 | 33096 | 33088 | 33080 | 33092 | 33076 | 33096 | 33031 | 33016 | 32991 | 32913 | 32805 | 32757 | 32753 | 32711 | 32723 | 32729 | 32766 | 32782 | 32842 | 32847
Chart: Average Winter Day
 | 1047.0238 | 1015.5298 | 997.317 | 994.4449 | 1015.0327 | 1071.0134 | 1148.5729 | 1179.8973 | 1167.4092 | 1132.6815 | 1096.4762 | 1068.6548 | 1047.6994 | 1042.9628 | 1058.8304 | 1090.9911 | 1148.1324 | 1252.5342 | 1324.5238 | 1304.2545 | 1267.933 | 1220.8914 | 1154.2649 | 1087.9926
Chart: Average Summer Day
 | 1363.6263 | 1293.6237 | 1242.6384 | 1214.5995 | 1210.4113 | 1237.1909 | 1284.578 | 1332.2392 | 1390.8763 | 1427.7285 | 1465.0591 | 1514.8387 | 1574.0376 | 1654.7688 | 1745.2997 | 1831.2097 | 1897.3589 | 1934.9798 | 1924.0081 | 1867.9825 | 1810.3306 | 1716.0094 | 1582.5228 | 1452.9086
Seasonal Differentiation
Sub-hourly Differentiation
Hourly and Period Differentiation
Figures show temporal differentiation in load, but there is also temporal differentiation in system costs and emissions that could be used as the design basis

## Slide 7: 3. Locational differentiation
Bulk power system
Distribution system
Site-specific

## Slide 8: Combining temporal and locational differentiation

## Slide 9: 4. Demand charges
Max demand period
Demand ratchet
Seasonal
Coincident peak
Non-coincident peak

## Slide 10: Load factor-based demand charges address utilization and coincidence at low deployment levels

## Slide 11: 5. Charging controls
Utility system
Account meter
EV Supply Equipment (EVSE)
Electric Vehicle
Utility control via account meter or EVSE
Customer control via EVSE
One-way communication
Two-way communication

## Slide 12: Control by the customer vs. utility may result in different rates
Tariff details available at: https://static.greenmountainpower.com/tariffs/rates/Rate-72-Off-Peak-EV-Residential.pdf and https://static.greenmountainpower.com/tariffs/rates/Rate-74-TOU-EV-Residential.pdf
Through 2023, ~895 customers enrolled in Rate 72 and ~1,737 customers enrolled in Rate 74. Only 0.25% of Rate 72 customers opted out of managed charging during a Peak Event.

## Slide 13: EV program elements can further EV-related objectives
Available at: https://sepapower.org/resource/managed-charging-incentive-design/

## Slide 14: Most utilities currently offer TOU rates to residential and commercial customers
Source: Cappers et al. (2023). A Snapshot of EV-Specific Rate Designs Among U.S. Investor-Owned Electric Utilities. Report and rates database available at: https://emp.lbl.gov/publications/snapshot-ev-specific-rate-designs
Based on a review of 136 EV-specific retail rates currently approved and/or offered to customers

## Slide 15: Do customers respond to EV rates?
Reviewed 11 evaluation reports of EV rate offerings published from 2013-2020
Most evaluation reports were outcomes of short-term (6 months – 2 years) pilots; very few system-wide roll-outs were evaluated
Pilots were evenly split between whole house vs. EV-only metering
Most pilots had at least a 2:1 peak-to-off peak price ratio and a small number had a 4:1 or greater price ratio
Individual rate offerings within 11 evaluation reports

## Slide 16: Properly designed rates can be an effective tool for managing EV charging behavior
Source: McDougall, L., Donnelly, A. and Chandra, K. (2019) Austin Energy's Residential "Off Peak" Electric Vehicle Charging Subscription Pilot: Approach, Findings, and Utility Toolkit. EV360 Whitepaper. Austin Energy, Austin, TX.
Source: DTE Energy (2020) Charging Forward: Annual Status Report. May.
Example: 93% of residential customer charging occurred off-peak on average
Example: Residential customers consistently charged off-peak on weekdays and weekends

## Slide 17: Higher price ratios encouraged greater off-peak charging
Values in the table represent differences in the share of charging load for customers on different rates
Customers on the rate with the lowest price ratio (EPEV-L) consumed more energy during the peak period than customers on the rate with the highest price ratio (EPEV-H)
But EPEV-H customers consumed a larger share during super off-peak period
Summer Price Ratio
EPEV-H
EPEV-M
EPEV-L
6.0
4.0
1.9
Rate Offering
Source: Cook, J., Churchill, C. and George, S. (2014) Final Evaluation for San Diego Gas & Electric’s Plug-in Electric Vehicle Tou Pricing and Technology Study. Nexant Inc. Prepared for San Diego Gas & Electric.

## Slide 18: The higher the price ratio, the quicker customers learned to shift charging to the off-peak period
Figure shows monthly share of charging as a function of the number of months after a customer started in the study
Customers on EPEV-H (highest price ratio) exhibited consistent charging behavior throughout the entire duration of the study
Customers on EPEV-L and EPEV-M (medium price ratio) increased charging consumption in super off-peak period by 1.8%–2.9% per month for the first four months, but consumption remained relatively stable thereafter
Summer Price Ratio
EPEV-H
EPEV-M
EPEV-L
6.0
4.0
1.9
Rate Offering
Source: Cook, J., Churchill, C. and George, S. (2014) Final Evaluation for San Diego Gas & Electric’s Plug-in Electric Vehicle Tou Pricing and Technology Study. Nexant Inc. Prepared for San Diego Gas & Electric.

## Slide 19: Customers who owned a PV system were significantly less responsive to prices than their non-PV counterparts
PV owners exhibit more consistent shares of charging by period across the three rates relative to non-PV owners
Selling PV electricity back to the grid may be valued more highly by customers than using it to charge their EV
PV owners may have certain characteristics that cause them to place an even higher premium on charging overnight regardless of the prices they face
Source: Cook, J., Churchill, C. and George, S. (2014) Final Evaluation for San Diego Gas & Electric’s Plug-in Electric Vehicle Tou Pricing and Technology Study. Nexant Inc. Prepared for San Diego Gas & Electric.

## Slide 20: Considerations to move from pilots to programs
Clearly defined roles and responsibilities for utilities vs. third-party companies/EV solutions providers
Robust customer enrollment and engagement
Stakeholder-driven program design and/or planning collaborative
Iterative program design to meet needs of larger customer population
Meaningful community engagement

## Slide 21: Resources for More Information
Alliance for Transportation Electrification. 2021. Electric Transportation Rate Design Principles for Regulated Utilities.
Ball, J., S. Forrester, A. Grayson, A. Satchwell. 2023. Electric Vehicle Program Designs and Strategies to Enhance Equitable Deployment.
Cappers, P. and A. Satchwell. 2022. EV Retail Rate Design 101.
Cappers, P., A. Satchwell, C. Brooks, S. Kozel. 2023. A Snapshot of EV-Specific Rate Designs Among U.S. Investor-Owned Electric Utilities.
Ryan, N. A. Burger, J. Bosco, J. Howat, M. Muller. 2022. Best Practices for Sustainable Commercial EV Rates and PURPA 111(d) Implementation.
Satchwell, A., P. Cappers, G. Barbose. 2019. Current Developments in Retail Rate Design: Implications for Solar and Other Distributed Energy Resources.
Whited, M., A. Allison, R. Wilson. 2018. Driving Transportation Electrification Forward in New York: Considerations for Effective Transportation Electrification Rate Design.
Hledik, R., A. Ramakrishnan, S. Patel, and A. Satchwell. 2024. Distributed Energy, Utility Scale: 30 Proven Strategies to Increase VPP Enrollment.
————
Forthcoming: Collins, M. et al. Best Practices Guide for Benefit-Cost Analysis of Managed EV Charging. Lawrence Berkeley National Laboratory.

## Slide 22: Contact
Andy Satchwell
Lawrence Berkeley National Laboratory
asatchwell@lbl.gov