## Slide 1: 2011 Integrated Resource Plan Overview
Washington Utilities and Transportation Commission
July 28, 2011

## Slide 2: Significant Changes from the Last IRP
Decrease in peak resource need of 175 MW on an average annual basis for 2011 through 2020; capacity deficit begins in 2011 for both IRPs
  Reduction in system coincident peak load of 345 MW on an average annual basis for 2011 through 2020 (west down 283 MW; east down 62 MW)
Decrease in projected natural gas and wholesale electricity prices relative to the forecasts prepared in 2008 and 2009
Methodology
  Updated demand-side management/distributed generation potential study
  Conducted Energy Gateway scenario analysis prior to preferred portfolio determination
  Conducted Loss of Load Probability (LOLP) study, leading to selection of a 13% capacity planning reserve margin
  Disaggregated west-side transmission topology
    West Main bubble converted to four new bubbles (Portland/North Coals, Willamette Valley/Central Coast, South-Central Oregon/North California, Bethel Substation)
  Implemented System Optimizer proof-of-concept modeling for optimized coal plant replacement scenarios

## Slide 3: Other Key Drivers of the 2011 IRP
Loss of momentum in federal energy and climate change policies contribute to continued uncertainty regarding long-term investment in clean energy technologies
Public and legislative support for clean energy policies at the state level remains robust
Continued efforts by the U.S. Environmental Protection Agency to regulate electric utility plant emissions, including greenhouse gases, criteria pollutants, and other emissions
Expectations for a more favorable economic environment than assumed in 2009. Load growth in such areas as data centers and natural resource extraction
Progress and challenges in planning for, permitting, and building the Energy Gateway transmission project
Near-term procurement activities, including the planned acquisition of Lake Side 2 in Utah, with a 2014 in-service date

## Slide 4: 2011 IRP Regulatory Compliance
Address each requirement under WAC 480-100-238
  Compliance described in Table B.5, Appendix B of Volume II
2008 IRP Acknowledgment Letter Requirements
  Transmission planning:

## Slide 5: 2011 IRP Regulatory Compliance
2008 IRP Acknowledgment Letter Requirements
  Out-year resource modeling and energy efficiency targets under RCW 19.285

## Slide 6
IRP Results

## Slide 7: Coincident Peak Load Forecast
Reflects peak loads prior to any load reductions from energy efficiency (Class 2 DSM)

## Slide 8: Resource Need Determination - System

## Slide 9: Resource Need Determination - West

## Slide 10: Power Purchase Contract Trends
Expiration of BPA peaking contract (575 MW in late 2011) and hydro contracts in 2011-2012
Expiration of third-quarter firm purchases (“front office transactions”)

## Slide 11: System Energy Balance
Heavy load hour energy deficits begin in 2011

## Slide 12: West-side Energy Balance

## Slide 13: Addressing PacifiCorp’s Peak Capacity Deficit

## Slide 14: 2011 IRP Resource Strategies – DSM
Energy efficiency: acquire up to 1,200 MW of cost-effective capacity by 2020 (~4.5 million MWh)
  Washington, 79 MW by 2020 (~383 thousand MWh)
  Preferred portfolio includes about 2,560 MW by 2030 (~10.7 million MWh)
Load control: acquire up to 250 MW of cost-effective irrigation load control, commercial curtailment, and residential direct load control by 2020 (~60 MW in the west)

## Slide 15: 2011 IRP Resource Strategies – Thermal and Market
Combined-cycle combustion turbines: 1,700 MW acquired by 2019
  additions in 2014 (Lake Side 2), 2016, and 2019
Firm market purchases: ranges from 350 MW to ~1,400 MW on an annual basis, peaking in 2013
Coal plant turbine upgrades: 65 MW (12 MW at Jim Bridger)

## Slide 16: 2011 IRP Resource Strategies – Renewables and Distributed Generation
Wind: Additions beginning in 2018, 800 MW added through 2020 and 2,100 MW added by 2030
  additions driven by
    Assumed long-term state/federal renewables policies and/or carbon policies and associated uncertainty
    Fuel risk mitigation and resource diversity benefits
    Federal production tax credit assumed to fully expire by 2015
Distributed generation: acquire up to 100 MW by 2020
  Combined Heat & Power, ~50 MW
  Solar photovoltaic programs
  Investigate cost-effectiveness of a solar hot water heating program
Energy storage evaluation

## Slide 17: Resource Energy Mix: 2011 versus 2020
* Energy mix expressed in megawatt-hours.
** Renewable resources include wind, solar, and geothermal.
*** Hydroelectric resources include owned, PURPA Qualifying Facilities, and contract purchases.
2011 Energy Mix*
2020 Energy Mix*

## Slide 18: Carbon Dioxide Emissions Trend Based on nominal $19/ton CO2 Tax beginning in 2015
Gas prices have a significant impact on CO2 emissions—lower prices lead to lower coal plant utilization and greater gas plant reliance

## Slide 19
Energy Gateway Status and IRP Scenario Analysis

## Slide 20: Energy Gateway Overview
Key Principles
  Secure capacity for the long-term benefit of customers
  Load service needs first, regional needs second
  Support multiple resource scenarios
  Secure regulatory and community support
  Build it
Highlights
  Approximately 2,000 new line miles
  Multi-year, multi-billion dollar investment
  Segment “B” completed November 2010
  Segment “C” under construction
  Ratings and license obtained from WECC to interconnect and operate all segments

## Slide 21: 2011 IRP System Optimizer Scenarios
Wind ( MWs) | 
East | 811
West | 1421
Total | 2232
Wind ( MWs) | 
East | 1758
West | 284
Total | 2042
Wind ( MWs) | 
East | 1768
West | 300
Total | 2068
Wind ( MWs) | 
East | 1758
West | 284
Total | 2042
Wind ( MWs) | 
East | 811
West | 1421
Total | 2232
Wind ( MWs) | 
East | 811
West | 1421
Total | 2232
Wind ( MWs) | 
East | 1828
West | 238
Total | 2066
Scenario 1
Scenario 2
Scenario 3
Scenario 4
Scenario 5
Scenario 6
Scenario 7

## Slide 22: Foundational Assumption: Green Resource Future
The IRP considered “green resource” and “incumbent resource” futures based on varying RPS and CO2/gas price assumptions
Seven Energy Gateway scenarios modeled
The full Energy Gateway footprint (Scenario 7) provides the necessary capacity for a green resource future, with a PVRR $830 to $907 million lower than a limited transmission expansion (Scenario 1)
However, without the mandate for additional renewables consistent with a green resource future, and regulatory support for associated transmission, the risk of building increases significantly
Regulatory support is critically important to these investments materializing
Notes: Verbal point: PacifiCorp looks to its regulators for guidance and support on these planned investments.

## Slide 23
2,100 MW Wyoming Wind
1,697 MW Utah CCCT
19 MW Oregon Solar
84 MW west-side CHP Biomass
Planned generation additions per the 2011 IRP preferred portfolio
GATEWAY WEST
GATEWAY SOUTH
GATEWAY CENTRAL

## Slide 24
Portfolio Modeling and Preferred Portfolio Selection Approach

## Slide 25: 2011 IRP Modeling Approach - Steps
Use capacity expansion optimization tool, System Optimizer, to develop alternative resource portfolios that meet capacity, energy, and resource-related state regulatory requirements, based on numerous input scenarios
Conduct Monte Carlo production cost modeling of each portfolio (100 simulations resulting in 100 distinct portfolio costs) – accounts for stochastic behavior of loads, prices, and plant availability
Select top-performing portfolios based on simulations with alternative CO2 tax levels
  Best combinations of low “average” and “upper-tail” portfolio costs

## Slide 26: 2011 IRP Modeling Approach - Steps
Final screen: compare other performance metrics, including risk-adjusted cost, 10-year customer rate impact, CO2 emissions, supply reliability, etc
Select top three portfolios and simulate with System Optimizer given different deterministic cost assumptions (deterministic risk assessment)
Select top-performing portfolio

## Slide 27: 2011 IRP Modeling Approach - Steps
Preferred portfolio determination
  Evaluate top portfolio based on resource-specific acquisition risks
    Geothermal resource development costs (“dry hole” risk)
    Preferred wind schedule for meeting regulatory compliance requirements, address public policy goals, mitigate fuel price risk
    Timing of next major thermal resource (after Lake Side 2 in 2014)
  Refine preferred portfolio resources and re-optimize with System Optimizer to ensure that capacity reserve margins are met for every year

## Slide 28
Key IRP Inputs/Assumptions

## Slide 29: Load Forecast - Comparison

## Slide 30: Transmission System Model Topology

## Slide 31: Resource Option Categories

## Slide 32: Natural Gas Price Forecast Scenarios
Three underlying forecasts—High, Medium, Low—support development of scenario forecasts reflecting CO2 prices and other IRP input assumptions
Henry Hub Natural Gas Price Forecast Summary (nominal $/MMBtu)
Gas price forecasts significantly lower than the 2008 IRP and 2008 IRP Update

## Slide 33: Carbon Dioxide Price Scenarios
Also modeled CO2 emissions physical hard cap scenarios
  Base – 15% below 2005 emission levels by 2020, and 80% by 2050
  Oregon – 10% below 1990 emission levels by 2020, and 80% by 2050

## Slide 34: Conclusion
2011 IRP complies with Washington’s IRP guidelines
  Lowest reasonable cost criterion, considering:
    Market volatility risks
    Other risks
    Washington state resource preferences
    Resource dispatchability for resource mix
  Conservation and load management assessment
    Potential study available at: http://www.pacificorp.com/es/dsm.html
  Short term action plan and progress report (Chapter 9)

## Slide 35
Questions?