| Switched DS1 Message Trunk Port Provisioning Task List |  |  |
| --- | --- | --- |
| Task | Description |
| 1 | Access Service Request (ASR) form submitted by CLEC |
| 2 | ASR and associated forms reviewed for completeness |
| 3 | Service Delivery Coordinator (SDC) imputs Faxed ASR into EXACT |
| 4 | SDC distributes IABS service order into service order processor (SOP) |
| 5 | SDC logs order into TIRKS to start provisioning process of Port |
| 6 | Trunk request and work authorization forms completed by Designer |
| 7 | Trunk port in designed in TIRKS |
| 8 | Design layout record (DLR) created |
| 9 | SDC creates and sends firm order confirmation and DLR to CLEC |
| 10 | CLEC receives firm order confirmation and DLR from USWC |
| 11 | Trunk port installation is coordinated by implementor |
| 12 | Load Central Office work steps |
| 13 | Central Office wiring completed |
| 14 | Central Office conformance testing completed |
| 15 | Test results recorded |
| 16 | Implementor contacts CLEC for turn up, completes order in WFA/C |
| 17 | CLEC accepts Service |
| 18 | Implementor completes order in WFA/C |
| 19 | SDC completes order in EXACT and IABS to begin billing |

| Unbundled Switch Maintenance Task List |  |  |
| --- | --- | --- |
| Assoc. Task # | Process |
| 1 or 2 | Trouble ticket submitted NOTE: If CLEC has a system interface they may submit report electronically. Otherwise CLEC calls AMSC to report trouble and steps 3 and 4 are required. |
| 3 | Process ticket received from CLEC |
| 4 | Trouble ticket created |
| 5 | Analyze trouble ticket, identify location, and assign to appropriate organization |
| 6 | If part of major outage SAT follows major outage notification processes Note: then skip to step 13 |
| 7 | Translations Trouble is resolved Note: then skip to step 13 |
| 8 | SAT hands off physical trouble to network operations |
| 9 | CORAC loads to appropriate LNO Technician |
| 10 | Trouble is isolated |
| 11 | Trouble repaired |
| 12 | Trouble ticket updated |
| 13 | Contact SAT with ticket results |
| 14 | CLEC notified |
| 15 and 16 | CLEC accepts service and Trouble ticket closed |