## Slide 1: Avista’s 2018 Natural Gas IRP
November 30, 2018

## Slide 2: Purpose of IRP
Security of supply to meet demand on a peak day
Least cost mix of supply and conservation
2

## Slide 3: 2018 IRP Timeline
August 31, 2017 – Work Plan filed with WUTC
January through May 2018 – Technical Advisory Committee meetings. Meeting topics will include:
  TAC 1: Thursday, January 25, 2018: TAC meeting expectations, review of 2016 IRP acknowledgement letters, customer forecast, and demand-side management (DSM) update.
  TAC 2: Thursday, February 22, 2018: Weather analysis, environmental policies, market dynamics, price forecasts, cost of carbon.
  TAC 3: Thursday, March 29, 2018 : Distribution, supply-side resources overview, overview of the major interstate pipelines, RNG overview and future potential resources.
  TAC 4: Thursday, May 10, 2018: DSM results, stochastic modeling and supply-side options, final portfolio results, and 2020 Action Items.
  June 21, 2018– TAC final review meeting to review final stochastics (if necessary)
July 2, 2018 – Draft of IRP document to TAC
July 13, 2018 – Comments on draft due back to Avista
August 31, 2018 – File finalized IRP document
3

## Slide 4: WA-ID Region Firm Customers: 2018 IRP and 2016 IRP
IRP | Avg. Annual Growth 2018-2037
2016 | 1.1%
2018 | 1.3%
≈ +16,500
2

## Slide 5: Estimating the IMPACT of LEAP in WA: Residential Customers
WA IRP | Residential Change by 2037
2018 IRP with LEAP Less 2016 IRP | +11,300
2018 IRP w/o LEAP Less 2016 IRP | +2,200
LEAP Contribution | +9,100

## Slide 6: Planning Standard Assumptions
Cooling
Degree Days
Heating
Degree Days
Area | Coldest on Record | °Fahrenheit
 | HDD | Average
WA-ID | 82 | -17
Klamath Falls | 72 | -7
La Grande | 74 | -9
Medford | 61 | 4
Roseburg | 55 | 10
6

## Slide 7: Spokane
*1947 - 2017
7

## Slide 8: Temperature Anomaly Distribution
Source: Hansen, J., R. Ruedy, M. Sato, and K. Lo (2010), Global surface temperature change, Rev. Geophys., 48, RG4004,
doi:10.1029/2010RG000345. This research has been updated and can be found at http://www.giss.nasa.gov/research/briefs/hansen_17/.
Temperature anomaly distribution: The frequency of occurrence (vertical axis) of local temperature anomalies (relative to 1951-1980 mean) in units of local standard deviation (horizontal axis). Area under each curve is unity. Image credit: NASA/GISS.
NASA Temperature Anomaly Distribution for Northern Hemisphere
Normal Distribution: Base Reference Period 1951-1980
8

## Slide 9: Spokane
9

## Slide 10: WA Carbon Tax Summary
WA – Governor Inslee proposed Carbon tax (SB 6203)
  Starts at $10 per MTCO2e in July 2019 and in 2021 adds $2 per year until capping at $30 in 2030
10
Chart: $ per Dth – Carbon Tax
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037
WA | 0.53061 | 0.53061 | 0.63673 | 0.74286 | 0.84898 | 0.9551 | 1.0612 | 1.1673 | 1.2735 | 1.3796 | 1.4857 | 1.5918 | 1.5918 | 1.5918 | 1.5918 | 1.5918 | 1.5918 | 1.5918 | 1.5918

## Slide 11: 2018 Henry Hub Expected Price Including Carbon Adders by State
Chart: $ per Dth
| 2017-2018 | 2018-2019 | 2019-2020 | 2020-2021 | 2021-2022 | 2022-2023 | 2023-2024 | 2024-2025 | 2025-2026 | 2026-2027 | 2027-2028 | 2028-2029 | 2029-2030 | 2030-2031 | 2031-2032 | 2032-2033 | 2033-2034 | 2034-2035 | 2035-2036 | 2036-2037
ID - HH Expected Price Nominal $ | 2.8657 | 2.7889 | 2.8191 | 2.9702 | 3.134 | 3.2822 | 3.653 | 3.863 | 3.9485 | 4.1396 | 4.429 | 4.6845 | 4.9859 | 5.2111 | 5.3696 | 5.6343 | 5.8825 | 6.1074 | 6.3957 | 6.7133
OR - HH Expected Price Nominal $ | 2.8657 | 2.7889 | 2.8191 | 3.7598 | 4.137 | 4.3551 | 4.8002 | 5.0893 | 5.2595 | 5.5413 | 5.9286 | 6.2893 | 6.7033 | 7.049 | 7.3365 | 7.739 | 8.1347 | 8.5167 | 8.9533 | 9.4242
WA - HH Expected Price Nominal $ | 2.8657 | 2.9658 | 3.3497 | 3.5362 | 3.8591 | 4.1135 | 4.5905 | 4.9065 | 5.0982 | 5.3954 | 5.7909 | 6.1525 | 6.5601 | 6.8029 | 6.9615 | 7.2261 | 7.4744 | 7.6992 | 7.9875 | 8.3051
11

## Slide 12: Potential by Sector
Total Avista Washington, Cumulative Potential
All potential “ramps up” over time – all ramp rates are based on those found within the NWPCC’s Seventh Power Plan
Achievable technical potential reaches 85% of technical by the end of the study, consistent with the Council assumptions
UCT Savings (Dth) | 2018 | 2019 | 2022 | 2028 | 2038
Residential | 39,979 | 88,051 | 345,801 | 1,362,078 | 3,107,847
Commercial | 20,731 | 44,393 | 151,733 | 547,834 | 1,021,211
Industrial | 569 | 1,132 | 2,887 | 6,528 | 9,957
Total | 61,279 | 133,576 | 500,422 | 1,916,441 | 4,139,016
Chart: UCT AEP Share of Total Savings by Sector
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038
Residential | 39978.6574 | 88050.6681 | 151814.7994 | 233065.6989 | 345801.4523 | 491108.6272 | 519377.6086 | 703213.0428 | 909273.0258 | 1131012.5281 | 1362078.4086 | 1595564.5739 | 1824208.0682 | 2038249.0442 | 2236755.9411 | 2417134.8701 | 2585729.5844 | 2736961.9207 | 2876533.242 | 3003788.6165 | 3107846.7524
Commercial | 20731.0716 | 44392.8391 | 73253.2878 | 107739.2707 | 151733.4354 | 204797.7793 | 265592.8632 | 333535.7319 | 403863.778 | 476648.3143 | 547834.165 | 617994.7441 | 683076.8047 | 745390.4246 | 803475.0453 | 856159.166 | 899068.6974 | 936306.6595 | 968117.6884 | 994794.7981 | 1021211.3428
Industrial | 569.353 | 1132.1187 | 1709.0041 | 2290.3242 | 2887.2351 | 3485.7451 | 4112.3429 | 4744.7392 | 5377.8789 | 5973.8564 | 6528.2089 | 7027.1142 | 7484.7261 | 7905.8589 | 8300.2415 | 8655.8946 | 8991.9413 | 9312.706 | 9624.3679 | 9916.4786 | 9957.4836
TRC Savings (Dth) | 2018 | 2019 | 2022 | 2028 | 2038
Residential | 14,920 | 32,308 | 139,361 | 824,953 | 1,573,939
Commercial | 18,376 | 39,603 | 134,004 | 465,827 | 836,014
Industrial | 597 | 1,188 | 1,785 | 6,899 | 10,696
Total | 33,893 | 73,100 | 276,379 | 1,297,679 | 2,420,649
Notes: Potential by Sector: UCT and TRC
Update from gradual ramp up to Seventh Plan ramp rates
  Later-year potential is substantially higher
  Please note Power Council’s ramp rates include potential realized from outside of utility DSM programs, including regional initiatives and market transformation.
Inclusion of TRC screening as a secondary test (with Power Council non-energy impacts)
  Significantly lowers potential – although results are in line with other jurisdictions who use TRC
As the largest sector, residential represents the largest portion of cumulative UCT achievable economic potential (AEP) throughout the study period.
The industrial sector only includes customers eligible for programs, which represent a very small percentage of total industrial consumption.
Some residential measures are not cost-effective on a TRC basis. This is due to the use of full measure costs rather than just a utility’s portion. Inclusion of a heating calibration credit and non-gas impacts somewhat mitigates this effect.

## Slide 13: Comparison with 2016 CPA
 | Current Study: 2027 Potential (Dth) | Prior Study: 2026 Potential (Dth) | Change from Prior Study (Dth)
Washington |  |  | 
Residential | 1,131,013 | 497,074 | 633,939
Commercial | 476,648 | 413,219 | 63,429
Industrial | 5,974 | 4,050 | 1,924
WA Total | 1,613,635 | 914,343 | 699,292
Idaho |  |  | 
Residential | 596,450 | 208,875 | 387,575
Commercial | 205,064 | 170,883 | 34,181
Industrial | 6,034 | 4,411 | 1,623
ID Total | 807,547 | 384,169 | 423,378
Avista |  |  | 
Residential | 1,727,462 | 705,949 | 1,021,513
Commercial | 681,712 | 584,102 | 97,610
Industrial | 12,007 | 8,461 | 3,546
Avista Total | 2,421,181 | 1,298,512 | 1,122,669
  10-year cumulative UCT Achievable Potential increased substantially
  In the prior CPA, we gradually increased ramp rates over time and did not max out ramp rates at 85%
  This is causing a spike in mid-year potential since many of the faster rates are already at 85%
10-year Cumulative UCT Achievable Potential
Notes:   Comparison with prior (2016) CPA. This is a high-level slide
  Illustrates the ramp rate change (85% achievability)

## Slide 14: Sendout and Dynamic DSM
Action Plan: Avista’s 2018 IRP will contain a dynamic DSM program structure in its analytics. In prior IRP’s, it was a deterministic method based on Expected Case assumptions. In the 2018 IRP, each portfolio will have the ability to select conservation to meet unserved customer demand. Avista will explore methods to enable a dynamic analytical process for the evaluation of conservation potential within individual portfolios.
14

## Slide 15: DSM Example
Com
Ind
WA GTN
245 Measures
658 Measures
54 Measures
957 Total Measures
15
Res

## Slide 16: Needed Measures
WA GTN
WA NWP
ID GTN
ID NWP
Medford GTN
Roseburg
Klamath Falls
Demand Areas
11 demand areas X 957 measures per area = 10,527 needed measures to solve
16
Medford NWP
La Grande
WA Both
ID Both

## Slide 17: Sendout and DSM Issues
Attempts to group measures
  Unique measures can have different curves and device lives
  Intent of modeling DSM as a resource is to provide individual resources the ability to fill demand along the demand curve and not lump assumptions
  As the model works today, we would have to solve for individual area and class, each in a separate model; this would miss the mark on system optimization and peak day events
17

## Slide 18: 2018 Proposed Scenarios
18

## Slide 19: Existing Resources vs. Peak Day Demand Expected Case – Washington/Idaho
19

## Slide 20: Decarbonization of Natural Gas
Renewable Natural Gas (RNG)
Energy Efficiency
Hydrogen (H2)
$4+ per therm
$1.10 – $3.90 per therm
$0.49 per therm
20

## Slide 21: 2020 IRP - Action Items
Dynamic DSM - In the 2020 IRP, each portfolio will have the ability to select conservation to meet unserved customer demand. Avista will explore methods to enable a dynamic analytical process for the evaluation of conservation potential within individual portfolios.
Distribution as supply option - Work with Staff to get clarification on types of natural gas distribution system analyses for possible inclusion in the 2020 IRP.
Distribution in avoided cost calculation - Work with Staff to clarify types of distribution system costs for possible inclusion in our avoided cost calculation.
Weather standard - Revisit coldest on record planning standard and discuss with TAC for prudency.
Supply resource optimization benefits - Provide additional information on resource optimization benefits and analyze risk exposure.
DSM—Integration of ETO and AEG/CPA data. Discuss the integration of ETO and AEG/CPA data as well as past program(s) experience, knowledge of current and developing markets, and future codes and standards.
Carbon Costs – consult Washington State Commission’s Acknowledgement Letter Attachment in its 2017 Electric IRP (Docket UE-161036), where emissions price modeling is discussed, including the cost of risk of future greenhouse gas regulation, in addition to known regulations.
*A few additional action items specific to Oregon
21