## Slide 1: Real Reliability The Value of Virtual Power
Washington UTC Resource Adequacy Meeting
July 24, 2023
Prepared by
  Ryan Hledik
  Kate Peters

## Slide 2: What Is a VPP?
Power system
Utility or aggregator
DERs are controlled by utility
Utility manages DERs to provide grid benefits
1
2
Virtual Power Plant
Examples of potential elements
Smart thermostats
Electric vehicles (EVs)
Rooftop solar PV
Distributed batteries
Smart water heaters
Commercial building automation systems
Shared cost savings
4
Power system costs & emissions are reduced
3
A VPP is portfolio of distributed energy resources (DERs) that are actively controlled to provide benefits to the power system, consumers, and the environment.

## Slide 3: VPPs are at a deployment inflection point
Homes with Smart Thermostats
Residential Rooftop Solar
Light-Duty Electric Vehicles
Homes with Electric Water Heating
Behind-the-Meter (BTM) Batteries
PRESENT | 2030
10% | 34%
PRESENT | 2030
27 GW | 83 GW
PRESENT | 2030
3 mil. | 26 mil.
PRESENT | 2030
49% | 50%
PRESENT | 2030
2 GW | 27 GW
Drivers
  Declining DER costs
  Technological advancement
  Inflation Reduction Act
  FERC Order 2222
  Growing model availability
  The decarbonization imperative

## Slide 4: Resource adequacy needs persist in the US
Historical U.S. Capacity Additions for Resource Adequacy
~110 GW, 2012-2021
 | Battery
 | Gas
  $120 billion of investment in past decade
  Driven by electrification, coal retirements, and growing renewables dependence
  Our study:
    Can VPPs reliably serve this resource adequacy need?
    And can they compete economically with gas peakers and batteries?

## Slide 5: The modeled VPP can fully provide 400 MW of resource adequacy for a moderately-sized utility
 | Net Load
 | Net Load
 | After Dispatch
Home Managed EV Charging
Smart Water Heating
Smart Thermostat
BTM Battery
VPP shifts customer usage to low cost hours
Hour of Day
Peak Net Load Day
400 MW Reduced Load
The VPP reduces load in:
Summer and winter
7 months
63 hours of the year
7 consecutive hours
We modeled four commercially available residential demand flexibility technologies for an illustrative utility composed of 1.7 million customers

## Slide 6: Simulated VPP dispatch is based on observed performance in actual deployments
EV Home Charging Load Profile Relative to Hourly System Costs
(Average across days and EV portfolio)
1
2
3
4
5
Max 1 event per day
 | Before Dispatch
 | After Dispatch
 | Emissions
 | Energy

## Slide 7: Resource Adequacy… For Cheap
Annualized Net Cost of Providing 400 MW of Resource Adequacy
RMI estimated that 60 GW of VPPs could be deployed nationally by 2030. At that scale, VPPs would save $15 to $35 billion in resource costs relative to the alternatives over 10 years … plus $20 billion in societal benefits

## Slide 8: The VPP could provide resource adequacy at a negative net cost to society
Net Cost of Providing 400 MW of Resource Adequacy
(Range observed across all sensitivity cases)
High
Low
Base
Gas
Battery
VPP
In markets with higher T&D costs or higher GHG emissions costs, the additional (i.e., non-resource adequacy) value of a VPP can outweigh its costs
Economic competitiveness of battery storage and VPPs varies across markets, depends trajectory of future cost declines.

## Slide 9: The ideal conditions for VPP deployment
MARKET DESIGN
  Wholesale markets provide a level playing field for demand-side resources.
  Retail rates and programs incentivize participation in innovative, customer-centric ways.
Maximized
VPP Value
MARKET
DESIGN
POLICY
SUPPORT
TECH
INNOVATION
REGULATORY
FRAMEWORK
TECHNOLOGY INNOVATION
  DERs are widely available and affordable. DERs can communicate with each other and the system operator.
  Algorithms effectively optimize DER use while maintaining customer comfort and convenience.
REGULATORY FRAMEWORK
  Utility business model incentivizes deployment of VPPs wherever cost-effective.
  Utility resource planning and evaluation accounts for the full value of VPPs.
POLICY SUPPORT
  Codes and standards promote deployment of flexible end-uses.
  R&D funding supports removal of key technical barriers.

## Slide 10: Three low-risk actions utilities and regulators can take now
Conduct a jurisdiction-specific VPP market potential study. Then establish VPP procurement targets.
Establish a VPP pilot. Test innovative utility financial incentive mechanisms.
Review and update existing policies to comprehensively account for VPP value.
For more information:
https://www.brattle.com/real-reliability/

## Slide 11: Appendix

## Slide 12: VPPs can provide several additional major benefits not modeled in this study
Increased renewables deployment
Better power system integration of electrification
Faster grid connection
Flexible scaling
Enhanced customer satisfaction
Improved behind-the-meter grid intelligence

## Slide 13: We conducted hourly reliability analysis for a VPP, a gas peaker, and a utility-scale battery
Utility Hourly Net Load Profile
400 MW Reduced Load
Net Load (gross system load minus renewable generation)
63 hrs must be addressed to serve top 400 MW of load
The illustrative utility
  Mid-sized (1.7 million customers)
  50% renewables by 2030
  Winter and summer resource adequacy needs
Defining resource adequacy
  Serve all load contributing to top 400 MW of net peak demand
  Requires performance during 63 hours of the year
  7 consecutive hours in one day

## Slide 14: We modeled a VPP composed of four commercially available residential load flexibility technologies
 | Smart Thermostat DR | Smart Water Heating | Home Managed EV Charging | BTM Battery DR
Eligibility (% of residential customer base) | 67% summer; 35% winter | 50% | 15% | 1%
Participation (% of eligible customers) | 30% | 30% | 40% | 20%
Total Controllable Demand at Peak (MW) | 204 MW | 114 MW | 79 MW | 26 MW
VPP Operational Constraints | 15 five-hour events per season, plus 100 hrs of minor setpoint adjustments per year and energy savings | Daily load shifting of water heating load, ancillary services | Daily load shifting of vehicle charging load | 15 demand response events per year
We model all utility-incurred costs (incentives, implementation including marketing and per-unit DERMS costs)