## Slide 1: July 24, 2023
Saad Malik (Director, Reliability Assessments)
Victoria Ravenscroft (Sr. External Affairs & Policy Manager)
Washington Department of Commerce & Utilities and Transportation Commission Meeting

## Slide 2: Responsibility for Reliability
§215 Federal Power Act—
FERC certifies an Electric Reliability Organization (ERO)
The ERO may delegate authority to Regional Entities
The Regional Entity carries out delegated responsibilities

## Slide 3: WECC’s Work
WECC has a responsibility to help create, monitor, and enforce reliability standards and promote activities that ensure the reliability of the Bulk Power System in the Western Interconnection.
Develop, monitor, and enforce mandatory reliability standards
Identify and assess emerging risks
Analyze and evaluate system performance
Educate and share information

## Slide 4: WECC’s Reliability Risk Priorities

## Slide 5: Summer 2023 Assessment Highlights
All areas are resource adequate at the peak hour
Demand is at risk outside of the peak hours
Supply chain issues
Heat waves
Wildfires

## Slide 6: Trajectories of New Renewable Resources
Chart: Cumulative Capacity of Renewables, 2012-2032
Pumped Storage | 4366 | 4366 | 4366 | 4366 | 4366 | 4366 | 4366 | 4366 | 4366 | 4536 | 4536 | 4706 | 4706 | 4706 | 4706 | 4706 | 4706 | 4706 | 4706 | 5333 | 5333 | 5333
Hydro | 61454.44 | 61871.12 | 62868.25 | 64500.53 | 64850.19 | 66400.28 | 67024.01 | 67982.41 | 69390.53 | 69623.38 | 69653.28 | 70076.59 | 70839.91 | 71030.74 | 71780.74 | 72335.94 | 72861.84 | 72917.74 | 72972.64 | 73044.64 | 73489.64 | 73934.64
Wind | 18185.28 | 18897.12 | 20096.02 | 20938.7 | 21461.37 | 23282.32 | 24431.74 | 26026.19 | 30381.76 | 34060.3 | 36602.3 | 39831.18 | 42105.63 | 44325.93 | 46455.93 | 46955.93 | 48039.93 | 48601.53 | 49359.13 | 53374.13 | 53899.13 | 54024.13
Solar | 2438.17 | 5755.76 | 8509.09 | 10302.779 | 15219.319 | 17015.7982 | 18240.8749 | 20836.5299 | 23589.7044 | 26752.0907 | 30782.1654 | 45254.1654 | 52284.9654 | 58610.9654 | 62618.9654 | 63992.9654 | 65602.9654 | 66532.9654 | 67618.9654 | 81432.9654 | 82789.9654 | 83039.9654
BESS | 0.8 | 5.8 | 7.8 | 8.8 | 86.8 | 148.7 | 210.7 | 220.7 | 701.06 | 2517.41 | 4572.41 | 11743.69 | 14739.69 | 15929.69 | 16484.69 | 16499.69 | 17251.19 | 17516.19 | 17974.19 | 27547.08 | 27993.08 | 28093.08
Chart: Nameplate Capacity of Incremental New Renewables 2016-2022, and 2023 Planned
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Pumped Storage Annual | 170 | 170
Hydro Annual | 349.66 | 1550.09 | 623.73 | 958.4 | 1408.12 | 232.85 | 29.9 | 423.31
Wind Annual | 522.67 | 1820.95 | 1149.42 | 1594.45 | 4355.57 | 3678.54 | 2542 | 3228.88
Solar Annual | 4916.54 | 1796.4792 | 1225.0767 | 2595.655 | 2753.1745 | 3162.3863 | 4030.0747 | 14472
BESS Annual | 78 | 61.9 | 62 | 10 | 480.36 | 1816.35 | 2055 | 7171.28

## Slide 7: 2022 Resources (Planned minus Actual)
Chart: 
Geothermal | 67.9
Hydro | -350.96
Solar | -2807.3053
Wind | 129.26
Natural Gas | -407.3
Energy Storage | -330.4
Other (Bio) | -45.25

## Slide 8: Energy Emergency Alerts (EEA)
Chart: EEA Events by Year
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 (YTD)
EEA-1 | 3 | 5 | 8 | 26 | 7 | 11 | 1
EEA-2 | 4 | 15 | 14 | 6 | 5 | 8
EEA-3 | 4 | 4 | 16 | 14 | 3 | 15 | 3

## Slide 9: Demand at Risk
Demand at Risk

## Slide 10: Western Assessment of Resource Adequacy
Assessment footprint
  Western Interconnection
  Five subregions
10-year, hourly analysis (2023-2032)
Probabilistic approach
Data comes from WECC Balancing Authorities
  Includes expected demand and resource information

## Slide 11: Demand-at-Risk Hours Results
Subregional Demand-at-Risk Hours
2023-2032
(with New Resources and Imports)
Chart: CAMX
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
2021 Assessment | 8 | 23 | 42 | 57 | 68 | 83 | 103 | 106 | 3
2022 Assessment | 1 | 5 | 23 | 48 | 67 | 75 | 115 | 116 | 6 | 8
Chart: NWPP-Central
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
2021 Assessment | 11 | 29 | 54 | 92 | 120 | 224 | 408 | 397 | 400
2022 Assessment | 0 | 4 | 18 | 42 | 80 | 134 | 209 | 263 | 481 | 656
Chart: NWPP-NE
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
2021 Assessment | 13 | 17 | 59 | 94 | 773 | 872 | 1187 | 1235 | 1270
2022 Assessment | 0 | 0 | 0 | 20 | 60 | 85 | 146 | 185 | 112 | 145
Chart: NWPP-NW
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
2021 Assessment | 1 | 2 | 30 | 47 | 66 | 90 | 92 | 91 | 27
2022 Assessment | 0 | 0 | 0 | 3 | 16 | 17 | 40 | 31 | 2 | 5
Chart: DSW
| 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032
2021 Assessment | 0 | 3 | 10 | 13 | 28 | 61 | 87 | 101 | 24
2022 Assessment | 0 | 0 | 5 | 17 | 52 | 85 | 128 | 124 | 72 | 100
2021 Assessment 2022 Assessment

## Slide 12: Western Assessment of Resource Adequacy
While there has been some improvement in near-term (2–3 years) resource adequacy risk, it has not been eliminated
  Actions like retirement delays and expedited building of resources
Likelihood and magnitude of resource adequacy risk have increased compared to previous analyses
Long-term, the risk increases over the next 10 years
Variability drives resource adequacy risk, and variability increases over the next decade

## Slide 13: Year 20 Assessments
Year 20 Foundational Case Development
Extreme Heat
Extreme Cold
Impact of Changing Loads
Transmission Trends