BEFORE THE WASHINGTON UTILITIES AND TRANSPORTATION COMMISSION

| GRANT COUNTY Petitioner, v. COLUMBIA BASIN RAILROAD COMPANY Respondent. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | ) ) ) ) ) ) ) ) ) ) ) ) | DOCKET NO. TR-020114 ORDER GRANTING PETITION TO RECONSTRUCT A HIGHWAY-RAIL GRADE CROSSING AT Q NE ROAD D.O.T. 089809W W.U.T.C. 34C 150.30 |
| --- | --- | --- |

# BACKGROUND

- On February 4, 2002, Grant County filed a petition with the Commission, seeking authority to reconstruct a highway-rail grade crossing.  The crossing is located at the intersection of Q NE Road and the tracks of the Columbia Basin Railroad Company, in the SE ¼ of the SE ¼ of Section 26, Township 29, Range 19 E, W.M., in Grant County, Washington.

- Respondent has consented to an entry of an order by the Commission without further notice or hearing.

# DISCUSSION

- Q NE Road, in the vicinity of the crossing, is classified as a rural-collector road.  The roadway consists of a gravel surface, with one lane for each direction of traffic and a vehicle speed limit of 50 MPH.  Average daily traffic through the crossing is estimated to be 200 vehicles.  The roadway and tracks intersect at a slightly acute angle, and sight distance down the tracks is restricted for the north-bound approach to the crossing due to presence of a house and fence in the southeast quadrant of the crossing.

- Respondent maintains one main track through the crossing.  Daily train traffic includes two freight trains operating at a maximum timetable speed of 25 MPH.

- The petition to reconstruct the crossing is related to a Grant County roadway improvement project that includes paving Q NE Road, including the portion that crosses the tracks.  In addition to paving the roadway approaches to the crossing, the parties have agreed to install a concrete crossing surface.

- Warning devices at the crossing include standard Crossbuck signs and Stop signs.  Petitioner seeks to upgrade the warning devices at the crossing through the installation of shoulder-mounted flashing-light signals.  The upgrades are being proposed in the interest of improving safety for the motoring public.

- Commission Staff investigated the petition and recommended that it be granted, subject to specified conditions.

- This matter was brought before the Commission at its regularly scheduled open meeting on May 8, 2002.  The Commissioners have reviewed the petition and have been advised in the matter.  They believe that granting the petition, subject to the conditions set forth below, is in the public interest, and direct the Secretary to issue the Order.

# O R D E R

- THE COMMISSION GRANTS the petition of Grant County to reconstruct and upgrade the warning devices at a highway-rail grade crossing located at the intersection of Q NE Road and the tracks of the Columbia Basin Railroad Company, in Grant County, Washington, subject to the following conditions.

  - The upgrades must conform to the plans filed in this proceeding.

  - Traffic control devices must comply with all applicable standards specified in the U.S. Department of Transportation Manual on Uniform Traffic Control Devices.

  - Traffic control devices and instrument housing must be installed in such a manner as to provide the required clearances for both rail and vehicular traffic.

  - Grant County must remove the Stop signs at the crossing at such time that active warning devices become operational.

  - The roadway grade for 25 feet on each side of the centerline of the railway at the crossing must be level.

  - The crossing must be hard-surfaced between the rails and for a distance of one foot outside of each rail for the full width of the traveled roadway.

  - Upon completion of the reconstruction and installations authorized herein, Petitioner must notify the Commission.  Acceptance of the changes is subject to a compliance inspection by Commission Staff, verifying that they are in full compliance with law, regulation, and the conditions specified herein.

DATED at Olympia, Washington and effective this 8th of May, 2002.

WASHINGTON UTILITIES AND TRANSPORTATION COMMISSION

CAROLE J. WASHBURN, Secretary