## Slide 1: Cascade Natural Gas 2014 Integrated Resource Plan Overview
September 10, 2015
WUTC Presentation
Olympia, Washington

## Slide 2: Overview
Introductions 
2014 IRP
  Demand Forecast 
  Distribution System Enhancements
  Demand Side Management
  Supply Side Resources
  Resource Integration
Two-Year Action Plan: Action Items will be noted throughout.

## Slide 3
Cascade anticipates its Core Customer Base will continue to grow over the planning horizon, with annual throughput anticipated to increase between 1.0% and 1.2% per year.
Chart: Throughput By Class
| Residential | Commercial | Core Market Industrial | Non Core Industrial
 | 0.13 | 0.1 | 0.02 | 0.75

## Slide 4: Demand Forecast Summary

## Slide 5: Load Growth
Period | Low | Mid | High
2012 | 299,970,548 | 301,803,755 | 303,636,961
2020 | 310,390,084 | 321,795,524 | 333,666,127
2025 | 317,840,415 | 339,187,714 | 362,250,502
2030 | 326,362,761 | 357,990,520 | 393,367,474
2034 | 332,954,119 | 372,970,513 | 418,914,457
Deviation | (40,016,394) |  | 45,943,944

## Slide 6: Peak Day Forecast:
Developed in conjunction with annual basis load forecasts.
Enable Cascade to make prudent distribution system and peak capacity planning decisions to fulfill our responsibility to provide heating under all but force majeure conditions.
Method:
  Historically, Cascade developed peak day forecasts based on a 65 HDD day (0°F) to reflect the coldest day in Cascade’s 60-year weather history.
  In 2008, Cascade’s IRP changed this practice to reflect the coldest day during the past 30 years. This record is held by December 21, 1990 at 61 HDDs.
  In 2014, Cascade’s IRP changed the HDD reference temperature to 60°F, therefore, a 60 HDD day is 0°F. The coldest day on record is still held by December 21, 1990 at 56 HDDs.
  HDDs for the December 21, 1990 day is applied to each CityGates regression and escalated into the future at the forecasted therm usage annual growth rate.
To ensure satisfaction of core customer demand on the coldest days

## Slide 7: Peak Day Forecast:
This method rests on the assumption that core market load shape does not significantly change throughout the forecast horizon.
Cascade believes the peak day forecast conservatively overestimates peak day usage because the base forecast does not explicitly include future conservation measures implemented by customers that would act to increase energy efficiency and reduce daytime therm usage.

## Slide 8: Overview
Introductions 
2014 IRP
  Demand Forecast 
  Distribution System Enhancements 
  Demand Side Management
  Supply Side Resources
  Resource Integration
Two-Year Action Plan: Action Items will be noted throughout.

## Slide 9: Distribution System pipeline, gate station, and other related projects

## Slide 10: Overview
Introductions 
2014 IRP
  Demand Forecast 
  Distribution System Enhancements 
  Demand Side Management 
  Supply Side Resources
  Resource Integration
Two-Year Action Plan: Action Items will be noted throughout.

## Slide 11: Washington Demand Side Management
Presented by Monica Cowlishaw Manager, Energy Efficiency and Community Outreach

## Slide 12: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Inputs & Assumptions
  Outcome
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 13: HIGHLIGHTS
Separation of Oregon & Washington
Nexant Study

## Slide 14: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Outcome
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 15: EM&V

## Slide 16: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Final Program Goals Outcome
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 17: INPUTS & ASSUMPTIONS
20 year volume & customer figures by rate class
Load Profile
2014 Avoided Costs
Long-term Discount Rate = 4.17%
Inflation Rate = 2%
Transmission Loss Rate = 0.1959%
Incentive level = 30%
UCT under UG 121207
  Cost effectiveness ≥ 0.90

## Slide 18: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Outcome
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 19: MODEL
Technical
Economic
Achievable
Program
Represents substitution of all technically feasible measures at the end use level.
Considers the most efficient measures that pass economic screening tests.
Reflects assumptions about decisions consumers make regarding the efficiency of the equipment they purchase, to simulate a realistic estimate of real-life conditions.
Subset of achievable potential attainable given constraints on program budget and implemented measures.

## Slide 20: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Final Programmatic Plan
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 21: PLAN
Chart: Annual Incremental Energy Savings Program Goal Forecast 2015-2034
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034
Com/Ind w/ Custom Programatic | 394390.7143 | 423047.1429 | 455702.1429 | 496650 | 549621.4286 | 615660 | 685525.7143 | 764359.2857 | 845747.1429 | 929648.5714 | 999574.2857 | 1066320 | 1123945.7143 | 1178235 | 1197053.5714 | 1230570 | 1259065.7143 | 1298436.4286 | 1316528.5714 | 1333212.8571
Realistic Residential | 132084.75 | 138073.75 | 284585 | 295123.75 | 307570.5 | 323250.25 | 337396.25 | 353822.5 | 370797.75 | 388645.5 | 401940.25 | 415556.5 | 427574 | 439742.25 | 446846.5 | 454904.75 | 462117.25 | 472184.25 | 476373.25 | 482057.25
Low Income | 7000 | 7000 | 15000 | 15000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000

## Slide 22: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Final Program Goals Outcome
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 23: INCENTIVE LEVEL MEASURE IMPACTS
Chart: Current Measures Passing Cost-Effectiveness by Incentive Level
| Res 30% | Res 50% | Res 75% | Com 30% | Com 50% | Com 75% | Ind 30% | Ind 50% | Ind 75%
Current Measures | 0.92105 | 0.75 | 0.47368 | 0.56752 | 0.48034 | 0.4 | 0.29167 | 0.25 | 0.083333

## Slide 24: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Final Program Goals Outcome
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 25: TECHNOLOGICAL FRONTIER
Energy code changes
  Water Heaters
  Air Sealing
  Furnaces
NWPCC Building Forecast
Emerging Technologies & NEEA Results
Incorporation of new measures

## Slide 26: POLITICS
State Legislation
  SB 5854
DOC Biennial Energy Report
WCI GHG Cap & Trade Design
Federal legislation traction
C02/GHG Tax Options

## Slide 27: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Final Program Goals Outcome
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 28: LOW INCOME
Declining trend in weatherization for Low-Income Natural Gas Heated Homes
  US DOE-WAP Priority Guidelines
  Current Low Income Weatherization Environment
2015 Therm savings projection is similar to 2014 therm savings achieved.
The company has decreased expected savings from the 2012 IRP estimates due to these factors.

## Slide 29: AGENDA:
Highlights
Nexant Potential Study
  EM&V
  Inputs & Assumptions
  Model
  Final Program Goals Outcome
  Incentive Level Scenarios
Political & Technological Frontier
Low Income Program Status
Action Plan

## Slide 30: ACTION PLAN
Reducing DSM chapter and transitioning to Conservation Plan in December, 2015.
Support communities participating in the GUEP.
Collaborate with NEEA to promote market transformation, technology research and implementation strategies.
Discuss alternative incentive level options and potential tariff revisions with our CAG.

## Slide 31: Questions?
Monica Cowlishaw
Manager, Energy Efficiency & Community Outreach
Monica.Cowlishaw@cngc.com
Amanda Sargent
Conservation Analyst II
Amanda.Sargent@cngc.com

## Slide 32: Overview
Introductions 
2012 IRP
  Demand Forecast 
  Distribution System Enhancements 
  Demand Side Management 
  Supply Side Resources 
  Resource Integration
Two-Year Action Plan: Action Items will be noted throughout.

## Slide 33: GSOC & Risk Management
In the 2014 IRP, Cascade has assumed that current forward price curves for natural gas are comparatively low and expected to remain in the $3-6 range.
Approximately Year 1: 70-80% of annual requirements; Year 2: 40%, Year 3: 20%. GSOC should consider a modification from portfolio if: 1) reasonable concerns exist regarding the availability of supply in a particular basin; 2) the outer year 3 year forward price is 20% higher/lower than the front month over a reasonably sustained period.
Due to expected lack of prolonged or significant price volatility, no financial derivatives are to be included in the portfolio. Hedging in the portfolio is through fixed priced physical gas supply contracts.

## Slide 34: Price Picture

## Slide 35: Principle supply and transport paths

## Slide 36: Transport paths at time of 2014 IRP

## Slide 38: Storage Services
 | Storage Capacity (therms) | Withdrawal (therms/day)
Jackson Prairie (Principle) | 6,043,510 | 167,890
Jackson Prairie (Expansion) | 3,500,000 | 300,000
Plymouth LNG | 5,622,000 | 600,000
Jackson Prairie (new - 2012) | 2,812,420 | 95,770
Both of the Jackson Prairie facilities and Plymouth are located directly on NWP's transmission system.
Because of that, storage withdrawal rates can be changed several times during an individual gas day to accommodate weather driven changes in core customer requirements.

## Slide 46: Overview
Introductions 
2012 IRP
  Demand Forecast 
  Distribution System Enhancements 
  Demand Side Management 
  Supply Side Resources 
  Resource Integration 
Two-Year Action Plan: Action Items will be noted throughout.

## Slide 47: Sampling of citygates with peak day upstream pipeline capacity concerns
Citygate | 2021 Capacity Under-utilized/(Short) on Peak Day | 2026 Capacity Under-utilized/(Short) on Peak Day | 2031 Capacity Under-utilized/(Short) on Peak Day | 2032 Capacity Under-utilized/(Short) on Peak Day | 2033 Capacity Under-utilized/(Short) on Peak Day
Arlington | -3,795 | -4,266 | -4,735 | -4,829 | -4,922
Beauchene Rd (Moxee) | -1,335 | -1,373 | -1,410 | -1,418 | -1,425
Bend | -5661 | -7516 | -9355 | -9722 | -10087
East Stanwood | -578 | -658 | -738 | -753 | -770
Kennewick | -14,842 | -16,408 | -17,954 | -18,262 | -18,568
Madras | -1272 | -1366 | -1463 | -1482 | -1502
Mount Vernon | -5,428 | -6,179 | -6,925 | -7,074 | -7,222
North Pasco | -7,136 | -7,675 | -8,207 | -8,313 | -8,418
Oak Harbor/Stanwood | -3,980 | -4,673 | -5,365 | -5,503 | -5,640
Redmond | -7510 | -8590 | -9662 | -9875 | -10088
S. Bend | -8800 | -11156 | -13495 | -13960 | -14425
Stearns | -2485 | -3071 | -3652 | -3767 | -3883
Walla Walla | -3,414 | -3,409 | -3,408 | -3,408 | -3,408
Yakima/Union Gap | -9,942 | -10,210 | -10,480 | -10,533 | -10,587

## Slide 48: Area Storage

## Slide 49: Alternative Resources– another view (source: NWGA)

## Slide 50: Addressing Resource Concerns

## Slide 51: Addressing Resource Concerns

## Slide 52: 20 Year Portfolio Costs NPV
SCENARIO NAME | IN $000s | AVG. COST PER THEM
As Is Scenario | $ 5,198,207 | $ 0.609505
Base Case | $ 5,198,207 | $ 0.609505
All in Case | $ 5,199,687 | $ 0.609835
Ryckman Creek | $ 5,209,426 | $ 0.620024
Limited Canadian Imports | $ 5,212,722 | $ 0.620410
Mist | $ 5,247,142 | $ 0.624446
All Storage Options | $ 5,265,794 | $ 0.626633
T-South Enhancement with incremental Sumas (WA Expansion) | $ 5,281,914 | $ 0.628523
T-South Enhancement/Southern Crossing | $ 5,292,254 | $ 0.629736
Pacific Northwest Regional (NMAX, WA Expansion) | $ 5,293,561 | $ 0.629889
Wild Goose | $ 5,294,807 | $ 0.630035
Gill Ranch | $ 5,313,505 | $ 0.632228

## Slide 53: Questions?
 Contact Information:
  Mark Sellers-Vaughn, Manager of Supply Resource Planning
  509-734-4589, Mark.Sellers-Vaughn@cngc.com
  Brian Robertson, Supply Resource Planning Analyst II
  509-734-4546, Brian.Robertson@cngc.com
  Monica Cowlishaw, Manager, Energy Efficiency & Community Outreach
  360-788-2357, Monica.Cowlishaw@cngc.com
  Amanda Sargent, Conservation Analyst II
  360-788-2347, Amanda.Sargent@cngc.com
  Jeremy Ogden, Director, Engineering Services
  509-734-4509, Jeremy.Ogden@cngc.com
  Jon Whiting, Director of Gas Supply and Control,
  (509) 7340-4549, Jon.Whiting@cngc.com