## Slide 1
Washington Utilities and Transportation Commission
Docket UE-140546
Recessed Open Meeting
June 25, 2015

## Slide 2: 2015 IRP Highlights
No new generating resources in the action plan.
  Near-term resource needs continue to be met with demand-side management (DSM) and Front office Transactions (FOTs).
  The first new generating resource, a 423 MW CCCT, is not needed until 2028.
  We will issue at least annually, RFPs seeking unbundled RECs that will qualify in meeting Washington renewable portfolio standard targets through 2017.
No new emission control installations in the action plan.
  Naughton Unit 3 natural gas conversion in 2018.
  Cholla Unit 4 permitting to cease coal-fueled operations by the end of April 2025.
  Currently no plans to install selective catalytic reduction (SCR) at Dave Johnston Unit 3 or Wyodak.
  By the end of the 20-year planning horizon, it is assumed that approximately 2,800 MW of existing coal-fueled generation will either be retired or converted to burn natural gas.
Complete construction of the transmission customer-driven Wallula to McNary transmission project and continue Energy Gateway permitting activities.

## Slide 3: Key Elements of PacifiCorp’s IRP Process
7 Public Input Meetings
  Initiated June 5, 2014
  4 of the 7 meetings scheduled as two-day sessions
5 State-Specific Meetings
  Held over the course of June 2014
2 Technical Workshops
  Portland/Salt Lake City to review the 111(d) modeling tools
Portfolio Modeling
  33 core case portfolios
  15 sensitivity studies
Public Input/Feedback Form
10 Supplemental Studies
  Conservation Potential Study
  Distributed Generation Study
  Wind Integration Study
  Planning Reserve Margin Study
  Wind & Solar Capacity Contribution Study
  Stochastic Parameter Study
  Anaerobic Digester Resource Assessment
  Energy Storage Screening Study
  Flexible Resource Needs Assessment
  Resource Adequacy Evaluation
Filed March 31, 2015
  Filing includes 5 DVD data disks

## Slide 4: 2015 IRP Preferred Portfolio
Firm market purchases (labeled as FOTs) are down 29% relative to the 2013 IRP
Accumulated acquisition of new energy efficiency resources account for 86% of load growth over the next decade
First deferrable thermal resource, new combined cycle plant, is added the portfolio in 2028
By 2034 approximately 2,800 MW of existing coal capacity is assumed to retire or be converted to burn natural gas
The portfolio reflects 816 MW of qualifying facility power purchase agreements from wind and solar projects expected to come online in 2015 and 2016
CO2 emissions are projected to fall below 1990 levels by 2025, and fall 14% below 1990 levels by 2034

## Slide 5: Preferred Portfolio: Class 2 DSM
Penetration of energy efficiency is up 59% by 2024 relative to the 2013 IRP, driven by opportunities in:
  Cost-effective lighting
  Heating & cooling
  Water heating
  Appliances
  Industrial process end-uses

## Slide 6: Preferred Portfolio: Front Office Transactions
With increased energy efficiency, reliance on FOTs (or short-term firm market purchases) is reduced as compared to the 2013 IRP Preferred Portfolio.
Over the 2015–2024 period, FOTs are approximately 29% lower when compared to the 2013 IRP preferred portfolio.
  West-side market purchases are reduced at COB and Mid-C.
  East-side market purchases are reduced at Mona (eliminated through the front ten years of the planning horizon).

## Slide 7: 2015 IRP – Transmission
Segment & Name | Status | Scheduled In-Service
(A) Wallula-McNary | Status: local permitting completed | 2017 sponsor driven
(B) Populus-Terminal | Completed and in-service November 2010 | 
(C) Mona-Oquirrh | Completed and in-service May 2013 | 
(C) Oquirrh-Terminal | Rights-of-way acquisition underway | June 2021
(D) Windstar-Populus | Permitting underway | 2019-2024
(E) Populus-Hemingway | Permitting underway | 2019-2024
(F) Aeolus-Mona | Permitting underway | 2020-2024
(G) Sigurd-Red Butte | Completed and in-service May 2015 | 
(H) Boardman to Hemingway | Pursuing joint-development and/or firm capacity opportunities with project sponsors | Sponsor driven

## Slide 8: 2015 IRP Regional Haze Scenarios
Coal Unit | Reference | RH-1 | RH-2 | RH-3
Dave Johnston 1 | Shut Down Dec 2027 | Shut Down Mar 2019 | Shut Down Mar 2019 | Shut Down Dec 2027
Dave Johnston 2 | Shut Down Dec 2027 | Shut Down Dec 2027 | Shut Down Dec 2023 | Shut Down Dec 2027
Dave Johnston 3 | SCR by Mar 2019; Shut Down Dec 2027 | Shut Down Dec 2027 | Shut Down Dec 2027 | Shut Down Dec 2027
Dave Johnston 4 | Shut Down Dec 2027 | Shut Down Dec 2032 | Shut Down Dec 2032 | Shut Down Dec 2027
Hunter 2 | SCR by Dec 2021 | Shut Down by Dec 2032 | Shut Down by Dec 2024 | Shut Down by Dec 2032
Huntington 1 | SCR by Dec 2022 | Shut Down by Dec 2036 | Shut Down by Dec 2024 | SCR by Dec 2022
Huntington 2 | SCR by Dec 2022 | Shut Down by Dec 2021 | Shut Down by Dec 2021 | Shut Down by Dec 2029
Jim Bridger 1 | SCR by Dec 2022 | Shut Down by Dec 2023 | Shut Down by Dec 2023 | SCR by Dec 2022
Jim Bridger 2 | SCR by Dec 2021 | Shut Down by Dec 2032 | Shut Down by Dec 2028 | SCR by Dec 2021
Wyodak | SCR by Mar 2019 | Shut Down by Dec 2039 | Shut Down by Dec 2032 | Shut Down by Dec 2039
Common to All Scenarios:
Carbon 1&2 shutdown 2015; Cholla 4 gas conversion 2025; Colstrip 3&4 SCR 2023/2022, respectively; Craig 1&2 SCR 2021/2018, respectively; Hayden 1&2 SCR 2015/2016, respectively; Naughton 1&2 shutdown 2029; Naughton 3 gas conversion 2018, shutdown 2029; Hunter 1&3 SCR 2021/2024, respectively; and Bridger 3&4 SCR 2015/2016, respectively

## Slide 9: 111(d) Modeling in the 2015 IRP
111(d) Compliance Scenarios
  Emission rate targets (all states/retail states)
  Emission rate targets and future CO2 prices
  Mass cap (existing resources only/new and existing resources)
Emission Rate Target Scenarios
  State emission rate targets are applied to each PacifiCorp state
  New combined cycle plants are subject to 111(b) and 111(d) and therefore, not allowed in Oregon, Washington, and Idaho
  Flexible allocation of system renewable resources and energy efficiency from Idaho and California
  Allocation of system renewables for 111(d) compliance are independent from RECs used for state RPS compliance
  Sensitivity requiring concurrent use of RECs for RPS with 111(d) renewables

## Slide 10: 111(d) Emission Rate Target Modeling Steps
Compliance Strategies (111(d) Emission Rate Target Scenarios)
Prioritize re-dispatch with base energy efficiency
Prioritize re-dispatch with incremental energy efficiency
Prioritize new renewable resources with incremental energy efficiency

## Slide 11: Balancing Authority Area Sensitivity: S-10
The Washington Utilities and Transportation Commission requested the Company model the East and West control areas separately:
  “The Company must model the two areas separately in the next IRP as a prerequisite for acknowledgement.”
S-10 assesses the impact of independently planning for a sub-system as compared to planning for PacifiCorp’s system as a whole.
Sub-systems are defined by PacifiCorp’s east and west balancing authority areas (BAAs), also referred to as east and west control areas (ECA and WCA).
Comparison of ECA and WCA standalone resource portfolios to benchmark system portfolio.
  Benchmark system portfolios is derived under Regional Haze Scenario 3 and assumes unbundled REC strategy for state RPS, consistent with draft preferred portfolio.
  Portfolio and system cost impacts are reported.
  With and without 111(d).

## Slide 12: S10 Sensitivity: Overview of Assumptions
WCA standalone portfolio developed with System Optimizer.
  Winter peak, maintain 13% planning reserve margin.
  Allow January on-peak FOTs, maintaining limits at Mid C (775 MW), COB (300 MW), and NOB (100 MW)
  Class 2 DSM capacity contribution updated to align with a winter peak.
  With 111(d), assumes Chehalis is retired at the end of 2019, new CCCT resources are not allowed, and Oregon can use a WCA allocation of renewables to meet PacifiCorp’s share of its 111(d) targets.
  Without 111(d), new CCCT resources are allowed.
ECA standalone portfolio developed with System Optimizer.
  Summer peak, maintain 13% planning reserve margin.
  Summer on-peak FOTs, no access to west-side FOTs, but inclusion of Mona (300 MW).
  Class 2 DSM capacity contribution updated to align with a summer peak.
  With 111(d), assume flexible allocation of ECA renewable resources can be used to meet PacifiCorp’s share of Utah and Wyoming emission rate targets.

## Slide 13: S-10 Sensitivities: Summary of System Costs
System Optimizer results show that planning the system on a WCA standalone and ECA standalone basis leads to higher costs.
The incremental cost of planning for two standalone system increases under 111(d).
*Note, PaR results reflect resource portfolios developed under 111(d) but do not capture re-dispatch costs under 111(d).
Increase/(Decrease) Relative to the System Benchmark ($m) | System Optimizer | PaR Stochastic Mean |  | 
 | Medium Gas | Low Gas | Medium Gas | High Gas
Without 111(d) | $1,149 | n/a | n/a | n/a
With 111(d)* | $1,326 | $2,031 | $2,109 | $2,158

## Slide 14: S-10 Sensitivity : ECA+WCA Portfolio Results
As compared system benchmark portfolio, combined standalone ECA and WCA portfolios cannot rely on resource selections in the other BAA to meet their respective planning reserve margin targets.
January FOTs are needed for the WCA; and incremental DSM is needed for the ECA.
Without the ECA, the WCA includes a gas peaking resource in 2023 without 111(d) and in 2020 with 111(d) (coinciding with the retirement at Chehalis) and needs January FOTs
Without the WCA, the ECA no longer has access to west side FOTs and needs incremental Class 1 and Class 2 DSM resources; Mona FOT limit had to be increased to allow the ECA to achieve its target 13% planning reserve margin in 2015 – 2017 (711 MW, 459 MW, and 359 MW, respectively)
Total increase in System Optimizer PVRR = $1,149m without 111(d) and $1,326m with 111(d)