## Slide 1: Washington State Next Generation 911 System Carrier Summit
Washington State 911 Coordination Office
&
Comtech/NoaNet
September 5, 2018

## Slide 2: AGENDA
Welcome – Adam Wasserman
Introductions – Andy Leneweaver
  Around the Room, On the Phone, Web Only Participants
Overview of the Washington State NG 911 System
  NG911 System Overview – Andy Leneweaver
ESInet II Project Overview – Comtech
  Phases & Timing
ALI Transition – Comtech
  Scope – Project Team – Timing Details - Expectations
Carrier Transition – Comtech/NoaNet
  Scope – Project Team – Timing Details - Expectations
Questions – Andy Leneweaver
Way Ahead & Ending Thoughts – Adam Wasserman

## Slide 3: A Quick History of WA STATE 911
1968: “9-1-1” as an emergency number began in Alabama
  50th Anniversary celebrated February 16th
1969: Puyallup became first locality west of the Mississippi in the lower 48 to have a 911 call center
  (Now called Public Safety Answering Points – PSAPs)
1985: King County implemented first Enhanced 911 system in the state
1991: “Referendum 42” – “Shall Enhanced 911 emergency telephone dialing be provided throughout the state and be funded by a tax on telephone lines?” Passed Yes 61%, No 39%
1992: STATE ENHANCED 911 COORDINATION OFFICE (SECO) established to assist and facilitate statewide Enhanced 911 implementation
1996: Congress passes “Telecommunications Act of 1996”
  (addressed 9-1-1 at national level)
Washington State: A consistent national leader in development and refinement of 911 services

## Slide 4: A Quick History of WA STATE 911
1998: Statewide migration to Enhanced 911 begins – physical address and other information displayed for call-taker, selective routing to correct PSAP
2009: Migration to Next Generation—first step—interim NG911 Emergency Services Internet Protocol (ESInet) buildout begins – IPSR
  Completed 2012
2013-2016: PSAPs begin converting to “Next Generation” capable CPE
2014: SECO begins work to acquire a fully capable NG911 ESInet (II) that is designed to transport Calls, Text, data, Images & Video.
2016: Apparent Successful Bidder announced. Work begins on NG 911
2019: End-state is a NENA i3 (+) Standard Statewide NG911 ESInet connected to NG911-Capable Primary PSAPs.
Washington State: A consistent national leader in development and refinement of 911 services

## Slide 5
Statewide Services - Provided on behalf of all counties
  Statewide 911 System
  Tele-communicator Training
  Language Translation Services
  TTY/TDD Support and Training
  Technical Support
Financial Support to Maintain a Baseline Level of Service
  Support based on amount of local excise tax revenue
  County / WSP Contracts for some operational costs
  Capital equipment replacement (when/if funds available)
Coordinator Professional Development - Provided to all counties
  Training, coordination, and NG modernization
Washington State 911 Coordination office

## Slide 6: Revised Code of WA (RCW) WA Admin. Code (WAC)
911 RCWs - Chapter 38.52.500 thru 38.52.577
  Statewide Enhanced 911 Service
  State Enhanced 911 Advisory Committee
    Representing: NENA-WA, APCO-WA, various WA Law, Fire & EMS Associations, various WA city & county associations, large & small wireline & wireless providers, VOIP providers, the WA UTC and the WSP
911 Tax RCWs - Chapter 82.14B.030 thru 82.14B.210
  Establishes Tax on Telephone Access Line Use
  To be used only for the emergency services communication system
911 WACs – Chapter 118-66-010 thru 118-68-090
  118-66 – Defines/describes 911 Funding and eligibility
  118-67 – Defines/describes uniform technical and operational standards for wireless 911 calls
  118-68 – Defines/describes Automatic Location Information

## Slide 7: Evolving Nature of 9-1-1 Calls
17 Years ago (2000):
73% of 9-1-1 calls came from Landlines
27% came from ‘Cell Phones’
0% came from VoIP
Last Year (SFY 2017):
13% of 9-1-1 calls came from Landlines
81% come from ‘Cell Phones’
6% come from VoIP

## Slide 8: Washington State 911 Statistics
FY17 – 911 Calls for service
  Statewide Total Year = 6,699,977 (-1%)
  Average Per Day = 18,356
  Average Per Hour = 765
FY17 – 911 Calls by Service Type
  13% Wireline = 853,718 (-9%)
  81% Wireless = 5,448,361 (+.01%)
  6% VoIP = 397,898 (+8%)
FY17 - 8,525,824 phone subscribers statewide
  14 % Landline = 1,219,727 (-1%)
  13% VOIP = 1,113,677 (+1%)
  62% Wireless = 5,304,898
  10% Pre-Paid Wireless = 887,522
*Percentages shown in comparison to FY16 numbers

## Slide 9: Status of Text-2-911

## Slide 10: ESInet II Project Overview
Scope
Project Team
Timing

## Slide 11: Modernizing the ESInet
Nationally Standardized System =
  Compatible with All PSAPs (Intra and Interstate)
Enhanced Call-Type capabilities (Voice, Text, Data, Imagery, etc.) =
  Accessibility
Enhanced Network Reporting, Monitoring and Troubleshooting Displays (We can see our network working and allows for immediate action in event of an outage) =
  Recoverability, Situational Awareness/Insight
Enhanced Geo-diversity (Dual pathways, Active/Active Processing) =
  Resilience
Transition to true geo-location validation and call-routing =
  Accuracy of Caller location (even if caller is on the move)
Single Data Set (instead of multiple data bases) =
  Simplified Processes
Enhanced Service Level Agreements =
  Assured Reliability

## Slide 12
The Washington State
Next Generation 911 System
GIS
…
BCF
IP Entry Point
LNG
Analog Entry Point
BCF
ESRP
ECRF
LVF
Web
Portal
Policy
Store
Events
Presence
u
u
p
PSTN
Gateway
Internet Gateway
Network Location Information System
ALI
LIS
CIDB
The Emergency Service IP Network
ESInet
Traditional Wireline
Wireless/ Text-2-911
VOIP/Other
From
The Call-Maker
To
The Call-Taker
Legacy PSAPs
NG911 PSAPs
Originating Network
Terminating Network
The Contract is for This
Comtech TCS ESInet

## Slide 13: The next episode… what are we getting?
NENA i3-based ESInet
  Defined in NENA 08-003/STA-010
  Continued support for Interim RFAI and Legacy CAMA
Major Features
  Media agnostic (voice, txt, video, pictures, telematics, etc.)
  Geospatial call routing and location validation
  Extensive Policy Routing…see next slide
  Stringent and comprehensive SLAs with Remedies that will hurt
  Extensive reporting capabilities
  Enhanced monitoring and troubleshooting capabilities
    Quality per call
    Monitoring dashboard…shows status of network and components at glance
  Elimination of ALI (eventually)
Completion October 2019
Next Generation is Now!

## Slide 14: SECO Project Team
SECO
  Executive Sponsor – Adam Wasserman
  Project Director – Andy Leneweaver
  Project QA – Jonathan Cochran
  Telephone/Network – Kenn Moisey
  GeoSpatial Data – Dan Miller
  Security – Steve Walsh
State CIO – Project Oversight
  Rich Tomsinski

## Slide 15: Project Team
Comtech
  Program Management
    Greg Pittsford, Dir, Andrew Singer and SVP Mark Longstaff
  Project Management
    Sr PM Rebecca Yeatman, Sr PM Lynne Warren and Sr Manager PMO Kris Herzog
  NG deployment services
    Shae Shaffer, Brody Evans and Michael Mihelich
  NG Data Services
    Madison Hite, Mandy Naylor and Michael Mihelich
  Comtech NOC, Product Management, Network/Telecom/ Application/System Engineering
  And the product teams from West viper, Comtech CPE, Zetron, Solacom, Motorola CallWorks , Motorola Vesta

## Slide 16: High Level Timeline: SoWA ESInet II conversion
Transition Kick Off
Amendments and SOW Complete
ESInet I Gateway Upgrade
West Upgrade of ESInet I for Comtech Interconnection
ESInet II ITT
Intertandem Trunk Testing and Acceptance
Acceptance Test Plan Executed, Completed, Accepted
Comtech and West ALI Interconnection Upgraded and ALI 04-001 Inter-Operability Testing Performed
Carrier Kick-Off
Provide Ingress Details and ICDs
Map Carrier Capacity Requirements
Kick-Off Interconnection Orders
Test New Circuits
Provide ALI training to Carriers and PSAPs
Upload ALI data
ESInet II ALI Migration
Migrate PSAPs to ESInet II ALI
Carriers and PSAPs start using Comtech ALI
Carriers Migrate Traffic from ESInet I Interconnection to ESInet II
Carrier Cutover
7/25/2017
10/1/2019
10/1/2017
1/1/2018
4/1/2018
7/1/2018
10/1/2018
1/1/2019
4/1/2019
7/1/2019
7/26/2017
-
12/6/2017
ESInet I Gateway Upgrade
12/10/2017
-
4/22/2018
ESInet II ITT DS3/DS1/DS0 Acceptance &
State Acceptance Test Plan Completed
3/13/2019
-
10/1/2019
Carrier Cutover’s to ESInet II
9/30/2017
-
5/21/2019
Carrier Kick Off, Ordering, Training, Testing
PSAP/Carrier Training for ESInet II ALI
4/27/2018
-
1/22/2019
PSAP ESInet 1 to ESInet 2 cutover
1/19/2019
-
3/12/2019
ALI Cutover
7/29/2019
LVF Milestone
7/25/2017
Transition Agreement
Kick
-
Off
10/1/2019
Conversion
Complete

## Slide 17: Comtech’s NG DIG
State of Washington ALI Kickoff 2018/2019
ALI Database Transition

## Slide 18: Overview
Introduction
Schedule
Access and Verification Testing
Training Sessions
Q&A

## Slide 19: Introduction
Next Generation Data Integrity Group (NG DIG)
Working with you to provide access to the new ALI DB
Contact Info:
  ng-data-services@comtechtel.com
  206.792.2285
  M-F 6:00 – 18:00 (PST)

## Slide 20: Schedule
User Forms Submitted (November – December 2018)
User Setup and Verification (December 2018 - January 2019)
Training Sessions (November 2018 – January 2019 )
Dual Provisioning Starts (1/23/19)

## Slide 21: Access and Verification Testing
User forms will be used to grant access
We will need user information, as well as IP addresses to be loaded behind our internal firewall
Setup can take up to 2 weeks
Once complete, we test and will verify user accounts

## Slide 22: Training Sessions
NG DIG will provide user trainings
This will cover things like downloading MSAG and ALI, searching customer records, and processing discrepant records
We will outreach with information closer to that time and provide numerous training dates/times

## Slide 23: Q & A
Thank you for your time!

## Slide 24: Carrier Transition
Scope
  Move all required voice trunks from ESINet I to the new Ingress sites for ESINet II
  Two Redundant Pairs
    North Pair (STTLWAWB and 422 Riverside Dr Spokane, WA)
    South Pair (PTLDORPB and KNWKWA01)
  Each required Trunk will be redundant based on the pair chosen
  Facilities available, DS1, DS3, Gigabit Ethernet, OCx by ICB

## Slide 25: Carrier Transition
Project Team
  Mike Henson
    360-815-4630 mhenson@noanet.net
  Tom Villani
    509-668-0409 tvillani@noanet.net
  Inquiry email
    ecomm@noanet.net
  Escalation point
    Greg Pittsford, 206-792-2238

## Slide 26: Carrier Transition
Timing Details
  Carrier Introductions- Q3 2018
  Carrier Facility Plan- Q4 2018
  Carrier Order- Q1 2019
  Carrier Migration- Q2-Q3 2019

## Slide 27: Carrier Transition
Expectations
  Technical contact needed
  Introduction call
  Worksheet for ALI
  Worksheet forecast for network
  System Introduction and training for Online ASR for ordering

## Slide 28: 911 – The First First Responder

## Slide 29: 911 TRIVIA: “Did you Know?”
You can use your old cell phone to dial 911!
Britain implemented the “999” emergency number in 1937
Indonesia- Dial 118 or 119* for general emergency, and…
  115- for Search & Rescue
  129- for a Natural Disaster