## Slide 1: 2017 IRP Overview
Presentation to the WUTC
John Mannetti
Director, Operations Solutions
Phillip Popoff
Manager Resource Planning and Analysis
February 21, 2018

## Slide 2: A rapidly changing planning landscape shapes this IRP
The 2017 Integrated Resource Plan (IRP) responds to rapid changes in carbon regulation, technology and regional markets to preserve strategic agility for PSE. The plan delays the need to acquire fossil fueled generation assets as these uncertainties take shape over the next few years.
Newer technologies, including demand response and batteries, coupled with energy efficiency push out the need for additional natural gas fired generation to 2025
In the renewables space, solar appears more cost effective than wind
Redirecting existing transmission for market purchases is a very low-cost source of capacity
Carbon regulation may adversely affect economics of Colstrip 3&4 continued operation
Resource Plan Takeaways

## Slide 3: Electric IRP results find investment in solar and newer technologies to be least cost. Natural Gas IRP results point to upgrades and additional pipeline capacity in 2029.
Electric: Cumulative nameplate (MW) capacity additions1
Gas: Cumulative Additions in MDTH/day of Capacity2
1PSE 2017 IRP, Figure 1-4 page 1-18
2PSE 2017 IRP, Figure 1-8, page 1-25

## Slide 4
Credit Collections, Field Collections
PSE improved transparency in the IRP process
PSE incorporated numerous stakeholder requests into the IRP
16
IRP Advisory Group Meetings
30+
Responses to detailed technical questions from stakeholders
1
Additional employee hired to manage the stakeholder process
1
    Additional fully integrated scenario
1
    Additional consulting study performed to validate wind and solar costs
7 of 13
Sensitivities analyzed were stakeholder driven
PSE made improvements to the IRP process and incorporated stakeholder requests

## Slide 5: Required by the WUTC, the IRP determines “the mix of energy supply and conservation resources that will meet future and current needs at the lowest reasonable cost to the utility and its ratepayers.”1
Compliance filing at WA Utility Commission
  Filed Every Other Year: Gas and Electric
20+ year look at needs and resources
Determine least cost mix of supply and demand-side resources
Understand how uncertainty affects findings
Actual energy efficiency and supply-side resource decisions are not made in the context of the IRP.
Establish Resource Needs
Planning Assumptions & Resource Alternatives
Make Decisions
Commit to “Action”
Analyze Alternatives and Portfolios
Analyze Results
Analyze Market Risk
1
2
3
4
5
6
7
1/WAC 480-100-238 (2) (a) Definitions, Integrated Resource Plan.

## Slide 6: Establish Resource Needs: Electric Peak Hour Capacity Resource Need
1
PSE 2017 IRP Figure 1-1, page 1-13
February 21, 2018: 2017 IRP Overview
Projected peak hour need and effective capacity of existing resources
PSE 2017 IRP Figure 1-1, page 1-13

## Slide 7: Establish Resource Needs: Electric Renewable Need
1
PSE 2017 IRP Figure 1-3, page 1-16
Renewable Resource/REC Need

## Slide 8: Planning Assumptions & Resource Alternatives: Integrated Scenarios
Fourteen fully integrated scenarios were analyzed in the 2017 IRP
2

## Slide 9: Planning Assumptions & Resource Alternatives: Carbon Regulation
Carbon regulation assumptions varied across 14 different scenarios
2
Applying a carbon price to all thermal resources (Base + All-thermal CO2 scenario) may be the most aligned with current WA state emissions proposals
Findings / Outcome
Base Case Assumptions
  Forecasted carbon costs ranged from $19/ton to $51/ton in the base case
  Utilized a combination of state and federal rulemakings to forecast carbon prices
  Applied Clean Air Rule until 2022
    Application to gas utilities and petroleum suppliers invalidated by Court after IRP filed
  Applied Clean Power Plan after 2022
    Not being pursued by administration
    Simplified to WECC CO2 price

## Slide 10: Planning Assumptions & Resource Alternatives: Resource Costs
Demand response assumptions updated to improve capacity contribution
Solar and battery costs have declined
Resource cost studies from developers with on-the-ground experience Black and Veatch and DNVGL
  PSE needs a detailed cost assumptions to calculate revenue requirements—levelized costs are insufficient
  Cost decreases for natural gas-fired peakers and wind
Incorporated the latest resource cost and characteristic information
2
Solar is more cost effective than wind to meet renewable need
Batteries are present in the plan for the first time
Demand response continues to be cost effective, however policy hurdles exist
Findings / Outcome

## Slide 11: Planning Assumptions & Resource Alternatives
Responding to stakeholder input, PSE included a large chapter on local system planning describing in detail the planning process and an upcoming transmission projects
PSE anticipates further integration between local system planning and the IRP process and looks forward to rulemakings that may provide further guidance
Transmission and Distribution Planning
Inclusion in IRP will require new processes and education to incorporate effectively.
DER technology effectiveness in meeting grid needs is maturing and PSE will continue to incorporate through least cost solution objectives
Findings / Outcome
2

## Slide 12: Analyze Alternatives and Portfolios
Portfolio optimization results by resource type
3
Cost-effective conservation does not vary across scenarios. This is consistent with findings in prior IRPs.
Conservation
All scenarios have at least 60 MW of demand response, with a few scenarios having as much as nearly 160 MW.
Demand Response
Increasing market reliance by redirecting 188 MW of transmission from Hopkins Ridge and Lower Snake River is least cost across all scenarios and sensitivities.
Transmission Redirect
A small amount of utility-scale batteries appears cost effective at some point in the planning horizon in every scenario, given the assumed transmission and distribution benefits. By 2037, all scenarios have at least 50 MW, while a few have approximately 100 MW.
Energy Storage

## Slide 13: Analyze Alternatives and Portfolios
Portfolio optimization results by resource type
3
Solar appears to be the most cost-effective renewable resource to comply with RCW 19.285. PSE is a winter peaking utility, so solar provides virtually no capacity value.
Eastern Washington Solar
Wind in eastern Montana would not be a qualifying renewable resource under RCW 19.285, unless it were delivered all the way to Washington state on a real-time basis without shaping or storage. This is a resource that could be identified as more cost effective in the upcoming RFP.
Montana Wind
Wind in the Pacific Northwest did not appear to be a cost-effective resource in any scenario. Again, this resource may prove to be more cost effective in the upcoming RFP.
Pacific Northwest Wind
Dual fuel frame peakers were found cost effective over baseload gas plants in almost every scenario. Most scenarios show peakers as the go-to capacity resource later in the planning horizon, however this is also a result carbon regulation affecting baseload plants but not peakers. There are no baseload gas plants in the resource plan.
Peakers & Baseload Gas Plants

## Slide 14: Analyze Alternatives and Portfolios: Sub-hourly Flexibility
Purchased Plexos and hired E3 to perform analysis
Two Key Questions Explored:
  Does the resource portfolio have Adequate Flexibility?
    Results showed it is not likely that PSE needs to add resources just for flexibility
  What is the value of sub-hourly flexibility benefit?
    Adding different and more flexible resources such as reciprocating engines and energy storage decreased the total production cost and added more flexibility to the portfolio
PSE made significant improvements in sub-hourly flexibility modeling that will be leveraged in future IRPs
Continued focus for the future:
  Resource Planning Team is currently analyzing key portfolio questions in Plexos, so we are up and running on our own
  PSE will continue to refine assumptions and improve modeling capability
Findings / Outcome
3

## Slide 15: Analyze Market Risk
Updated analysis of wholesale market risk leveraging NPCC and BPA regional studies
Results showed that market capacity purchases are nearly as reliable as a gas peaker, however this is dependent on regional conservation keeping pace with the NPCC 7th Power Plan
Additionally, PSE’s participation in the EIM has created opportunities to look at optimizing our transmission resources differently
4
Understanding market risk is critical because PSE relies on the short-term market to meet peak capacity needs
Redirect 188MW of firm transmission from LSR/Hopkins Ridge to Mid-C
Action Plan item to develop options to mitigate risk of market reliance
Findings / Outcome

## Slide 16: Analyze Results: Carbon Regulation
IRP Results Still Valid:
Resource plan recognized this unintended consequence and took results of the unbiased application of carbon regulation, which causes an insignificant increase in cost, but pushes out need for fossil fuel plants so technology and policy can continue to work
Findings / Outcome
The form of carbon regulation affects portfolio cost and resource decisions:
There are unintended consequences created by base case carbon regulation:
  Carbon price only assigned to gas CCCT, not gas peakers
  Renders Colstrip uneconomic—only under CPP, not CAR
  When carbon regulation is applied across all gas resources, demand response and batteries are cost effective
5

## Slide 17: Analyze Results: Carbon Regulation
Portfolio CO2 Emissions From Electric Service
PSE 2017 IRP Figure 2-4, page 2-7
5
Projected Annual Total PSE Portfolio CO2 Emissions and Savings from Conservation

## Slide 18: Analyze Results: Colstrip
PSE examined replacement options for Colstrip units1&2 as well as the effect of a carbon price on Colstrip units 3&4
PSE also examined early retirement sensitivities for Colstrip units 3&4 as requested by stakeholders
Replacing Colstrip 1&2 will not result in additional fossil generation being acquired
5
Colstrip units 1&2 shutdown in 2022 will not create a need for additional fossil resources. The plan shows it would be cost effective to replace units 1&2 will with a combination of conservation, demand response, redirected transmission and batteries
Continued operation of units 3&4 is highly dependent on environmental regulation. Placing a carbon price on plant dispatch for units 3&4 could adversely effect the plant economics to where it would be more cost effective to replace it with other resources
Findings / Outcome

## Slide 19: Analyze Results: Portfolio Costs
Incremental Portfolio Costs Over Time are consistent with recent IRPs
PSE 2017 IRP Figure 2-4, page 2-7
5

## Slide 20: Make Decisions: Electric Resource Plan
6
The application of judgement – bringing together a resource plan
Resource Plan Compared to Base Case:
  The resource plan includes more demand response and early batteries in order to delay the need for peakers until 2025.
  This decision comes at a slight premium. Expected cost of the resource plan is 0.5% higher than the base case portfolio (roughly $50 million over the planning horizon).
  PSE views the slight increased cost of demand response and energy storage, as an important risk mitigation decision as the state considers future carbon regulation.
  Pushing out the need for additional fossil fuel plants to 2025 or beyond is a reasonable strategy. This will provide time for technology to work on reducing alternative resource costs as well as time for carbon regulations to become clearer.

## Slide 21: Make Decisions: Gas Resource Plan
6
The application of judgement – bringing together a resource plan
Demand-side Resources (DSR)
  Analysis applies a 10-year ramp rate for acquisition of DSR measures
Swarr Upgrade - 2024/25 heating season
  This IRP finds that upgrading the Swarr LP-Air facility’s production capacity to Swarr’s original 30 MDth per day capability
PSE LNG Distribution Upgrade - 2027/28 heating season
  Expansion of the distribution network’s capacity east of Tacoma that will allow more gas to flow from the LNG facility into PSE’s gas supply network
Northwest Pipeline/Westcoast Expansion - 2029/30 heating season
  Additional transportation capacity from the gas producing regions in British Columbia at Station 2 south to PSE’s system on the Westcoast pipeline

## Slide 22: Commit to Action
7
Electric Action Plan:
Develop two-year targets and implement programs that will put us on a path to achieve an additional 374 MW of energy efficiency by 2023 through program savings combined with savings from codes and standards.
1. Acquire Energy Efficiency
Clarify the acquisition, prudence criteria and cost recovery process for demand response programs and issue a demand response RFP. Re-examine the peak capacity value of demand response programs in the 2019 IRP to include day-ahead demand response programs, and use the sub-hourly flexibility modeling capability developed in this IRP to value sub-hourly demand response programs.
2. Demand Response
Install a small-scale flow battery to gain experience with the operation of this energy storage system in anticipation of greater reliance on flow batteries in the future.
3. Energy Storage

## Slide 23: Commit to Action
7
Electric Action Plan (continued):
Issue an all-source RFP in the first quarter of 2018 that includes updated resource needs and avoided cost information. PSE has a need for renewable and capacity resources as early as 2022, after cost-effective conservation and demand response are accounted for.
4. Supply-side Resources: All-source RFP
Develop strategies to mitigate the risk of redirecting transmission and increasing market reliance.
5. Develop Options to Mitigate Risk of Market Reliance
Continue to participate in the California Energy Imbalance Market for the benefit of our customers.
6. Energy Imbalance Market (EIM)
Examine regional transmission needs in the 2019 IRP in light of efforts to reduce the region’s carbon footprint.
7. Regional Transmission

## Slide 24: Commit to Action
7
Natural Gas Sales Action Plan:
Develop two-year targets and implement programs to acquire conservation, using the IRP as a starting point for goal-setting. This includes 14 MDth per day of capacity by 2022 through program savings and savings from codes and standards.
1. Acquire Energy Efficiency
Complete the PSE LNG peaking project located near Tacoma:
Construction of the facility is under way and should be completed in time for the storage project to be filled for the 2019/20 heating season. This resource is essential to delaying investment in additional interstate and international year-round pipeline capacity.
2. LNG Peaking Plant
Maintain the ability upgrade the Swarr propane-air injection system in Renton, which the plan forecasts will be needed by the 2024/25 heating season.
3. Option to Upgrade Swarr

## Slide 25: Next steps
Request for Proposals to be conducted in Q2 2018
WUTC acknowledgement letter
Launch of 2019 IRP process in Q2 2018 (Work Plan in July 2018)
Continuous improvement to incorporate new rule changes to the IRP process, better tools for IRP modeling, improved stakeholder education, engagement and communication, and improved collaboration with UTC.

## Slide 26: Q&A