## Slide 1: Seventh Power Plan and Regional Recommendations
July 6, 2016

## Slide 2: Resource Strategy
Energy Efficiency Development
  1400 aMW by 2021
  3100 aMW by 2026
  4500 aMW by 2035
Expand Use of Demand Response
  Be prepared to develop a significant quantity of demand response resources by 2021
  Review out-of-region market depth assumptions for energy and capacity
Renewable Resources
  Expand the resource options considered for renewable requirements, utilities should consider the value of diversity from both adding different technologies and different geographic locations
  Encourages research on and demonstration of renewable energy with a more consistent output like geothermal or wave energy

## Slide 3: Resource Strategy
Natural Gas
  Increase use of existing gas generation to offset coal plant retirements
  Low probability of regional need for new gas-fired generation prior to 2021
  Individual utility circumstances and need for capacity and other ancillary services may dictate development
Regional Resource Use
  Continue to improve system scheduling and operating procedures across the region’s balancing authorities to maximize cost-effectiveness and minimize the need for new resources to integrate renewable generation
Expand Resource Alternatives
  Continue to research and expand energy efficiency options
  Expand renewable generating options to capture technological diversity
Adaptive Management

## Slide 4: 7th Plan Resource Portfolio Energy
Chart: Cumulative Resource Development (Average Megawatts)
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Conservation | 0 | 174.2734 | 369.0716 | 590.4662 | 839.9377 | 1120.59 | 1427.0487 | 1750.225 | 2086.0662 | 2433.8175 | 2785.95 | 3135.3663 | 3478.7575 | 3812.0575 | 4053.8288 | 4180.2787 | 4268.775 | 4343.385 | 4409.89 | 4470.3887 | 4529.0237
Natural Gas | 0 | 0 | 0 | 0 | 0.2125 | 0.8425 | 4.64 | 12.8725 | 12.67 | 12.9588 | 15.5263 | 23.4513 | 23.3875 | 29.3163 | 47.2725 | 81.9613 | 103.2725 | 152.7737 | 207.8238 | 327.455 | 328.1937
Solar | 0 | 0 | 0 | 0 | 0 | 0 | 0.01875 | 0.0725 | 0.105 | 0.18 | 7.31 | 37.8988 | 77.8963 | 104.9463 | 120.395 | 127.9725 | 132.09 | 135.555 | 140.475 | 150.2775 | 166.4688
Wind | 0 | 0 | 0 | 0 | 1.505 | 2.0963 | 2.0963 | 2.0963 | 2.0963 | 2.0963 | 2.9988 | 8.8575 | 14.6087 | 16.7575 | 17.085 | 17.22 | 17.275 | 19.0225 | 30.3637 | 68.2413 | 128.3538

## Slide 5: 7th Plan Resource Portfolio Winter Capacity
Chart: Cumulative Resource Development (Megawatts)
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Conservation | 197.055 | 608.7538 | 1090.975 | 1641.1337 | 2263.6013 | 2959.3338 | 3710.0338 | 4498.035 | 5319.9987 | 6170.6513 | 7028.1313 | 7881.5837 | 8721.4112 | 9471.6187 | 9925.365 | 10143.7338 | 10340.2088 | 10508.9075 | 10663.1875 | 10810.17
Demand Response | 429.64 | 631.5825 | 677.0187 | 684.1912 | 695.8312 | 695.8312 | 695.8312 | 696.3687 | 696.3687 | 697.3662 | 697.3662 | 697.3662 | 697.3662 | 697.3662 | 697.3662 | 697.3662 | 697.3662 | 698.1138 | 698.1138 | 698.1138
Thermal (Natural Gas) | 0 | 0 | 2.4337 | 27.0787 | 27.0787 | 27.0787 | 27.0787 | 50.3963 | 50.3963 | 50.3963 | 50.3963 | 174.96 | 174.96 | 306.6475 | 306.6475 | 647.57 | 647.57 | 647.57 | 647.57 | 649.3425
Renewable (Wind & Solar PV) | 0 | 0.26875 | 0.26875 | 0.26875 | 0.26875 | 0.26875 | 0.26875 | 0.26875 | 0.26875 | 0.48125 | 1.6688 | 2.3875 | 2.4812 | 2.5125 | 2.525 | 2.5312 | 2.8575 | 4.8 | 11.0088 | 20.155

## Slide 6: Range of Energy Efficiency Development
Chart: 
| Existing Policy | Existing Policy_NoDR | Increased Market Reliance | SCC_MidRange | Max CO2 Reduction
10th Percentile | 1285.255 | 1389.337 | 1160.065 | 1389.736 | 1405.107
90th Percentile | 1361.048 | 1442.735 | 1285.819 | 1438.788 | 1451.004

## Slide 7: Demand Response Plays a Key Role in Regional Reliability
Chart: Megawatts Deployed - 2021
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700
Existing Policy_Final | 0 | 0 | 0 | 0 | 0 | 0 | 0.03 | 0.0375 | 0.05875 | 0.08375 | 0.1175 | 0.43125 | 0.49875 | 0.565 | 0.63125 | 0.69875 | 0.82 | 0.855 | 0.87375 | 0.9025 | 0.9175 | 0.935 | 0.9475 | 0.9625 | 0.9675 | 0.98125 | 0.9825 | 1
1B_MarketReliance-Final | 0.035 | 0.04875 | 0.07 | 0.105 | 0.13875 | 0.9075 | 0.93375 | 0.96 | 0.975 | 0.98125 | 0.99 | 0.9925 | 0.99875 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SCC_MidRange_Final | 0 | 0 | 0 | 0 | 0 | 0 | 0.0325 | 0.0475 | 0.0675 | 0.09875 | 0.13 | 0.49 | 0.55625 | 0.6225 | 0.67875 | 0.74 | 0.8475 | 0.8675 | 0.895 | 0.91 | 0.935 | 0.945 | 0.9575 | 0.965 | 0.975 | 0.985 | 1 | 1

## Slide 8: Without Demand Response Additional Natural Gas Development is Very Likely
Chart: Capacity Developed - 2021 (MW)
| 0 | 175 | 350 | 525 | 700 | 875 | 1050 | 1225 | 1400 | 1575 | 1750 | 1925 | 2100
Existing Policy_NoDR-Final | 0.1175 | 0 | 0.0675 | 0.0875 | 0.12125 | 0 | 0.10125 | 0.09 | 0.09 | 0 | 0.07625 | 0.06375 | 0.0475
88% probability of needing to develop new gas generation by 2021

## Slide 9: Impact of Policy on Emissions
Chart: 
| No Coal, Carbon Cost and No New Gas | No Coal | Internalized Social Cost of Carbon | Northwest Regional 35% RPS | Expected with Planned Coal Retirements | Expected without Coal Retirements* | Average 2000-2012
CO2 Emissions (MMTE) | 10.8087 | 13.4337 | 18.23 | 21.6788 | 33.5375 | 45 | 55
*Assumes Centralia, Boardman and North Valmy are not retired.

## Slide 10: Action Plan Recommendations

## Slide 11: Energy Efficiency
Achieve the regional goal for energy efficiency and report on progress in the annual Regional Conservation Progress survey
Evaluate cost-effectiveness of measures considering capacity
Continue support of NEEA
Conduct conservation program impact evaluations
Improve participation in cost-effective programs for underserved or hard-to-reach segments, e.g. low-income households
Support end-use load research
Provide flexibility in pursuing measures that may not be cost-effective but demonstrate likely cost reductions to help in improving future codes and standards

## Slide 12: Resource Adequacy
Identify system specific least-cost resources to maintain resource adequacy considering demand response and energy efficiency
Consider individual utility contributions to regional resource adequacy

## Slide 13: Demand Response
Support regional market transformation
Provide public data on impact of DR dispatch on historic loads

## Slide 14: Renewables
Consider diversity in technology and geography when acquiring new renewables
In addition to wind generation, both solar and geothermal generation were cost-effective options in resource strategies identified in the Seventh Plan

## Slide 15: Carbon Emissions
Re-dispatching the existing system can significantly reduce carbon emissions without requiring the significant capital associated with building new generation
Complying with the EPAs Clean Power Plan, if upheld, should be possible with announced retirements on a regional level – at a state level will likely take some coordination

## Slide 16: Operating Reserves
An estimate of utilities requirement for operating reserves
Reasonable planning assumptions for the demand for and supply of reserves including which projects or plants should be assigned in power system models to provide these reserves or what level of third-party provision of reserves is anticipated

## Slide 17: Load Forecasting
Support end-use load research
Reflect the impact of codes and standards in load forecasts
Facilitate sharing whole-building consumption data to improve energy and demand savings estimates

## Slide 18: Backup Slides

## Slide 19: Updated Scenario Analysis Shows Little Change In Conservation Development Patterns Across Scenarios Compared To Draft Plan
Chart: Average Megawatts Developed - 2021
| 1150 | 1175 | 1200 | 1225 | 1250 | 1275 | 1300 | 1325 | 1350 | 1375 | 1400 | 1425 | 1450 | 1475 | 1500 | 1525
Existing Policy_Final | 0 | 0 | 0 | 0 | 0.00125 | 0.03 | 0.3275 | 0.385 | 0.11125 | 0.0825 | 0.04 | 0.015 | 0.005 | 0.0025 | 0.0025 | 0.0025
Existing Policy_NoDR-Final | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0025 | 0.02875 | 0.175 | 0.47375 | 0.275 | 0.04125 | 0.00375 | 0
1B_MarketReliance-Final | 0.0225 | 0.2975 | 0.2525 | 0.1175 | 0.1075 | 0.07 | 0.07 | 0.035 | 0.0175 | 0.005 | 0.0025 | 0.0025 | 0 | 0 | 0 | 0
SCC_MidRange_Final | 0.00125 | 0.00125 | 0.00125 | 0.00125 | 0.00125 | 0.00125 | 0.0025 | 0.00125 | 0.0125 | 0.01625 | 0.21 | 0.48375 | 0.23125 | 0.0375 | 0.00375 | 0
Max CO2 Reduction_Final | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0025 | 0.04375 | 0.42875 | 0.41 | 0.10125 | 0.0125 | 0.00125

## Slide 20: All Resource Cost – Energy
Chart: Real Levelized Cost (2012$/MWh)
| Energy Efficiency (Average Cost w/ T&D Credit) | Energy Efficiency (Average Cost w/o T&D Credit) | Solar PV - Low Cost S. ID | Natural Gas - CCCT Adv1 | Natural Gas - CCCT Adv2 | Solar PV - S. ID | Wind -MT w/ new transm. | Wind - MT w/ Transm. Upgrade | Wind - Colum. Basin | Natural Gas - Frame GT East | Solar PV- S. ID w/ Transm. Expan. | Natural Gas - Recip Engine East | Natural Gas - Aero GT East
Capital | 18 | 30 | 44.4391 | 20.3375 | 22.8199 | 71.645 | 63.5716 | 63.5716 | 75.7771 | 32.3322 | 71.645 | 52.0197 | 44.4568
O&M + Property Taxes + Insurance | 0 | 9.1095 | 8.1357 | 8.377 | 14.6854 | 17.6376 | 17.6376 | 21.2176 | 16.2473 | 14.6854 | 18.5225 | 20.5858
Fuel + Transmission | 0 | 12.8983 | 47.2084 | 46.8136 | 13.1961 | 24.5171 | 28.084 | 13.3359 | 85.8686 | 51.6606 | 72.0013 | 80.1644

## Slide 21: All Resource Cost – Peak Capacity
Chart: Real Levelized Fixed Cost (2012$/KW-year)
| Demand Response Price Block 1 | Demand Response Price Block 2 | Demand Response Price Block 3 | Solar PV - Low Cost S. ID | Natural Gas - Frame GT East | Natural Gas - CCCT Adv1 | Demand Response Price Block 4 | Natural Gas - Recip Engine East | Natural Gas - Aero GT East | Natural Gas - CCCT Adv2 | Solar PV - S. ID | Wind - Colum. Basin | Solar PV- S. ID w/ Transm. Expan. | Wind -MT w/ new transm. | Wind - MT w/ Transm. Upgrade
Capital | 24.9169 | 54.1667 | 77.2698 | 101.99 | 70.81 | 106.89 | 189.0389 | 113.92 | 97.36 | 119.94 | 164.43 | 212.42 | 164.43 | 222.75 | 222.75
O&M + Property Taxes + Insurance | 20.91 | 13.81 | 25.67 | 20.97 | 34.2 | 26.94 | 33.7 | 53.92 | 33.7 | 54.86 | 54.86
Fuel + Transmission | 23.9 | 63.02 | 49.23 | 55.69 | 60.21 | 49.09 | 24.58 | 37.05 | 112.86 | 85.43 | 97.93