BEFORE THE WASHINGTON STATE

UTILITIES AND TRANSPORTATION COMMISSION

| THE WASHINGTON STATE DEPARTMENT OF TRANSPORTATION, Petitioner, v. COLUMBIA AND COWLITZ RAILROAD, Respondent. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . | ) ) ) ) ) ) ) ) ) ) ) ) ) | DOCKET NO. TR-051191 ORDER NO. 01 ORDER GRANTING PETITION FOR INSTALLATION OF HIGHWAY-RAIL GRADE CROSSING WARNING DEVICES WUTC NO. 11A.10 USDOT NO. 840534K |
| --- | --- | --- |

BACKGROUND

On August 5, 2005, the Washington State Department of Transportation (WSDOT) filed a petition with the Commission seeking approval to install warning signals and gates at the intersection of SR 432 (Industrial Way) and the tracks of the Columbia and Cowlitz Railroad (Railroad), in the NW ¼ of the SE ¼ of Section 31, Township 8 N., Range 2W., W.M., in Cowlitz County, Washington.  Funding for the upgrades is pursuant to the Inter-modal Surface Transportation Efficiency Act.

On August 17, 2005, the Railroad filed a document in this matter consenting to entry of a final order without further notice of hearing and agreeing that the petition should be granted.

In the vicinity of the crossing, Industrial Way is a state highway with one lane of travel in each direction.  Highway speed is 50 mph.  The estimated daily traffic is 10, 000 vehicles, which includes school buses and trucks.  Sight distance along the tracks is not obstructed; however, the tracks cross the road at about an angle of 130 degrees, which makes it difficult for drivers to observe trains approaching from their left.

The Railroad maintains one branch line track through the crossing.  Daily train traffic averages 10 trains traveling at a maximum speed of 20 mph.  Railroad warning devices at the grade crossing consist of “rotatable” cantilever-mounted signals with outmoded AC/DC circuitry.

WSDOT proposes to replace the existing signals with walk-out cantilever signals and gates, and SCX-1(AC/DC) circuitry.  The upgrades are proposed in the interest of improving safety for roadway users.  A multi-jurisdictional diagnostic team reviewed the crossing in 2003 and recommended that the warning devices be upgraded as proposed.

FINDINGS AND CONCLUSIONS

(1)	The Washington Utilities and Transportation Commission is an agency of the State of Washington having jurisdiction over public railroad-highway grade crossings within the state of Washington.  Chapter 81.53 RCW.

(2)	The Industrial Way grade crossing, identified as USDOT 840534K, is a public railroad-highway grade crossing within the state of Washington.

(3)	RCW 81.53.261 requires that the Commission grant approval prior to any changes in the method and manner of traffic control at public railroad-highway grade crossings within the state of Washington.

(4)	Commission Staff investigated the petition and recommended that it be granted, subject to specified conditions.

(5)      	This matter was brought before the Commission at its regularly scheduled meeting on September 28, 2005.

(6)	After examination of the petition filed by WSDOT on August 5, 2005, and giving consideration to all relevant matters and for good cause shown, the Commission grants the petition.

O R D E R

THE COMMISSION ORDERS:

The petition of the Washington State Department of Transportation to upgrade warning devices at a railroad-highway grade crossing, located at the intersection of Industrial Way and the petitioner’s tracks, in Cowlitz County, Washington, is granted, subject to the following conditions:

  - The upgrades must conform to the plans filed in this proceeding.

  - Traffic control devices must comply with all applicable standards specified in the U.S. Department of Transportation Manual on Uniform Traffic Control Devices.

  - Traffic control devices and instrument housing must be installed in such a manner as to provide required clearances from both the roadway and railroad tracks.

  - Upon completion of the upgrades authorized herein, petitioner must notify the Commission.  Acceptance of the changes is subject to inspection by Commission Staff, verifying that the crossing is in full compliance with applicable laws, regulations, and the conditions specified herein.

The Commissioners, having determined that this filing complies with the requirements of RCW 81.53.261, directed the Secretary to enter this Order.

DATED at Olympia, Washington, and effective this 28th day of September, 2005.

WASHINGTON UTILITIES AND TRANSPORTATION COMMISSION

CAROLE J. WASHBURN, Secretary