## Slide 1: 2013 Integrated Resource Plan
October 10, 2013
Phillip Popoff
Manager, Integrated Resource Planning

## Slide 2: PSE 2013 IRP Agenda
Introduction and Key Findings
Electric IRP Overview
Resource Needs
Resource Plan
High Level Process & Assumptions
Results
Colstrip in IRP
Gas IRP Overview
Next Steps

## Slide 3: Key Findings
Northwest Energy Markets Changing
Dwindling Regional Capacity Surplus Will Impact PSE
Increasing Intermittent Resources Change Market Dynamics
Increasing Reliance on Natural Gas Flexibility
Upward Pressure on Gas Prices
Infrastructure May Become Challenged
Least-Cost Resource Plans
Conservation, Renewables, Peakers for Reliability
Similar Trends Across Nearly All Future Scenarios
Uncertainty For Coal Industry
Savings To Customers from Operation of Colstrip Are Significant
Planning for Possibility of Needing to Replace Colstrip Still Important

## Slide 4: Changing Regional Load-Resource Balance
Region Historically Surplus Energy and Capacity
PSE Heavily Dependent on Market for Capacity
~1400 MW of Firm Transmission to Short-Term Market for Peak Capacity
~23% of Capacity Need
Region Short 2000 MW of Firm Capacity by 2022
(See Appendix I)
IRP Update Planned for Q4 2013
Focus on Short-Term Market Reliance for Capacity

## Slide 5: PSE 2013 IRP Agenda
Introduction and Key Findings
Electric IRP Overview
Resource Needs
Resource Plan
High Level Process & Assumptions
Results
Colstrip in IRP
Gas IRP Overview
Next Steps

## Slide 6
Winter Peak Capacity Need (MW)
Firm Transmission to Short-Term Market

## Slide 7
Annual Energy Position in aMW: 2013 IRP

## Slide 8
Renewable “Energy” Need-Incl. Banking

## Slide 9: Electric Resource Plan-Resource Additions
Figure 1-4, p. 1-8
Direction for Electric Resource Plan
Energy Efficiency: Continue Accelerated Acquisition of Demand-Side Resources
Renewables: Forward Acquisition Has PSE Ahead-More by 2022
Reliability: Peakers Rather Than Base Load Gas Plants
Fuel Supply: Storage Increasingly Important for Generation

## Slide 10: Interpreting “The Plan”
 | At Least | Expected | As Much As
Conservation | 798 MW | 800 MW | 800 MW
Wind | 200 MW | 300 MW | 400 MW
*-Peakers | 0 MW | 442 MW | 1,106 MW
Range of Least-Cost Plans Across 30+ Scenarios by 2023
Colstrip Wild Card…
If Colstrip is Out of Portfolio: +663 MW of Peakers
*Note: Each Peaker is 221 MW

## Slide 11: PSE 2013 IRP Agenda
Introduction and Key Findings
Electric IRP Overview
Resource Needs
Resource Plan
Process & Assumptions
Results
Colstrip in IRP
Gas IRP Overview
Next Steps

## Slide 12
Resource Needs
Planning Assumptions & Resource Alternatives
Decisions
Commitment to “Action”
Analysis of Alternatives Portfolio Analysis
Analysis of Results
Regulatory Compliance
Customer Needs
Stakeholders
Market Outlook

## Slide 13: Two Categories of Uncertainty…
13
Resource Needs
Relative Value of Resources
-Peak Capacity
-Energy
-Renewable “Energy”
-Flexibility
-Demand-Side
-Peakers: CT & Recip
-Gas CCCT
-Transmission + Market
-Wind/Biomass
-Mid-Term Contracts
-Hydro
-Storage
-PSE Transmission
-Solar/Emerging?
-Gas Pipeline
-Gas Storage

## Slide 14: 2013 IRP: Scenarios/Sensitivities/Cases
Market Scenarios
Base: Mid Load, Mid Gas Price
Base + Low Gas
Base + Very Low Gas Price
Base + Very High Gas Price
Base + Low CO2 Cost
Base + High CO2 Price
Base + Very High CO2 Cost
Low: Low Load, Low Gas Price
High: High Load, High Gas Price
High + High CO2 Price
Portfolio Sensitivites
Peaker Type – CT vs Recip
CT With and Without Oil Back-up
Location: East/West Cascades
DSR Acquisition /Ramp Rates
Colstrip Forced Replacement
Replace Colstrip with MT Wind
RPS + 300MW Wind
Colstrip Environmental Compliance Cases
Case 1–Low Cost: Regional Haze Less Costly Technology Solution
Case 2–Mid Cost: Regional Haze Realistic Estimate of EPA Technologies
Case 3–High Cost: Case 2 + CCR Hazardous w/Offsite Disposal @ $8/ton
Case 4—Very High Cost: Case 2 + CCR w/Offsite Disposal at $24/ton
~48 Deterministic Portfolio Analyses
Stochastic Analyses: 250 – 1000 Draws
Reflecting Market/Load Uncertainty
Plus CO2 Policy Risk

## Slide 15
Range of Levelized Sumas Gas Prices With Carbon Costs
Figure 4-6, p. 4-7

## Slide 16
Range of CO2 Cost/Price Assumptions
Figure 4-7, p. 4-9
EPA Analysis Kerry-Lieberman: Hi 2011 IRP
Societal Costs from “Technical Support Document”

## Slide 17
Avg Annual Mid-C Power Prices
Figure 4-8, p. 4-21

## Slide 18
Re-ordered Figure 2-2, p. 2-4 (IRP Figure Left Out Three Scenarios from Case 2)

## Slide 19: Long-Term Portfolio Costs Uncertain
Figure 1-5, p. 1-11

## Slide 20: Projected CO2 Emissions Trending Up Under Existing Policies
Bump Reflects Coal Transition Power to Support Shut-Down of Centralia Coal Plant
This Forecasts PSE’s Portfolio--PSE Has Services to Help Customers to Manage Their Individual Carbon Footprint

## Slide 21: Electric Action Plan
Pursue Cost Effective Demand-Side Resources
Develop Strategy to Address Reliance on Market for Capacity in the Intermediate to Long-Term
  Update to IRP in 4th Quarter 2013
Align Timeline for Resource Acquisitions With Timeline Needed for Infrastructure
Pursue Prudent Gas Storage Acquisitions for Generation
Revise Stakeholder Process to Clarify Roles and Expectations & Provide Greater Transparency

## Slide 22: PSE 2013 IRP Agenda
Introduction and Key Findings
Electric IRP Overview
Resource Needs
Resource Plan
Process & Assumptions
Results
Colstrip in IRP
Gas IRP Overview
Next Steps

## Slide 23: 2013 IRP: Overview Colstrip Analysis
Summary Results and Conclusions
Overview of Colstrip: Plant and Commercial Arrangements
Analysis Performed
Results

## Slide 24: Colstrip: Conclusions in This IRP
Colstrip Significantly Reduces Cost and Cost Risk for Customers
Including Consideration of Future Carbon Regulation
Premature to Begin Developing Replacement Resources
May Change in Future
IRP Comprehensively Studied Potential Risks
Planning For Replacement
Peakers for Reliability and Market Energy As Needed Across Most Scenarios
24

## Slide 25: Colstrip: What’s in The IRP
Purpose of IRP Analysis
Broad Examination of Cost of Continuing Operation at Colstrip, Including Range of Anticipated Costs Associated with EPA Regulations
Understand Factors That Could Render Colstrip Uneconomic
Understand Impact of Existing Policies
Purpose is to Plan
What If Policies/Market Conditions Change Unexpectedly?
What Would Be Least Cost Resources to Replace Colstrip?
IRP is Not A “Decision” To Keep Colstrip Running

## Slide 26: Colstrip: Overview
Plant Overview: Details in Appendix J
Units 1&2, Each 307 MW—PSE 50% Ownership
Units 3&4, Each 740 MW—PSE 25% Ownership
PSE is Not Plant Operator
Ownership Agreement Summarized in Appendix J
Much More Complicated Than Boardman or Centralia
PSE Contractually Obligated to Pay Its Share of Operating Costs
PSE Obligated to Take Its Share of Plant Output
PSE Cannot “Retire” Its Portion of Colstrip Units Unilaterally

## Slide 27: Colstrip: What Was Analyzed
Examined Broad Range of Future Colstrip Costs Across Broad Range of Possible Market/Policy Scenarios
Focus on Replacement Costs
Four Colstrip Cases: Based on Different Potential Regulation Costs
41 Market Scenarios: Loads/Gas Prices/CO2 Prices-Costs
Deterministic and Stochastic Analyses
Colstrip Costs Included
Units 1&2 Modeled Separately From Units 3&4
Base-Level Capital Expenditures
Variable Operating Costs
Opportunity Cost of Transmission Based on Timing of Contracts
Colstrip Costs Not Included
Decommissioning and Remediation Costs: Requirements Not Yet Defined
Unamortized Capital: No Acceleration/Change
Impact: Full Cost Impacts to Customers Higher Than Modeled in IRP

## Slide 28: 4 Colstrip Environmental Compliance Cases
Low Cost Case (Case 1): Based on achieving compliance using existing, installed equipment with a minimum of modifications or additions of equipment.
Mid Cost Case (Case 2): Includes the cost for addition of equipment that may be needed to assure compliance and is largely based on the analysis of Unit 1 & 2 equipment identified by the EPA’s Regional Haze FIP.
High Cost Case (Case 3): Additional costs for new equipment to meet future requirements and is based on CCR being determined to be hazardous.
Very High Cost (Case 4): Based on Sierra Club letter. Assumes all Case 2 costs plus it triples the hazardous waste disposal costs included in Case 3 and it accelerates the schedule for meeting other requirements.
See Appendix J, p. J-14 to J-23

## Slide 29: Colstrip: Analysis Performed
Portfolio Analysis
Least Cost Combination of Resources Given Resource Alternatives and Possible Future Conditions
Stochastic Analysis in Base and With Risk of Future Carbon Policies
Included Possible Carbon-Price Scenarios
Studied Key States of World for Colstrip
1-All Four Units of Colstrip Continue Operation
2-Units 1&2 Replaced in 2017, While 3&4 Continue Operation
3-All Four Units Need to be Replaced by 2017

## Slide 30: Colstrip: Summary Results and Conclusions
Savings to Customers From Colstrip Significant
Units 1&2: $55 Million in Savings/Year—2% Rate Increase
Units 3&4: $76 Million in Savings/Year—3% Rate Increase
Colstrip Total: $131 Million Savings/Year—5% Rate Increase
NOTE: Savings Reflect Only Replacement Costs
 | *Incremental Capital Expenditure for Case 2 (by 2017) | Annual Savings Given Case 2 (start 2018) | Simple Pay Back (in Years)
Units 1 & 2 | $70 Million | $55 Million/Yr | 1.3
“Near Term” Expenditures Not Long-Term Cost Risk for Customers
*--See Appendix J, p. J-19
Unit 3 & 4 Significant Expenditures More Than 10 Years Out
Incremental Expenditures 2026 & 2027: $190 Million
Cumulative Savings 2028-2030: $370 Million

## Slide 31: Colstrip Results Across Scenarios-(All Scenarios)
Figure 5-23, p. 5-47
Legend
Green indicates where all four units are cost effective.
Orange indicates where only Colstrip 3&4 are cost effective.
Red indicates scenarios where replacement power was more cost effective.

## Slide 32: Colstrip Results-Savings in Base Scenario
Figure 5-24, p. 5-49

## Slide 33: Wide Range of Savings in Base Scenario for Case 2
Figure 5-30, p. 5-56

## Slide 34: Colstrip 1 & 2 Savings Significant
Annual Incremental Revenue Requirement for Base Scenario, Case 2

## Slide 35: Wide Range of Savings in Base Scenario

## Slide 36: Annual Savings/ (Cost) of Continuing Operations of Colstrip Units 1 & 2 for Compliance Case 2 under all Scenarios

## Slide 37: Colstrip Reduces Cost & Risk Even With Carbon Price Risk
Figure 5-29, p. 5-55
Notes: Figure

## Slide 38: Colstrip: Conclusions in This IRP
Colstrip Significantly Reduces Cost and Cost Risk for Customers
Including Consideration of Future Carbon Regulation
Premature to Begin Developing Replacement Resources
May Change in Future
IRP Comprehensively Studied Potential Risks
Planning For Replacement
Peakers for Reliability and Market Energy As Needed Across Most Scenarios
38

## Slide 39: PSE 2013 IRP Agenda
Introduction and Key Findings
Electric IRP Overview
Resource Needs
Resource Plan
High Level Process & Assumptions
Results
Colstrip in IRP
Gas IRP Overview
Next Steps

## Slide 40
Resource Needs
Planning Assumptions & Resource Alternatives
Decisions
Commitment to “Action”
Analysis of Alternatives Portfolio Analysis
Analysis of Results
Regulatory Compliance
Customer Needs
Stakeholders
Market Outlook

## Slide 41: Gas Utility Resource Need
Figure 1-7, p. 1-13

## Slide 42: Gas Supply-Side Resource Alternatives
Figure 6-23, p. 6-37

## Slide 43: Gas Resource Plan
Gas Wild Cards…
If Swarr and/or LNG Peaking Unavailable: Additional NWP/Westcoast
Figure 1-8, p. 1-14

## Slide 44: Least-Cost Gas Portfolio Additions-MDth/Day
Figure 6-12, p. 6-24

## Slide 45: Gas Resource Sensitivities
Examined What-If:
LNG Peaker Does Not Become Available
Swarr is Not Upgraded
Findings:
Additional Storage w/Transport if Available
Existing Surplus Northwest/Westcoast Pipeline if Not

## Slide 46: Gas Action Plan
Pursue Cost Effective Demand-Side Resources
Continue Working Toward Developing PSE LNG Project
Decisions on Whether to Upgrade Swarr Propane Peaker
Continue Working with Northwest Natural on Possible Mist Expansion
Remain Active in Market Place to Move if Planned Resources Unavailable
Complete Analysis of Whether to Broaden Planning Standard
Revise Stakeholder Process to Clarify Roles and Expectations & Provide Greater Transparency

## Slide 47: PSE 2013 IRP Agenda
Introduction and Key Findings
Electric IRP Overview
Resource Needs
Resource Plan
High Level Process & Assumptions
Results
Colstrip in IRP
Gas IRP Overview
Next Steps

## Slide 48: IRP Next Steps
IRP Update To Examine Long-Term Market Reliance
Still Targeting 4th Quarter 2013
Restructuring Stakeholder Process
Begin Early 1st Quarter 2014
Finalizing Consulting Contract to Assist
Kick-Off 2015 IRP Process
Resource Needs: 1st Quarter 2014
Work Plan Filed: End of May 2014